## Slide 1: AERMOD Fundamentals Part 1
Course #MODL301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: AERMOD FUNDAMENTALS
Part 1 (Today)
Energy balance, atmospheric stability, and the structure of the Atmospheric Boundary Layer (ABL)
How AERMOD Characterizes the ABL
Help to understand AERSURFACE and AERMET and calculation of meteorological profiles
Part 2 (Wednesday)
AERMOD plume structure
Significant effects on Dispersion
  e.g. building wakes, terrain influences
Help to understand AERMOD

## Slide 3
Workhorse regulatory model (since 2006) for: SIPs, Air permitting, roadway hot spots, etc
Also commonly used for air toxics applications and health exposure and risk assessments
Steady-state Gaussian*-plume model
Near-source applications (< 50km)
Point, area, volume and line source types
Flat/complex terrain, urban/rural areas
Wet/dry deposition
NO2 chemistry
Building wake effects
One-hour average concentrations
aermod

## Slide 4
Gaussian
Plume

## Slide 5: What Does AERMOD Need From User?
Hourly near-surface wind and temperature measurements and a morning temperature sounding.
Source characteristics (emissions, stk.ht, stk. temp …)
Surface characteristics (terrain, land cover …)
Nearby building information
Other data depending on options (e.g. population for urban, particle size dist. for deposition)

## Slide 6: What Does AERMOD “Really” Need?
In addition to the required near surface winds and temperature provided by the user, AERMOD also requires the vertical structure of the atmospheric boundary layer, i.e., hourly profiles of winds, turbulence, and temperature.
If the user provides additional levels of winds, turbulence, and/or temperature, the model will use them.
At levels where data is not provided, the model simulates these profiles from boundary layer theory.

## Slide 7
AERMOD Modeling System
Input
Surface Characteristics AERSURFACE
Input
Meteorology AERMINUTE
Input
Terrain data
AERMAP
Input
Building data BPIPPRM
AERMOD
Compute PBL parameters
AERMET
Establish
Meteorology
Profiles
Compute
Concentrations

## Slide 8: Energy Balance and Heat Fluxes
RN = H + LE + G
  RN = Net radiation at the surface
  H = Sensible heat flux
    (H > 0) Daytime—convective—unstable—upward
    (H < 0) Nighttime—stable—downward
  LE= Latent heat flux
    Energy related to evaporation and condensation
  G = Heat absorbed by the soil
    Assumed to be 0.1 RN (based on field data)

## Slide 9: Surface Characteristics (AERSURFACE)
Albedo - reflectivity of surface
(fresh snow ~ 0.9 ; Forest ~ 0.15)
Bowen Ratio – function of surface moisture = Sensible heat flux / Latent heat flux
Surface Roughness – representation of the aerodynamic roughness

## Slide 10: Energy Balance and Heat Flux (Convective)
Bowen Ratio, B0 = H/LE (thus LE = H/ B0)
  ~ 5 to 10 over semi-arid/desert regions
  ~ 0.5 over forests and grassland
  ~ 0.1 over water
Substituting for LE and G = 0.1RN in RN = H + LE + G
  RN is derived from R, albedo, cloud cover

## Slide 11: Heat Flux (Stable)
H = function (U, cloud cover, sfc roughness)
If cloud cover is unavailable
H = function (U, temp gradient, sfc roughness)
(Bulk Richardson number approach)

## Slide 12: Atmospheric Stability
Stability—the ability of the atmosphere to either enhance or suppress vertical motion and thus pollutant dispersion.
Three general conditions of stability:
  Stable: vertical movement is suppressed; generally associated with cooling at surface
  Unstable: vertical movement is enhanced; generally associated with intense heating at the surface
  Neutral: when conditions neither significantly suppress nor enhance vertical movement; generally associated with cloudy and high wind conditions.

## Slide 13
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Height
Temperature
Adiabatic Lapse Rate
(-9.8 K/km)
Neutral Stability
Extremely Stable/
Inversion
(Temp increase with height)
Unstable
Stable
Static Stability

## Slide 14
Height
Potential Temperature
Stable
Unstable
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Adiabat

## Slide 15
Height
Potential Temperature
Stable
Unstable
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Adiabat

## Slide 16
Height
Potential Temperature
Stable
Unstable
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Adiabat

## Slide 17
Height
Potential Temperature
Stable
Unstable
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Adiabat

## Slide 18
Height
Potential Temperature
Stable
Unstable
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Adiabat

## Slide 19
Height
Potential Temperature
Stable
Unstable
Potential Temp = temperature that a parcel of air would obtain if brought adiabatically (no heat added or lost) to the surface
Adiabat

## Slide 20: Vertical Structure of ABL
  So, you’ve given AERMOD some surface characteristics and the wind and temperature at a single level……
  …how does AERMOD develop the vertical structure of the winds, temperature and turbulence needed for its dispersion calculations?

## Slide 21: Similarity Theory
Monin-Obukhov first proposed the similarity technique for characterizing the ABL when measurements at many levels are not practical:
  Using physical intuition ……
  Determine the relevant variables …..
  Apply dimensional analysis ……
  develop universal relationships describing how ABL parameters vary with ht.

## Slide 22: Similarity Theory
  These similarity relationships depends on:
  The scaling parameters for normalizing heights, velocities and temperatures along with ….
  Empirical constants derived from decades of field studies at a wide variety of sites and under widely varying conditions.

## Slide 23: Similarity Example
Log wind profile:
  U = mean horizontal wind speed
  u* = surface friction velocity
  z0 = surface roughness length
  z = height
  k = von Karman constant = 0.4

## Slide 24: Similarity Theory (cont.)
Scaling Parameters in AERMOD:
  Surface roughness length ()
  Monin-Obukhov length (L)
  Wind-driven mixing height (zim)
  Convection-driven mixing height (zic)
  Friction velocity (u*)
  Convective velocity scale (w*)
  Temperature scale (θ*)

## Slide 25: Surface Roughness Length ()
is the height at which the mean wind speed goes
to zero due to aerodynamic roughness.
ranges from a few millimeters over snow cover
or calm water to a meter or more in dense urban
areas.

## Slide 26: Friction Velocity (*)
represents the characteristic velocity of the
mechanically-induced turbulent eddies
near the surface.
is on the order of 10% of the mean
wind speed at 10 meters.

## Slide 27: Monin-Obukhov Length (L)
L represents the height below which mechanical production of turbulence is dominant
L is AERMOD’s primary stability indicator:
L
Mechanical Turbulence dominant
Buoyancy induced turbulence (large convective eddies) dominant
Notes: We need a scale that describes that magnitude of the atmospheric stability
The depth to which the mechanical turbulence is influential is the length of the scale we seek
𝑢_∗^3∕𝑘𝐿 is the mechanical turbulent energy produced by shear. This shear was derived by considering the stress on an infinitesimal volume of air
〖−𝑔𝐻〗∕〖𝑇_𝑎 𝜌𝑐_𝑝 〗 is the convective or buoyant turbulent energy produced by the wake of the rising parcels of air. OR The amount of turbulent energy destroyed by thermal stratification.
Next: Need a scale for the convective turbulence

## Slide 28: Monin-Obukhov Length (L)
Whether L is positive or negative,
as │L│ decreases, the stability becomes stronger
e.g. L = 5 is very stable;
L = -5 is very unstable;
L = ± 500 is solidly neutral stability
For stable conditions: L > 0 (since H < 0)
For unstable (convective) conditions:
L < 0 (since H > 0)
Notes: We need a scale that describes that magnitude of the atmospheric stability
The depth to which the mechanical turbulence is influential is the length of the scale we seek
𝑢_∗^3∕𝑘𝐿 is the mechanical turbulent energy produced by shear. This shear was derived by considering the stress on an infinitesimal volume of air
〖−𝑔𝐻〗∕〖𝑇_𝑎 𝜌𝑐_𝑝 〗 is the convective or buoyant turbulent energy produced by the wake of the rising parcels of air. OR The amount of turbulent energy destroyed by thermal stratification.
Next: Need a scale for the convective turbulence

## Slide 29: Convective Velocity Scale (w*)
w* represents the characteristic vertical velocities of the large convective eddies (thermals)
w* can be as high as 1 to 2 m/s
in highly convective conditions

## Slide 30: Temperature Scale (θ*)
θ* represents the characteristic temperature variations
in the wind-shear induced eddies.
θ* has been found to be a strong function of
cloud cover at night.

## Slide 31: Mechanical Mixing Height (zim)
The mechanical mixing layer height is estimated from its simple relationship to the friction velocity scale :
Note: zim is smoothed to avoid rapid changes from hour to hour.

## Slide 32: Convective Mixing Height (zic)
zic is computed from a simple energy balance where cumulative daytime heat flux is compared to the potential temperature profile from the morning sounding (Weil and Brower, 1983)
Equate the areas
Morning
Sounding
zic
z
θ
H
time

## Slide 33: Mixing Height
The Convective mixing height is computed for hours where the heat flux is positive (L is negative).
The Mechanical mixing height is computed for all hours.
In convective conditions, AERMOD chooses the larger of the two computed values.
In stable conditions (L is positive), the
mechanical mixing height is used.

## Slide 34: Turbulence
In general, irregular, chaotic motion – resulting from varying sized eddies
Generated and maintained by two primary mechanisms:
  Convection from radiative heating at the ground
  Wind shear from variation of wind speed with height due to friction at the surface
These eddies are responsible for both dispersion (eddies < plume dimensions) and plume meandering (eddies > plume plume dimensions)

## Slide 35: Turbulence
is the standard deviation of vertical velocity
(at z=0) = 1.3 u*
(Mechanically-induced)
(z) = function (u* and )

## Slide 36: Turbulence
is the standard deviation of vertical velocity
is the standard deviation of lateral velocity
(at z=0) = 1.3 u*
(Mechanically-induced)
(at z=0) = 1.9 u*
(z) = function (u* and )
(z) = function (u* and )

## Slide 37: Turbulence
(Convectively-induced)
(z) = function (u*, o)
Vertical turbulence
(z) = function (u*, and )
Lateral turbulence

## Slide 38: Potential Temperature
(z) = function ( , , )
Wind Speed
U(z) = function(u* , zo , L)
+ stability correction

## Slide 39: Vertical Structure of the ABL in AERMOD
σW
σV
u
θ
Zim
Sfc
Layer
Zic
STABLE
CONVECTIVE
M
I
X
E
D
L
A
Y
E
R
θ
u
σV
σW

## Slide 40: Profiles in AERMOD
  First and foremost, AERMOD uses measurements at all levels provided by the user.
  *but requires only winds and temp
  at one level.
  It then uses similarity relationships to interpolate between measurements and extrapolate above the highest and below the lowest measurement.

## Slide 41: Wind Direction
  There is no current similarity relationship for profiling wind direction.
  Therefore, AERMOD simply linearly interpolates between measurements at different heights but assumes the direction is constant above the highest and below the lowest measurement.

## Slide 42: Wind Direction
Note: Wind Direction is defined as the direction from which the wind is blowing.
90°
from East
180°
from South
270°
from West
0°
from North

## Slide 43
End Part 1 of Fundamentals