## Slide 1: AERMOD: Introduction to Running the model
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Develop an initial understanding of how the AERMOD system is structured
Develop an initial understanding of a simple AERMOD Control File: Pathway/Keyword/Parameters
Perform a simple AERMOD run

## Slide 3
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA
1 MINUTE ASOS DATA

## Slide 4: The Control File
AERMOD uses a Pathway/Keyword/Parameter approach to specify options and input data for running the model.
AERMOD uses 6 Pathways:
  CO: COntrol—titles, modeling options, pollutant IDs, averaging times
  SO: SOurce—source types, locations, and parameters/emissions, building parameters for downwash, and source groups
  RE: REceptors—discrete and gridded (Cartesian & Polar) receptor locations and elevations
  ME: MEteorology—AERMET-generated input files
  OU: OUtput—options for providing AERMOD output in various ways
  EV: EVent processing—analysis of source contributions (optional)

## Slide 5: Control File (Cont.)
Keywords:
  Keywords:
    Define the data being input, i.e. sources, building dimensions, met, surface and terrain
    Define the data to be output
    Direct AERMOD to perform the analysis you need for your application: i.e., identifies the options that are being used for the run

## Slide 6: Control File (Cont.)
Record structure
  2-character-pathway keyword(s) parameter(s) and/or secondary keyword(s)
The first keyword for all pathways is STARTING
The last keyword for all pathways is FINISHED
All Keywords, Secondary Keywords and Parameters are available in the AERMOD User’s Guides
Same is true for each of AERMOD’s Preprocessors

## Slide 7: To Perform a Simple Run of AERMOD
Run AERMET to produce AERMOD’s input meteorology (This has already been done for you. The 2 met files .sfc & .plf, that are needed to run AERMOD, can be found in: …\MODL_301\Hands-On\Sec-3_Run\)
Construct AERMOD control File
  The application’s data is in the file:
  …\Sec-3_Run\ Sec-3_AERMOD_Run_Data.txt
  Build the control file (i,e., “Input File -.inp” (this file has already been completed and can be found in …\MODL_301\Hands-On\Sec-3_Run\ with the data provided in “Sec-3_AERMOD_Run_Data.txt”)
Run AERMOD
  If executable is in same directory as the control file, simply double-click executable
  If not, construct a batch file that identifies where the .exe is located

## Slide 8: Perform AERMOD Run
RUN AERMOD
  In Hands_On directory open …\Sec-3_Run\ directory
  Examine the:
    Control file
    The 2 met files w/ header file
    The .bat file (needed since the AERMOD .exe is in a different directory)
  Double click .bat file to run AERMOD

## Slide 9: Analyze AERMOD Results
BRING UP OUTPUT FILE
Identify the 1, 3, and 24hr max concentrations
Identify the Period Ave. concentration
Determine where the 4 concentrations occurred and when they occurred

## Slide 10: AERMOD – PLOT FILES
Depending on the contouring program you are using will determine if and/or how much the .plt files will need to be edited.

## Slide 11
Next: Exercise 1