## Slide 1: EXERCISE 1
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Exercise 1
Consider the run made in …\Sec-3_Runs\ (referred to as the Base Case). For this exercise make 3 additional runs to compare to the Base Case:
  Case 1: Change stack height to 20 m
  Case 2: Change stack height to 300 m
  Case 3: Change Hs=20m, Ts=350K; & Vs=5.8m/s; Keep the same inside diameter as base case

## Slide 3: Exercise 1
Procedure for this exercise:
  A sub-directory named Exercise_1\ is in the …\Sec-3_Run\ sub-directory
  Within …\Exercise_1\ are 3 empty sub-directories named: …\20m_Stack\; …\300m_Stack\ & …\20m_Low_Buoy\
  Copy the following files from the …\Sec-3_Run\ sub-directory into the 3 empty sub-directories in …\Exercise_1, you will edit the .inp and .bat files for each of the specific runs:
    AERMOD_Sec-3_Run.inp
    Profile_Met.pfl
    Surface_Met.sfc
    Run_Sec-3.bat

## Slide 4: Exercise 1
4. Edit the Input files:
    Change HS to the appropriate stack height for each of the three cases
    For the …\20m_low_Buoy\ case, change TS to 350K and VS to 5.8m/s
5. Edit the batch files so they can find the AERMOD executable (i.e., move back 3 sub-directories when referencing AERMOD_24142.exe)
6. Run each case: double click each batch file
7. Identify the following Results:
What are the high 1, 3, 24 and Period averages for each case?
When did they occur?
Where are they located?

## Slide 5: RESULTS FROM ASSIGNMENT
20m Run:
  1hr Max: 225.9 µg/m3 (964.18m x 1149.07m) (5/27/11 – hr. 7)
  3hr Max: 128.9 µg/m3 (-321.39m x -383.02m) (5/8/11 – hrs. 13,14,15)
  24hr Max: 40.6 µg/m3 (-321.39m x -383.02m) (5/8/11)
  Period Max: 2.2 µg/m3 (128.56m x 153.21m)
100m Run (from the …\Sec-3_run performed earlier today):
  1hr Max: 136.7 µg/m3 (-342.02m x 939.69m) (10/14/11 – hr. 10)
  3hr Max: 49.2 µg/m3 (-574.53m x -482.09m) (8/17/11 – hrs. 13,14,15)
  24hr Max: 13.6 µg/m3 (-766.04m x -642.79m) (8/17/11)
  Period Ave: 0.82 µg/m3 (803.48m x 957.56m)

## Slide 6: RESULTS FROM ASSIGNMENT
300m Run:
  1hr Max: 107.9 µg/m3 (-513.03m x 1,409.54m) (10/14/11 – hr. 10)
  3hr Max: 36.6 µg/m3 (-513.03m x 1,409.54m) (10/14/11 – hrs. 10,11,12)
  24hr Max: 5.9 µg/m3 (2,114.31m x -769.55m) (12/1/11)
  Period Max: 0.37 µg/m3 (1,767.67m x 2,106.62m)
20m_Low_Buoy Run:
  1hr Max: 1126.2 µg/m3 (-153.21m x -128.56m) (9/26/11 – hr. 2)
  3hr Max: 834.2 µg/m3 (-383.02m x -321.39m) (9/26/11 – hrs. 1,2,3)
  24hr Max: 436.5 µg/m3 (-383.02m x -321.39m) (12/11/11)
  Period Max: 15.2 µg/m3 (-128.56m x -153.21m)

## Slide 7: 100m AERMOD 1 HR. PLOT
Source
Max 1 hr.
Max 1hr = 136.7 µg/m3

## Slide 8: 20m AERMOD 1 HR. PLOT
Source
Max 1 hr.
Max 1hr = 225.9 µg/m3

## Slide 9: 20m-Low-Buoy 1HR. PLOT
Source
Max 1 hr.
Max 1hr = 1126.2 µg/m3

## Slide 10: 300m AERMOD 1 HR. PLOT
Source
Max 1 hr.
Max 1hr = 107.9 µg/m3

## Slide 11: 100m AERMOD 3 HR. PLOT
Source
Max 3 hr.
Max 3hr = 49.2 µg/m3

## Slide 12: 20m AERMOD 3 HR. PLOT
Source
Max 3 hr.
Max 3hr = 128.9 µg/m3

## Slide 13: 20m-Low-Buoy 3HR. PLOT
Source
Max 3 hr.
Max 3hr = 834.2 µg/m3

## Slide 14: 300m AERMOD 3 HR. PLOT
Source
Max 3 hr.
Max 3hr = 36.6 µg/m3

## Slide 15: 100m AERMOD 24 HR. PLOT
Source
Max 24 hr.
Max 24hr = 13.6 µg/m3

## Slide 16: 20m AERMOD 24 HR. PLOT
Source
Max 24 hr.
Max 24hr = 40.6 µg/m3

## Slide 17: 20m-Low-Buoy 24 HR. PLOT
Source
Max 24 hr.
Max 24hr = 436.5 µg/m3

## Slide 18: 300m AERMOD 24 Hrs. PLOT
Source
24 hr Max.
Max 24hr = 5.9 µg/m3

## Slide 19: 100m AERMOD PERIOD PLOT
Source
Period Ave.
Period Ave = 0.82 µg/m3

## Slide 20: 20m AERMOD PERIOD PLOT
Source
Period Ave.
Period Ave = 2.2 µg/m3

## Slide 21: 20m-Low-Buoy PERIOD. PLOT
Source
Period Ave.
Period Ave = 15.2 µg/m3

## Slide 22: 300m AERMOD PERIOD PLOT
Source
Period Ave.
Period Ave = 0.37 µg/m3