## Slide 1: Introduction to Hands-on Activities
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Lesson Objective
The student should be able to:
  Explain the purpose of performing the hands-on activities
  Explain the directory structure in which all needed files can be organized
  Describe the modeling scenario that will be used throughout this course

## Slide 3: Directory Structure
:\>MODL_301\Hands-On\
  ...\Sec-3_Run\
  ...\ AERSURFACE\
  ...\ AERMINUTE\
  ...\ AERMET\
  ...\ AERMAP\
  ...\ BPIPPRM\
  ...\ AERMOD\
  …\AERSCREEN\
    (listed in the order to be completed)

## Slide 4: Input/Output Files
  A complete set of data files have been Provided for all the hands-on activities, including:
    Control files (Already filled out)
    Input data – All of the data needed to run the exercises have been provided.
  We will provide all the met, surface and terrain data you will need to run the preprocessors and the Model, except one of the met data files you will download in class.
  We will go over the control files and batch files needed to run the programs
  You will run the various preprocessors and AERMOD to produce the output files for each Hands-On exercise
  We have also provided a solutions directory in case your run fails. The solutions directory will contain the completed run.

## Slide 5: Martins Creek
An EGU Located on the Pennsylvania–New Jersey border, about 95 km north of Philadelphia and 30 km northeast of Allentown
This data set was developed because of a §126 petition from NJ
It is one of the independent databases used in the evaluation of AERMOD (complex terrain application)

## Slide 6: Martins Creek Cont’d
It's located in the Delaware River valley with elevated terrain on both sides of the valley
Scott’s Mountain to the southeast rises about 300–350 m above the valley floor ≈ 2.5–8.0 km southeast of the facility
There is also a ridge located about 2 kms west and north rising about 150–200 m above the valley floor

## Slide 7: Martins Creek Cont’d
The MC field study was conducted in 1992/1993
  Data were collected for one year
  SO2 measurements were made at 7 monitors on Scott’s Mountain
  Hourly CEM emissions data were collected
  Met data were collected from an 10m on-site tower & from a SODAR that measured wind speed and direction at 12 levels from 90m to 420m
Sources: We will be modeling the main power plant stack plus two smaller sources at the plant

## Slide 8: Topographical Map

## Slide 9: Martins Creek Cont’d
The term “wind direction” is ALWAYS the direction FROM WHICH THE WIND IS BLOWING. A flow vector is the direction TO WHICH THE WIND IS BLOWING.
This is a wind direction of 45o (or a NE wind), that is, the direction FROM WHICH THE WIND IS BLOWING

## Slide 10: Martins Creek Cont’d
We will run two scenarios using AERMOD:
First Scenario:
  1 year of meteorological data (May 1, 2011 through April 30, 2012):
    Martins Creek site-specific tower & SODAR data – Primary
    1-minute hourly ASOS data (KABE - Allentown) - produced using AERMINUTE– Secondary (used to fill in missing primary data)
    NWS Surface data - Standard ASOS – (KABE - Allentown)
    NWS upper air soundings from (KALB – Albany)
    2 Runs: 1) 1 hr SO2 & 2) 3 hr., 24 hr., Annual
  Why do we need to make 2 runs?

## Slide 11: Martins Creek Cont’d
Second scenario:
  Model 5 years of meteorological data (2008–2012) from Allentown:
    Hourly wind data, 1-minute ASOS data processed using AERMINUTE (KABE) – Primary
    NWS upper air soundings (KALB – Albany) Morning sounding only
  Two runs:
    1 hr SO2
    3 hr., 24 hr., Annual SO2