## Slide 1: Aermet—Part 1
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this session, the student should be able to:
  List AERMET’s data requirements
  Explain the difference between representative and non-representative data
  Explain how a 2nd met database can be used to substitute missing or questionable data found in the primary met dataset

## Slide 3: Overview
Meteorological observations:
  Site-specific Data
  NWS Surface data
  Upper Air Data (morning sounding only)
  Prognostic Data (this comes from models that predict meteorological conditions rather than measuring them) – will not be utilized in this course
Temporal Data Requirements
Surface Characteristics
Data Representativeness
Output files that are used by AERMOD

## Slide 4
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA
1 MINUTE ASOS DATA

## Slide 5: AERMET Minimum Data Requirements
Hourly Surface Observations
  Wind speed & direction, normally measured at about 10 meters
  Cloud Cover
  Temperature measured at about 2 meters

## Slide 6: Met Data Types Available for AERMOD
NWS Surface data (Winds, Temp & CC at 1 level)
  Ice Free Wind (IFW) sensor program:
    Standard ASOS data - non-commissioned (ISHD format): single observation at the top of the hour
    1-Minute ASOS data – commissioned (non-ISHD format): true hourly average
On-Site Data
  Tower (single or multi-level)
  SODAR
  Other remote sensing data
Upper Air data
  Morning sounding only
Prognostic: Provides all data needed

## Slide 7: Standard ASOS Wind Data (Non-Commissioned)
Does not archive every min of data. It archives only a 2min average at the top of the hour.
Mimics Observer-based observations
Calms increased from a few percent with pre-ASOS to 10%, 20% with Standard ASOS

## Slide 8: ASOS 1 Minute Wind Data (Commissioned)
Archived 2 min rolling averages from an ASOS stations are available throughout the hour once the station is commissioned (known as 1-min ASOS data).
AERMINUTE was developed to process the 2 min rolling average data into a true 1-hour average

## Slide 9: Upper Air Data (Radiosondes, Rawinsondes)
92 stations in North America; distance between stations in U.S.
10 stations in Caribbean
Taken twice daily – AERMOD only uses the morning sounding

## Slide 10: Upper Air Data Used By AERMET
FSL data is no longer available
NWS – IGRA Format
Data Elements Required by AERMET
  Morning sounding only
  Height, temperature
  Winds from sounding are not used

## Slide 11: Site-specific Data
AERMOD can use multiple levels of data
Generally, only one level of wind speed, direction, and temperature are collected
Sometimes solar or net radiation &/or σθ are collected

## Slide 12: Use of Prognostic Meteorological Data
The May 21, 2017 changes to Appendix W allowed the use of prognostic meteorological data
However, this data is not in a usable format ⸫ MMIF was developed
The Mesoscale Model Interface (MMIF) preprocessor is the only program approved for developing the needed input from a prognostic meteorological model for AERMOD (see Section 8.4.2(a) of Appendix W)

## Slide 13: Use of Prognostic Meteorological Data – Cont.
Prognostic data (modeled) can be used in lieu of all measured data
The output from models such as MM5 or WRF can be transformed to AERMOD’s surface and profile meteorological input files
MMIF Provides 2 ways to do this:
  MMIF to AERMOD - Non-regulatory applications
  MMIF to AERMET to AERMOD - Regulatory applications

## Slide 14: Meteorological Data Substitution
Missing Site-Specific data can be substituted using 1 min. ASOS data from an NWS site
This process is Automated using:
  AIRMINUTE to process the 1min. ASOS data
  &
  AERMET’S Stage 2 to performs the substitutions

## Slide 15: Length of Meteorological Data Record
Regulatory requirements—Appendix W, Section 8.4.2
  If using NWS data, 5 years are required
  If using Site-Specific data, only 1 year is required. But if more exists, then they must be used up to 5 years
  If prognostic data are used, then 3 yrs. are required

## Slide 16: Surface Characteristics Needed To Be Passed to AERMET
Noon-time Albedo (α):
  Surface reflectivity: Ranges from 0 (nighttime) to 1 (100% reflected)
Bowen ratio (B0)
  Measure of surface moisture typically ranges from 0.1 (water) to 10.0 (deserts)
Surface roughness length (z0):
  Measure of the degree to which the underlying surface reduces wind speed and increases mechanical turbulence, typically ranges from 0.001 (water) to 1.0 (urban or forested areas)

## Slide 17: Surface Characteristics - AERSURFACE
Input acquired from USGS used to calculate surface characteristic:
  National Land Cover Dataset (NLCD) data
  % of tree canopy
  % impervious surface
The surface characteristics (α, B0 and z0), which are estimated using AERSURFACE, are needed for AERMET to calculate surface parameters (e.g., u*, w*, L, etc.)

## Slide 18: Data Representativeness
EPA Meteorological Monitoring Guidance states
  “…meteorological data should be representative of conditions affecting transport and dispersion in the area of interest as determined by the locations of sources and receptors.”
Representativeness can be thought of as how similar the constructed profiles are between the NWS site and the source location
Representativeness is assessed case-by-case

## Slide 19: Pairing Hourly Surface Observations with Upper Air Data
First Choice: Data from collocated surface and upper air station
If not collocated, consider proximity & surface characteristics
Many states preprocess NWS hourly observations and upper air data and make the files available on their website