## Slide 1: AERSURFACE
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this session, the student should be able to:
List AERSURFACE’s data requirements
Explain, in general terms:
  How the control file is structured
  What options are available to the user

## Slide 3: Overview
This lesson introduces:
Surface Characteristics—Definitions and Averaging Methods for:
  Surface Roughness Length (z0)
  Daytime Bowen Ratio (B0)
  Noon-time Albedo (α)
Land Cover Data Products and Data Resources
    USGS Multi-Resolution Land Characteristics (MRLC) Consortium
    EPA archive located at:
How AERSURFACE averages the field of land use characteristics, in an area, to produce a single value for each of the three surface parameters for each month and Zo sector
https://gaftp.epa.gov/Air/aqmg/nlcd/

## Slide 4: What is AERSURFACE
AERSURFACE is a non-regulatory tool to aid modelers with development of monthly surface values for:
  Noon-time albedo
  Bowen ratio
  Roughness length
Uses land cover data from the National Land Cover Dataset (NLCD) developed and maintained by USGS, Impervious Surface data & Tree Canopy data

## Slide 5
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
SURFACE & UPPER AIR NWS DATA
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA

## Slide 6: Surface Characteristics
Noon-time Albedo (α)
  Reflectivity of the earth’s surface
  Fraction of incoming radiation reflected at the earth’s surface (0.00 < α < 1.00)
  Varies with land cover, latitude and season
  Typical values range from 0.1 for thick deciduous forests to 0.9 for fresh snow
  Using the noon-time AERMOD calculates α for each convective hour
Sun
Earth’s surface

## Slide 7: Surface Characteristics Cont’d
Daytime Bowen Ratio (B0)
  Ratio of sensible heat flux (H) to latent heat flux (L), B0 = H/L
  Varies by land cover type and moisture conditions (rainfall)
  Dry environment = larger B0
  Wet or moist environment = smaller B0
  Typical summer (winter) values for average moisture conditions:
    Water = 0.1 (0.1, 1.5 if water is frozen)
    Deciduous forest = 0.3 (1.5); Grassland = 0.8 (1.5)
    Desert shrubland = 4.0 (6.0)

## Slide 8: Surface Characteristics Cont’d
Surface Roughness Length (z0)
  Represents the height at which the mean horizontal wind speed is zero due to frictional forces from the ground
  AERSURFACE gets its value for Zo by averaging the values associated with the various land-use categories in a particular sector.
  Typical values range from 0.001 meter over calm water to 1 meter or more over an urban area
  It’s what creates mechanical turbulence by bleeding kinetic energy from the approach flow (the higher the wind and/or Zo the larger the mechanical turbulence)

## Slide 9: Acquiring Surface Characteristics
Land Use Data - NLCD
  Land Cover, Tree Cover & Impervious Surface are available from1985 through 2023
  Pixel resolution: We will use 30m x 30m (1o); other resolutions are available.
  16 classes to choose from for each pixel (4 more for Alaska)
AERSURFACE includes tables of monthly surface characteristic values for each land cover class

## Slide 10: Land Cover Classifications
From the Multi-Resolution Land Characteristics (MRLC) Consortium
http://www.mrlc.gov/index.php
(this applies to 2011)

## Slide 11: Averaging Methods for Surface Characteristics
AERSURFACE is provided a land cover class for each of the individual pixel in the area of the meteorological tower.
For zo it computes a monthly, seasonally or annual value for each sector (max # of sectors = 12)
For Bo & α it computes one value for each month, season of year
In addition to land use classes there is the option to incorporate:
  Tree canopy data (2011-2021)
  Impervious surface data (1985-2023)

## Slide 12: Averaging Methods for Zo
Surface Roughness Length (z0)—Regulatory Option (ZORAD)
  The roughness length is averaged over each user defined sector & distance (.5km to 5.0 km): sector centered on the met tower. Default distance is 1 km
  Before averaging Zo an inverse-distance weighting is applied to each grid cell
    The closer the cell is to the tower the greater it’s effect
  Z0 for a given sector & month is the geometric mean of the inverse-distance weighted roughness from each grid cell
Stull, R. B. (1988). An Introduction to Boundary Layer Meteorology.
Kluwer Academic Publishers. Dordrecht, Netherlands.

## Slide 13: Averaging Methods - albedo
Noon-time Albedo (α)
  Simple unweighted arithmetic mean
  No direction or distance dependency (wind sectors not applicable)
  10-km × 10-km region
10-km × 10-km region
(applies to Bowen ratio and albedo)
RDU Meteorological Tower
1-km Radius, 3 Wind Sectors
(applies only to roughness)
1
3
2

## Slide 14: Averaging Methods - Bo
Daytime Bowen Ratio (B0)
  Simple unweighted geometric mean since we are averaging ratios
  No direction or distance dependency (wind sectors are not applicable)
  10-km × 10-km region (same region used for albedo)
10-km × 10-km region
Met Tower

## Slide 15: Land Cover at RDU
NLCD 2001
NLCD 2011

## Slide 16: Impervious Data at RDU
NLCD 2001—Impervious
NLCD 2011—Impervious

## Slide 17: Canopy, Impervious Data at RDU
NLCD 2001—Canopy
NLCD 2011—Canopy

## Slide 18: Canopy, Impervious Data at RDU
NLCD 2001—Canopy
NLCD 2001—Impervious
NLCD 2011—Canopy
NLCD 2011—Impervious

## Slide 19: Roughness Adjustments for Developed Categories
Developed Categories are:
  21 - Developed Open space
  22 – Developed Low Intensity
  23 – Developed Med. Intensity
  24 – Developed High Intensity
Each Zo sector must be defined as either HIGHZO or LOWZO
  HIGHZO: This assumes a higher roughness then NLCD due to the presence of commercial and industrial buildings.
  LOWZ0: This assumes a lower roughness then NLCD due to the presence of roads, runways and parking lots.

## Slide 20: Certain Control Keywords/Parameters
ZORADIUS radius (0.5 km to 5.0 km) (applicable only to ZORAD)
CLIMATE Moisture* Snow Cover* Arid*
AVERAGE SNOW ARID
WET NOSNOW NONARID
DRY
Blue indicates default value if not specified.
CLIMATE: Climate conditions for the period being modeled.
Moisture: General amount of surface moisture in the region.
  Snow Cover: Was there at least one month of continuous snow cover during the winter?
  Arid: Is the area considered arid?

## Slide 21: Certain Control Keywords/Parameters
FREQ_SECT* Frequency* # Sectors* Roughness Adj.*
ANNUAL 1…12, OR 16 LOWZ0
SEASONAL HIGHZ0
MONTHLY VARYZ0
FREQ_SECT: Temporal resolution of derived surface characteristics and the treatment of wind sectors for surface roughness
Frequency: Indicate the temporal resolution ofVARYZ0 derived surface characteristics
# Sectors: Indicate the number of wind sectors for which surface roughness will be derived
Roughness Adj.: Indicate whether all wind sectors should be treated as though they are lower Z0’s than NLCD (e.g., airports), higher Z0’s than NLCD, or whether it is preferred to vary the roughness Adj. by individual sector

## Slide 22: Certain Control Keywords/Parameters
SECTOR Index* Begin Dir. End Dir. Roughness Adj
1…16 Whole or Decimal deg. LOWZ0 HIGHZ0
SECTOR: Used to define individual wind sectors. Conditional and repeatable based on FREQ_SECT keyword entries.
Index: Sector identifier, consecutive numbering required.
Begin Dir.: Beginning sector direction in whole degrees.
End Dir.: Ending sector direction in whole degrees.
Roughness Adj: Indicates whether a sector should be treated as though it is higher or lower than the NLCD. Required for all sectors when VARYZ0 is specified on FREQ_SECT keyword.

## Slide 23: Example RDU Airport
30 Degrees
60 Degrees
225 Degrees
LLOWZ0

## Slide 24: Certain Control Keywords/Parameters
SEASON Season* Months*
WINTERNS 0 or 1…12, default = 0
WINTERWS
SPRING
SUMMER
AUTUM
SEASON: Used to reassign months to seasons when the Frequency of surface characteristics specified on FREQ_SECT keyword is ANNUAL or MONTHLY. If Frequency is SEASONAL, AERMET default assignments will be used:
Winter = Dec, Jan, Feb; Spring = Mar, Apr, May
Summer = Jun, Jul, Aug; Autumn = Sep, Oct, Nov
Season: WINTERNS = winter months with no continuous snow cover, and WINTERWS = winter months with continuous snow cover.
Months: Space delimited list of months (month number where Jan = 1 and Dec = 12). All months must be assigned.

## Slide 25: AERSURFACE User Options
Control File Structure and Format
  ASCII Text control file
  aersurface.inp (not case sensitive)
  Pathway/Keyword/Parameter structure (similar to AERMOD and AERMAP)
  Two pathways
    CO = Control
    OU = Output
  Pathway order is important
  Keyword order is important for some keywords
  Order of the parameters following a keyword on a record is critical!
LLOWZ0
MODL_301

## Slide 26: AERSURFACE Output (SFC Values)