## Slide 1: AERSURFACE Hands-on
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Download land use data
Construct an input control file for AERSURFACE
Run the AERSURFACE program
Analyze the AERSURFACE results

## Slide 3: AERSURFACE—Obtaining Data
As of April 2020, a source of the data, without cost, is available from
For this exercise, the data has been provided
Multi-Resolution Land Characteristics (MRLC) Consortium at:
https://www.mrlc.gov/
Click Tools and select NLCD Viewer
Click OK in Notice to User and “x” out the pop-up
In the upper left hand corner click the dropdown box that has “All” in it and select Continental US
In the bottom left column select Land Cover, National Atlas States (under Boundaries).
Zoom map in on area where met tower/s are located
Click on the 2nd to right most icon at the middle pane
Move cursor to the upper right extreme of the area you want to extract and click the mouse. Then drag the courser to the lower left most portion of the area to be extracted and click
In the right column of the screen, under Data Download, select Fractional Impervious Surface, Land Cover and Tree Canopy.
Using the slide below “Select Years” move the two buttons so that only year 2011 is selected
Enter you email at the bottom of the panel and click download
Data will be sent to you within 24 hrs. (usually you will receive it within a few mins.

## Slide 4: AERSURFACE—Files
  The executable is in the following directory:
  \>MODL_301\Hands-On\AERSURFACE\
  Aersurface_24142.exe
  For this exercise, the data has been downloaded and is in: \>MODL_301\Hands-On\AERSURFACE\NLCD\
    The data is in 3 separate files: land Cover; %Tree Cover; & % Impervious Surface
    The area downloaded is large enough to cover both the on-site tower and the NWS site
  We need to run AERSURFACE three times:
    On-Site: …\MC\ - Primary
    NWS: …\KABE2\ - 1-min-ASOS for SECONDARY substitution for 1 yr.
    NWS: …\KABE\ - 1-min-ASOS PRIMARY for 5 yr case

## Slide 5: AERSURFACE—Control File Parameters For MC
Center of domain: 40.797 North, 75.136 West—The location of the Martins Creek onsite tower
Geographic reference datum: NAD83
Local climatic conditions:
  Average moisture
  Continuous snow cover
  Non-arid

## Slide 6: AERSURFACE—Control File Parameters For MC
Surface characteristics:
  Monthly Average
  2 sectors: 180–260 & 260–180
  Both sectors are defined as HIGHZ0
Seasons:
  Winter without continuous snow: 10 11 12 1
  Winter with continuous snow: 2 3
  Spring: 4 5 6
  Summer: 7 8 9
  Autumn: 0

## Slide 7: AERSURFACE—MC Site
To run AERSURFACE for the Martins Creek site:
  Navigate to the directory: \>MODL_301\Hands-On\AERSURFACE\MC\
  Construct .inp control file (already completed)
  The .bat file locates the AERSURFACE executable
  Double click the .bat file

## Slide 8: AERSURFACE Output of MC
FREQ_SECT MONTHLY
SECTOR 1 180.00 260.00
SECTOR 2 260.00 180.00
** Month Sect Alb Bo Zo
SITE_CHAR 1 1 0.17 0.74 0.028
SITE_CHAR 1 2 0.17 0.74 0.032
SITE_CHAR 2 1 0.54 0.48 0.013
SITE_CHAR 2 2 0.54 0.48 0.016
SITE_CHAR 3 1 0.54 0.48 0.013
SITE_CHAR 3 2 0.54 0.48 0.016
SITE_CHAR 4 1 0.15 0.39 0.038
SITE_CHAR 4 2 0.15 0.39 0.044
SITE_CHAR 5 1 0.15 0.39 0.038
SITE_CHAR 5 2 0.15 0.39 0.044
SITE_CHAR 6 1 0.15 0.39 0.038
SITE_CHAR 6 2 0.15 0.39 0.044
SITE_CHAR 7 1 0.18 0.42 0.165
SITE_CHAR 7 2 0.18 0.42 0.184
SITE_CHAR 8 1 0.18 0.42 0.165
SITE_CHAR 8 2 0.18 0.42 0.184
SITE_CHAR 9 1 0.18 0.42 0.165
SITE_CHAR 9 2 0.18 0.42 0.184
SITE_CHAR 10 1 0.17 0.74 0.028
SITE_CHAR 10 2 0.17 0.74 0.032
SITE_CHAR 11 1 0.17 0.74 0.028
SITE_CHAR 11 2 0.17 0.74 0.032
SITE_CHAR 12 1 0.17 0.74 0.028
SITE_CHAR 12 2 0.17 0.74 0.032

## Slide 9: AERSURFACE – Allentown NWS
Construct control file for Allentown NWS
1)…\AERSURFACE\KABE2\aersurface.inp (used for on-site data substitution)
2)…\AERSURFACE\KABE\aersurface.inp (primary surface characteristics for the 5 yr run)
Run AERSURFACE for each case
Compare output from the MC & KABE2 runs

## Slide 10: AERSURFACE—Control File Parameters for KABE and (KABE2)
Center of domain: 40.64990 North, 75.44883 West
SECONDARY Site
Geographic reference datum: NAD83
  Average moisture
  Continuous snow cover
  Non-arid
Surface characteristics
  Monthly
  3 sectors for Zo: 60–235, 235–320, 320–60
  All sectors are defined as LOWZO
Seasons:
  Winter without continuous snow: 10 11 12 1
  Winter with continuous snow: 2 3
  Spring: 4 5 6
  Summer: 7 8 9
  Autumn: 0

## Slide 11: AERSURFACE—KABE as Secondary Site
Now, develop the control file for the airport KABE as SECONDARY site for the PRIMARY MC on-site data, and run AERSURFACE (in AERMOD the secondary site must be referenced as KABE2)
  Construct control file for Allentown NWS …\AERSURFACE\KABE2\aersurface.inp
  Run AERSURFACE
Why are we running this? Because the 1 min. ASOS data from KABE will be used to substitute for any missing on-site data
N
60
235
320

## Slide 12: AERSURFACE—KABE as Primary Site For 5yr Runs
Now, develop the control file for the airport (KABE) as PRIMARY site and run AERSURFACE
  Construct control file for Allentown NWS …\AERSURFACE\KABE\aersurface.inp
  Run AERSURFACE
Why are we running this? Because Allentown is the only site for surface characteristics for 5 yr runs
N
60
235
320

## Slide 13: Comparison of Surface Chara. MC vs. KABE
FREQ_SECT MONTHLY 2
SECTOR 1 180.00 260.00
SECTOR 2 260.00 180.00
** Month Sect Alb Bo Zo
SITE_CHAR 1 1 0.17 0.74 0.028
SITE_CHAR 1 2 0.17 0.74 0.032
SITE_CHAR 2 1 0.54 0.48 0.013
SITE_CHAR 2 2 0.54 0.48 0.016
SITE_CHAR 3 1 0.54 0.48 0.013
SITE_CHAR 3 2 0.54 0.48 0.016
SITE_CHAR 4 1 0.15 0.39 0.038
SITE_CHAR 4 2 0.15 0.39 0.044
SITE_CHAR 5 1 0.15 0.39 0.038
SITE_CHAR 5 2 0.15 0.39 0.044
SITE_CHAR 6 1 0.15 0.39 0.038
SITE_CHAR 6 2 0.15 0.39 0.044
SITE_CHAR 7 1 0.18 0.42 0.165
SITE_CHAR 7 2 0.18 0.42 0.184
SITE_CHAR 8 1 0.18 0.42 0.165
SITE_CHAR 8 2 0.18 0.42 0.184
SITE_CHAR 9 1 0.18 0.42 0.165
SITE_CHAR 9 2 0.18 0.42 0.184
SITE_CHAR 10 1 0.17 0.74 0.028
SITE_CHAR 10 2 0.17 0.74 0.032
SITE_CHAR 11 1 0.17 0.74 0.028
SITE_CHAR 11 2 0.17 0.74 0.032
SITE_CHAR 12 1 0.17 0.74 0.028
SITE_CHAR 12 2 0.17 0.74 0.032
MC
FREQ_SECT MONTHLY 3
SECTOR 1 60.00 235.00
SECTOR 2 235.00 320.00
SECTOR 3 320.00 60.00
** Month Sect Alb Bo Zo
SITE_CHAR 1 1 0.18 0.90 0.025
SITE_CHAR 1 2 0.18 0.90 0.015
SITE_CHAR 1 3 0.18 0.90 0.018
SITE_CHAR 2 1 0.47 0.49 0.017
SITE_CHAR 2 2 0.47 0.49 0.009
SITE_CHAR 2 3 0.47 0.49 0.011
SITE_CHAR 3 1 0.47 0.49 0.017
SITE_CHAR 3 2 0.47 0.49 0.009
SITE_CHAR 3 3 0.47 0.49 0.011
SITE_CHAR 4 1 0.16 0.60 0.031
SITE_CHAR 4 2 0.16 0.60 0.021
SITE_CHAR 4 3 0.16 0.60 0.023
SITE_CHAR 5 1 0.16 0.60 0.031
SITE_CHAR 5 2 0.16 0.60 0.021
SITE_CHAR 5 3 0.16 0.60 0.023
SITE_CHAR 6 1 0.16 0.60 0.031
SITE_CHAR 6 2 0.16 0.60 0.021
SITE_CHAR 6 3 0.16 0.60 0.023
SITE_CHAR 7 1 0.17 0.67 0.036
SITE_CHAR 7 2 0.17 0.67 0.027
SITE_CHAR 7 3 0.17 0.67 0.029
SITE_CHAR 8 1 0.17 0.67 0.036
SITE_CHAR 8 2 0.17 0.67 0.027
SITE_CHAR 8 3 0.17 0.67 0.029
SITE_CHAR 9 1 0.17 0.67 0.036
SITE_CHAR 9 2 0.17 0.67 0.027
SITE_CHAR 9 3 0.17 0.67 0.029
SITE_CHAR 10 1 0.18 0.90 0.025
SITE_CHAR 10 2 0.18 0.90 0.015
SITE_CHAR 10 3 0.18 0.90 0.018
SITE_CHAR 11 1 0.18 0.90 0.025
SITE_CHAR 11 2 0.18 0.90 0.015
SITE_CHAR 11 3 0.18 0.90 0.018
SITE_CHAR 12 1 0.18 0.90 0.025
SITE_CHAR 12 2 0.18 0.90 0.015
SITE_CHAR 12 3 0.18 0.90 0.018
KABE