## Slide 1: AERMINUTE
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Describe the purpose of AERMINUTE
List the AERMINUTE data input requirements
Construct an AERMINUTE input control file

## Slide 3
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
1 MINUTE ASOS DATA
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA

## Slide 4: NWS Surface Data
NWS Standard ASOS Data - ISHD :
  Early NWS data consisted of hourly observations made at the top of the hour by a human observer.
  Around 2005 the observer was replaced by ASOS
  Integrated Surface Hourly data (ISHD). Data from multiple sites archived in one place and with one format
  This data is known as Standard ASOS data and can be downloaded at:
http://www1.ncdc.noaa.gov/pub/data/noaa/

## Slide 5: Change to ASOS - Ice free Winds
ASOS Ice Free Wind (IFW) sensor program replaced cup and vane sensors with heated sonic anemometers
Sensor replacement began in 2005
List of stations with their IFW installation dates, as of October 27, 2009, can be found at (Browser only)
  https://www.weather.gov/media/asos/ASOS%20Implementation/IFW_stat.pdf
  More information on ice-free winds at (Browser only)
    https://www.weather.gov/asos/ASOSImplementation

## Slide 6: ASOS Data
ASOS stations have one of two different statuses: commissioned and non-commissioned
A non-commissioned site is the Standard ASOS data we discussed before. This data is a 2 min average at the top of the hr. (automated version of human observations)
Once a site is commissioned a rolling 2 min averaged is archived for each 1 min in the hr. (1-min ASOS data)
With Commissioned data a true one-hour average can be produced. This significantly increased the accuracy of model predictions since the data, whether observer based, standard ASOS or 1-min ASOS data is assumed to be a 1hr average
⸫ Knowing the commissioned date is essential when choosing ASOS data.

## Slide 7: ASOS 1 Min Data
For each station and year, files are available in monthly blocks, i.e., one file per month for a station
Files are generally named: 64050XXXXYYYYMM.dat
  XXXX is the 4-character station call sign
  YYYY and MM are the 4-digit year and 2-digit month
This data needs to be processed by AERMINUTE to create the hourly averages and format it for AERMET’s use.
1 Min ASOS Data can be acquired from the following site:
https://www1.ncdc.noaa.gov/pub/data/asos-onemin/

## Slide 8: Control Options
Unless otherwise noted, all control file keywords and parameters are mandatory
  STARTEND – start and end dates of the data
  IFWGROUP—ice-free wind group
    Status—indicates if the station is part of the IFW group
    comm_month, comm_day, comm_year
  DATAFILE STARTING
    1min.Datafiles_list (1-minute ASOS data)
  DATAFILE FINISHED
  SURFDATA STARTING
    Surface_files_list (Standard ASOS ISH data)
  SURFDATA FINISHED

## Slide 9: Control Options
  OUTFILES STARTING—list of output files follows
    HOURFILE name (this is an AERMET input file)
    SUMMFILE name (Optional)
    COMPFILE name (Optional)
  OUTFILES FINISHED—list of output files is completed
  We will discuss the control file when we run AERMINUTE