## Slide 1: AERMINUTE Hands-on
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Describe the input requirements for AERMINUTE
Download the input meteorological data needed to run AERMINUTE
Run AERMINUTE and produce output that can be input to AERMET

## Slide 3: AERMINUTE—Obtaining Data
AERMINUTE processes one or more monthly files of 1 min. ASOS data
Data are available at:
  https://www1.ncdc.noaa.gov/pub/data/asos-onemin/
For this exercise download the following 1 min ASOS file:
  64050KABE200801.dat
  All other months of the 5 yr. data needed has been provided. This included NWS data for substitution
Place the downloaded file in the following sub-directory : \>MODL_301\Hands-on\AERMINUTE\

## Slide 4: AERMINUTE—Files Needed
  The 1-minute ASOS wind data files and program executable needed to complete this hands-on activity can be found in the following directory:
  \>MODL_301\Hands-on\AERMINUTE\
  aerminute_15272.exe: program executable
  aerminute.inp: AERMINUTE control file
  14737-yyyy.DAT: National Weather Service (NWS) hourly observations, Standard ASOS (used for substitution)
  64050KABEyyyymm.dat: 1-minute ASOS wind data files where:
  yyyy = year
  mm = month

## Slide 5: Running AERMINUTE
Run AERMINUTE by navigating to the directory: \>MODL_301 \Hands-On\AERMINUTE\
  To start AERMINUTE double click on the executable
  A command prompt will open and ask you to enter the name of the input file
  Enter the input file name and then hit enter
An Output file, which is named after the keyword HOURFILE (located in the input file), is an input file to AERMET

## Slide 6: Additional Output
aerminute.log: summary of user inputs, data files processed, and summary statistics
good_records.dat: valid records according to strict quality control checks in AERMINUTE and the winds from these files are considered valid
bad_records.dat: records from the 1-minute files that did not meet the strict quality controls in AERMINUTE and are unlikely to contain usable data
check_records.dat: records that did not meet the strict quality controls in AERMINUTE and are not used in calculating hourly averages but could possibly be edited to provide useful data
Four Optional files

## Slide 7: Reviewing AERMINUTE Output
HOURFILE (KABE_2008-2012_1-Min_hour.out) - this is the file that is passed to AERMET
AERMINUTE Version 15272 WBAN: 14737 Call sign: KABE
IFW date: 09/08/2006
Y M D H WS WD
8 1 1 1 999.00 999.0
8 1 1 2 999.00 999.0
8 1 1 3 999.00 999.0
8 1 1 4 999.00 999.0
8 1 1 5 3.64 100.0
8 1 1 6 5.59 124.0
8 1 1 7 2.07 180.0
8 1 1 8 3.67 152.0
8 1 1 9 4.47 186.0