## Slide 1: AERMET—Part 2
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Explain the pathways, keywords, and options in AERMET control files
Construct AERMET control files
Execute each of the two stages of AERMET
QA AERMET output

## Slide 3
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA
1 MINUTE ASOS DATA

## Slide 4: AERMET Processing

## Slide 5: The Control File
AERMET Pathways
  JOB—report files (all stages)
  SURFACE—Standard ASOS (Stage 1) and 1-min ASOS (Stage 2)
  UPPERAIR—typically twice-daily NWS soundings (Stage 1)
  ONSITE—site-specific data (Stage 1)
  METPREP—Stage 2

## Slide 6: The Control File—Stage 1
Allowable pathways in AERMET Stage 1:
  JOB
  SURFACE
  UPPERAIR
  ONSITE
What does AERMET Stage 1 do:
  Extracts data from two archive files:
  1) SURFACE & 2) UPPERAIR
  Archive file are fixed with unchanging format for storing data
  Performs a basic QA check on the quality of SURFACE, UPPERAIR & ONSITE data

## Slide 7: The Control File - Stage 1 Keyword JOB
  Allows the user to specify the files where all messages are stored and summarized
MESSAGES: Name of the file where AERMET will store all the messages during the run
  MESSAGES message filename
REPORT: Name of the file where AERMET generates a summary of the input and the messages
  REPORT summary filename

## Slide 8: The Control File Keywords - Stage 1 surface & upperair
  The section that tells AERMET what upper air sounding and surface data to process
DATA: Input filename of the “archived” data
  DATA archive_filename file_format
EXTRACT: Output filename of extracted data
  EXTRACT extracted_data_filename
LOCATION: Identifies the station and its location
  LOCATION site_id lat/lon lon/lat tadjust

## Slide 9: The Control File Keywords - Stage 1 surface & upperair
XDATES: Specifies the date range to extract from the “archive”
  XDATES YB/MB/DB [TO] YE/ME/DE
QAOUT: Output filename of extracted data after it has undergone quality assurance procedures
  QAOUT qa_output_filename

## Slide 10: The Control File Keywords—Stage 1 ONSITE
  Recall that site-specific data are not in a data archive, so there is no EXTRACT keyword
DATA: Input filename of the data to process
  DATA filename
LOCATION: Identifies the station and its location
  LOCATION site_id lat/lon lon/lat [tadjust]
XDATES: Specifies the date range to extract from the “archive”
  XDATES YB/MB/DB [TO] YE/ME/DE

## Slide 11: The Control File Keywords—Stage 1 ONSITE
QAOUT: Output filename of extracted data after it has undergone quality assurance procedures
  QAOUT qa_output_filename
READ: Specifies the list and order of variables in the site-specific data file that are to be read
  READ record_index variable_1 variable_2 …
Each record has a “record index”
FORMAT: The format of the data using FORTRAN formatting rules
  FORMAT record_index Fortran_format

## Slide 12: The Control File Keywords—Stage 1 ONSITE
THRESHOLD: Sets the minimum wind speed (meters/second) below which the wind is treated as calm
  THRESHOLD threshold_wind_speed
RANGE: Set new upper, lower bounds for the QA and missing indicator
  RANGE sfname lower_bound <[=] upper_bound missing_indicator

## Slide 13: The Control File Keywords—Stage 1 ONSITE
AUDIT: Identifies the variables to QA beyond the three default variables (Temp, wind speed & dir)
NO_MISSING: Suppresses missing data QA messages to the MESSAGE file and does not tally the number missing for the QA’d variables
  NO_MISSING sfname1 sfname2 … sfnameN

## Slide 14: The Control File—Stage 2
JOB – as in Stage 1
UPPERAIR – output from Stage 1
SURFACE
  output from Stage 1
  1 min. ASOS data
ONSITE - output from Stage 1

## Slide 15: The Control File Keywords—Stage 2 METPREP
The Pathway instructs AERMET how to process the data:
  Defines how the boundary layer calculations are to be made
  Creates the two meteorological files required by AERMOD
METPREP has an extensive array of keywords; we will look only at the one’s used in the exercise

## Slide 16: The Control File Keywords—Stage 2 METPREP
METHOD: Specifies the processing methodology/option for a variable
  METHOD atmospheric_variable option
NWS_HGT: NWS instrument height, in meters
  NWS_HGT variable_name instrument_height
OUTPUT: File of surface and near-surface parameters
  OUTPUT parameter_filename
PROFILE: File contains met observations
  PROFILE parameter_filename

## Slide 17: The Control File Keywords—Stage 2 METPREP
AERSURF (Identifies location of surface characteristics)
  File name from AERSURFACE “PRIMARY” output from on-site data …\MC\
AERSURF2 (Identifies location of surface characteristics)
  file name for AERSURFACE “SECONDARY” output from met site used for substitution …\KABE2\