## Slide 1: AERMET Hands-on
MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Execute AERMET’s two-stage processing
Download the meteorology needed for the exercises
Develop the needed input for each stage
Run each of AERMET’s stages
Analyze and evaluate the results produced from AERMET

## Slide 3: AERMET Processes in 2 Stages
Stage 1: Extract data from archive, format and QA data
Stage 2:
  Input 1-min. ASOS from AERMINUTE output
  Pass all meteorological observations through to AERMOD
  Utilize Surface Characteristics from AERSURFACE
  Calculate PBL parameters and output results for AERMOD
Run each separately

## Slide 4: Geographical Setting—Martins Creek

## Slide 5: Meteorological Data
Site Specific:
  A single level of data from a 10-meter tower
  12 levels of data from a nearby sodar
NWS Data:
  Standard ASOS (ISHD): Allentown/Bethlehem – WMO # 14737 (KABE)
  Upper Air Data (IGRA): Albany, NY
  Station#: USM00072518

## Slide 6: Hands-on Activity
Two AERMET scenarios
  1-year (5/1/2011–4/30/2012)
    Martins Creek site-specific data (5/1/1992 – 4/30/1993) – Primary met data
    NALC Surface data from MC onsite
    1-minute ASOS Data from Allentown airport– used for substitution into MC DATA Secondary met data
    NWS surface data from Allentown airport
    NWS upper air data Albany airport
  5-year (1/1/2008–12/31/2012)
    1-minute ASOS Data from Allentown airport– Primary met data
    NALC Surface data from Allentown airport
    NWS surface data from Allentown airport
    NWS upper air data from Albany airport
    No On-Site data

## Slide 7: AERMET—Files
  The program executable, along with the AERMET user’s guide, can be found in the following directory:
  \>MODL_301\Hands-On\AERMET\
  Develop data for two scenarios
    1 year with ONSITE data
    \>MODL_301 \Hands-On\AERMET\1-yr_Onsite\
    5 years with NWS data only
    \>MODL_301 \Hands-On\AERMET\5-yr_NWS\

## Slide 8: AERMET—Files Needed
  Input files for 1-year scenario
  …\1-yr_Onsite\MC_Site-Specific_Data\MCOSPFL_11-12.DAT: Onsite observations
  …\ 1-yr_Onsite\NWS_Surface_data\..... (Downloaded)
  …\ 1-yr_Onsite\NWS_Upper_Air_data\... (Downloaded)
  …\ 1-yr_Onsite\MC_ST1.INP: Stage 1 control file
  …\ 1-yr_Onsite\MC_ST2.INP: Stage 2 control file
  …\ 1-yr_Onsite\RunMC – Stage I.BAT: Runs Stage I
  \RunMC – Stage II.BAT: Runs Stage II

## Slide 9: AERMET—Files Needed
  Input files for 5-year scenario
  …\ 5-yr_NWS\NWS_Surface_data\........ (Download)
  …\ 5-yr_NWS\NWS_Upper_air_data\........ (Download)
  …\ 5-yr_NWS\MC_ST1.INP: Stage 1 input
  …\ 5-yr_NWS\MC_ST2.INP: Stage 2 input
  …\ 5-yr_NWS\RunMC.BAT: Batch file that runs both stages

## Slide 10: AERMET— Surface Hourly Observations
Download the 2008-2012 Standard ASOS data for WMO site 14737 – need to concatenate the 5 files into one file. Each file is a .gz file that needs to be unzipped.
https://www1.ncdc.noaa.gov/pub/data/noaa/
To run the one year of on-site data from 5/1/2011 to 4/30/2012:
  We will use the 5 years that we downloaded
  Instruct AERMET to extract the dates needed
5 yrs of Met surface data have already been downloaded and concatenated they are in both:
…\5-yr_NWS\NWS_Surface_data\
…\1-yr_Onsite\ NWS_Surface_data\

## Slide 11: AERMET—Upper Air
  Upper Air data is acquired from the Integrated Global Radiosonde Archive (IGRA)
  A README file for the IGRA data is at:
  https://www.ncei.noaa.gov/pub/data/igra/igra2-readme.txt
  Procedure for downloading the data of interest:
    Find the upper air station of interest at the following:
    https://www.ncei.noaa.gov/pub/data/igra/igra2-station-list.txt
    Format: https://www.ncei.noaa.gov/pub/data/igra/igra2-list-format.txt
    Write down the station ID and/or copy to clipboard
    Download the file from:
    https://www.ncei.noaa.gov/pub/data/igra/data/data-por

## Slide 12: AERMET—Upper Air
  Procedure for creating the file that contains UA data for 2008-2012
    The initial file you downloaded has data from 1930-2025
    Extract the data from 2008-2011 by copying this portion of the file to a separate .txt file or simply use the full file (but AERMET runs longer)
The Upper Air data from Albany has already been downloaded and the data for 2008-2012 has been extracted to a .txt file and placed in:
…\5-yr_NWS\NWS_Upper_Air_data\
…\1-yr_Onsite\ NWS_Upper_Air_data\

## Slide 13: Stage 1
Processing 1yr. Onsite
Scenario

## Slide 14: Stage 1—Control File Parameters
Hourly Surface Observations
  Data file name
  Data format: ISHD
  Latitude/longitude: 40.65N, 75.43W, Eastern time zone
  Dates to process: May 1, 2011–April 30, 2012
Upper Air Soundings
  Data file name
  Data format: IGRA
  Latitude/longitude: 42.75N, 73.80W, Eastern time zone
  Site Elevation = 94m
  Dates to process: May 1, 2011–April 30, 2012
Site-specific (Onsite) Data
  Data file name
  Data format: user-specified
  Latitude/longitude: 40.79N, 75.14W, local time
  Dates to extract: May 1, 2011–April 30, 2012
  Anemometer starting threshold speed: 0.3 m/s

## Slide 15: Running AERMET Stage i
Run Stage 1 for the Martins Creek 1-year scenario using the site-specific data:
Navigate to \>MODL_301\Hands-on\AERMET\1-yr_Onsite\
Start AERMET by double clicking the file: RunMC - Stage I.bat (This batch file identifies where the executable is and identifies the names and locations of the input file).
A command prompt window will open showing you the program’s progress.
The output from Stage 1 that will be input to Stage 2 are: ONSITE_QAOUT.TXT, SURFACE_QAOUT.TXT, UPPER_QAOUT.TXT
ControlFileName

## Slide 16: Stage 2

## Slide 17: Stage 2—Control File Parameters
Three processing options used in hands-on exercise (METHOD keyword)
  Substitute NWS data
  When NWS data are substituted, randomize the wind direction
  Anemometer height: 7.9 meters

## Slide 18: Running AERMET Stage 2
Run Stage 2 for the Martins Creek 1-year scenario using the site-specific data:
Navigate to \>MODL_301\Hands-on\AERMET\1- yr_Onsite\
Start AERMET by double clicking the file: RunMC - Stage II.bat (This batch file identifies where the executable is and identifies the name of the input file).
A command prompt window will open showing you the program’s progress.

## Slide 19: Run Both Stages with One Click
Using a batch file, AERMET can be run two separate times without user intervention between each stage
You will use this technique in developing the 5-year NWS dataset for AERMOD
aermet mcr_st1.inp
aermet mcr_st2.inp

## Slide 20: Run The 5yr Scenario
It is important to run the following, so you have a processed 5-year dataset for AERMOD (to examine the results for the new probabilistic 1-hour standards for SO2 and NO2)
Rerun AERMET for the 5-year NWS-only
  Navigate to: \>MODL_301\Hands-on\AERMET\5-yr_NWS\
  Double-Click on RunMC.bat

## Slide 21: Next: Exercise 2