## Slide 1: EXERCISE 2
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Exercise 2
Examine the sensitivity of the PBL parameters to defining different sectors for Zo
Re-Run AERSURFACE, using the …\AERSURFACE\KABE\ case based on your own selection of the number and size of the sectors used to calculate Zo. Procedure follows:
  A topo map of the area surrounding the Allentown airport is on the next two slides. The first map shows a color map. The 2nd map shows 12 sectors out to 1 km (the default distance for defining Zo) are illustrated.
  Using this topo map select the number and size of the sectors that you believe are adequate for calculating Zo for this location; i.e. for each sector chosen, define their starting and ending direction (make sure that the starting direction of the 1st sector = the ending direction of the last sector). And define each sector as either LOWZ0 or HIGHZ0 based on whether it contains industrial and commercial buildings (HIGHZ0) or contains mostly residential areas with roads, parking lots, runways (i.e., low level impervious surface) (LOWZ0).
Notes: This slide

## Slide 3
Allentown Airport
(Google Earth)

## Slide 4
60o
Allentown Airport (Google Earth)
0o
30o
150o
90o
120o
180o
210o
240o
270o
300o
330o
60o
0o
30o
150o
90o
120o
180o
210o

## Slide 5: Exercise 2
    3. An empty sub-directory named \Exercise_2_Zo\ located in …\AERSURFACE\KABE\. Copy the following files from …\AERSURFACE\KABE\ into …\AERSURFACE\Exercise_2_Zo\:
      AERSURFACE.inp
      RunKABE.bat
    Edit the file AERSURFACE.inp:
      Edit the keywords FREQ_SECT & SECTOR to represent the sectors you choose.
      Change the name of the output file from KABE_2011_Imp_Can.sfc to Ex_2_Imp_Can.sfc

## Slide 6: Exercise 2
    Make sure that all files that are not in the working directory are properly referenced in both AERSURFACE.inp and RunKABE.bat
    Run AERSURFACE using the .bat file
    Compare these results to the results from the Hands-On run

## Slide 7: Hand-On vs. Exercise 2
Hands-On Run
Month Sect Zo
1 1 0.025
1 2 0.015
1 3 0.018
4 1 0.031
4 2 0.021
4 3 0.023
7 1 0.036
7 2 0.027
7 3 0.029
10 1 0.025
10 2 0.015
10 3 0.018
Exercise 2
Month Sect Zo
1 1 0.017
1 2 0.015
1 3 0.031
1 4 0.115
1 5 0.056
1 6 0.074
1 7 0.024
1 8 0.017
1 9 0.014
1 10 0.014
1 11 0.021
1 12 0.021
4 1 0.023
4 2 0.021
4 3 0.037
4 4 0.138
4 5 0.072
4 6 0.092
4 7 0.030
4 8 0.023
4 9 0.019
4 10 0.020
4 11 0.027
4 12 0.027
Exercise 2
Month Sect Zo
7 1 0.028
7 2 0.026
7 3 0.041
7 4 0.156
7 5 0.085
7 6 0.108
7 7 0.036
7 8 0.028
7 9 0.025
7 10 0.025
7 11 0.034
7 12 0.034
10 1 0.017
10 2 0.015
10 3 0.031
10 4 0.115
10 5 0.056
10 6 0.074
10 7 0.024
10 8 0.017
10 9 0.014
10 10 0.014
10 11 0.021
10 12 0.021
Exercise 2
Sector Angles
1 0 - 30
2 30 - 60
3 60 – 90
4 90 – 120
5 120 – 150
6 150 – 180
7 180 – 210
8 210 – 240
9 240 – 270
10 270 – 300
11 300 - 330
12 330 - 360
Hands On
Sector Angles
1 60 - 235
2 235- 320
3 320 – 60

## Slide 8
Allentown Airport (Google Earth)
240o
270o
300o
330o
60o
0o
30o
150o
90o
120o
180o
210o
Hands On
Sector Angles Zo
1 60 – 235 L 0.031
2 235- 320 L 0.021
3 320 – 60 L 0.023
Exercise 2 (Al’s)
Sector Angles Zo
1 0 – 30 L 0.023
2 30 – 60 L 0.021
3 60 – 90 L 0.037
4 90 – 120 H 0.138
5 120 – 150 H 0.072
6 150 – 180 H 0.092
7 180 – 210 L 0.030
8 210 – 240 L 0.023
9 240 – 270 L 0.019
10 270 – 300 L 0.020
11 300 - 330 L 0.027
12 330 – 360 L 0.027
Exercise 2 (Steve’s)
Sector Angles Zo
1 90 – 210 H 0.093
2 210- 240 L 0.023
3 240 – 300 L 0.020
4 300 - 90 L 0.027

## Slide 9: Exercise 2
To examine the effects these changes in Zo have on the PBL parameters, we now need to run AERMET using the new Zo’s
An empty sub-directory named ...\Exercise_2\ is in the sub-directory …\AERMET\5-yr_NWS\. Copy the following files from …\ 5-yr_NWS \ into the …\Exercise_2\ sub-directory:
  KABE_ST1.INP
  KABE_ST2.INP
  RunKABE.bat

## Slide 10: Exercise 2
Edit file KABE_ST2.INP:
  Change “KABE_2011_Imp_Can.scf” to “\Exercise_2_Zo\Ex_2_Imp_Can.sfc”
  Change “KABE_2008-2012.sfc” to “Ex_2_ KABE_2008-2012.sfc”
  Change “KABE_2008-2012.pfl” to “Ex_2_ KABE_2008-2012.pfl”
  Make sure that all files that are not in the working directory are properly referenced to where they actually exist in both KABE_ST1.INP, KABE_ST2.INP and RunKABE.bat
  Execute RunKABE.bat

## Slide 11: Exercise 2
  What parameters in the AERMET’s Ex_2_ KABE_2008-2012.sfc file would you expect to change?
  After completing the exercise:
  Compare the Ex_2_ KABE_2008-2012.sfc met file with the .sfc met file from the hands-on run, KABE_2008-2012.sfc (AERMET\5-yr_NWS)
    Open the header file (MC_2011-2012_header.SFC.txt) to facilitate the comparison

## Slide 12
Exercise 2
  Effect of sector selection and roughness designation
  2008 May 1 hr. 9 (U = 2.6, WD = 91)
  zo L u* zim
  Hands on 0.031 -9.2 0.23 264
  Al (12 sectors) 0.138 -21.5 0.30 403
  Steve (4 sectors) 0.093 -16.8 0.28 356
  __________________________________________________
  2008 May 6 hr. 10 (U = 1.3, WD = 186)
  zo L u* zim
  Hands on 0.031 -1.6 0.14 127
  Al (12 sectors) 0.030 -1.6 0.14 126
  Steve (4 sectors) 0.093 -2.9 0.17 173