## Slide 1: AERMOD Fundamentals Part 2
Course #MODL301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: FUNDAMENTALS
Part 1 (Monday)
Energy balance, atmospheric stability, and the structure of the Atmospheric Boundary Layer (ABL)
How AERMOD Characterizes the ABL
Part 2
AERMOD – vertically varying meteorology
AERMOD plume structure
Significant effects on Dispersion
  (building wakes, terrain influences)

## Slide 3
AERMOD Modeling System
Input
Surface Characteristics AERSURFACE
Input
Meteorology AERMINUTE
Input
Terrain data
AERMAP
Input
Building data BPIPPRM
AERMOD
Compute PBL parameters
AERMET
Establish
Meteorology
Profiles
Compute
Concentrations

## Slide 4
Steady-state Gaussian-plume model
(Not single Gaussian in Convective)
Near-source applications (< 50km)
Point, area, volume and line source types
Flat/complex terrain, urban/rural areas
Wet/dry deposition
NO2 chemistry
Building wake effects
One-hour average concentrations
aermod

## Slide 5
Gaussian
Plume

## Slide 6: AERMOD—Effective Parameters
AERMOD accounts for the vertical inhomogeneity of the ABL by "averaging" that portion of a variable’s profile from the plume center to the receptor height to produce a single effective value for calculations at that receptor (iterative).

## Slide 7
zi
Plume Centerline
U(z)
Ueff = avg U
over layer
receptor
AERMOD—Effective Parameters

## Slide 8: AERMOD PLUMES Stable Boundary Layer (L > 0)
Strength of stability influenced by surface cooling
Turbulence in the SBL is driven by shear
Turbulence is largest at surface and decays with height
Mixing is suppressed by temperature gradient

## Slide 9
  Both the horizontal and vertical concentration distributions are Gaussian
AERMOD PLUMES Stable Boundary Layer (L > 0)

## Slide 10
  The horizontal concentration distribution is assumed to be a simple Gaussian form (as with Stable conditions)
AERMOD PLUMES Convective Boundary Layer (L < 0)

## Slide 11
Growth of layer and strength of instability is due primarily to surface heating
Convective cells create areas of updrafts and downdrafts
  60% downdrafts vs. 40% updrafts resulting a non-Gaussian vertical structure
AERMOD accounts for non-Gaussian vertical structure of dispersion in the CBL
  Pollutants released into updrafts are simulated separately from those released into downdrafts
AERMOD PLUMES Convective Boundary Layer (L < 0)

## Slide 12: Convective Boundary Layer
EPA, AERMOD: Description of Model Formulation, 2004

## Slide 13
AERMOD PLUMES Convective Boundary Layer (L < 0)
Zi
Height
Mixed
Layer
Surface
Layer
Penetrated Material
Direct Material
w*
Indirect Material
Vertical concentration distribution results from a combination of three plume types (Weil and Brower, 1984)

## Slide 14
AERMOD PLUMES Convective Boundary Layer (L < 0)
Direct
Indirect
Penetrated

## Slide 15
  Injected plume: the plume is released into the elevated stable layer above the mixed layer
    Modeled in a manner similar to that of the penetrated plume. That is, with the stable plume equations but the calculation of effective parameters will consider the level of the turbulence and the winds both in the stable layer and the convective mixed layer.
AERMOD PLUMES Convective Boundary Layer (L < 0)

## Slide 16
AERMOD Model Formulation
- November 2024

## Slide 17
Terrain Influences
Dividing Streamline Concept
Dividing Steamline (Hc)
Can the kinetic energy of flow at each level overcome the potential energy needed to surmount the terrain feature?
U(z)
Hc

## Slide 18: Terrain Influences
Plume is modeled as a combination of two limiting cases
  A horizontal (terrain impacting) plume representing the material below Hc
  A terrain-following (terrain responding) plume representing the material above Hc

## Slide 19
Terrain Influences
Dividing Streamline Concept
Dividing Steamline (Hc)
Can the kinetic energy of flow at each level overcome the potential energy needed to surmount the terrain feature?
U(z)
Hc

## Slide 20: Terrain Influences
EPA, AERMOD: Description of Model Forumulation, 2004
Hc
hc

## Slide 21: Terrain Influences
AERMAP uses gridded terrain data to obtain a representative terrain-influence height (or hill height scale, hc) for each receptor
  Actual terrain height, which most influences the flow in the vicinity of the receptor
  Not necessarily the height of a particular hill
Inherent assumptions in determining hc
  Terrain influence decreases with distance from receptor
  Terrain influence increases with increasing terrain height

## Slide 22
hc
Receptor
10° slope
Estimation of hill-height scale
AERMAP estimates hill-height scale in all directions
(every ten degrees azimuth) for each receptor

## Slide 23: Building Influences/Downwash
Cavity or
Near Wake
Far Wake

## Slide 24: Building Influences/Downwash
Cavity or
Near Wake
Far Wake

## Slide 25: Building Influences/Downwash
Primary effects of downwash on plume
  Plume rise / Plume height
    Suppression due to increased turbulence and descending streamlines
    Enhancement due to velocity deficit and ascending streamlines
  Enhanced vertical and lateral turbulence
  Reduced wind speed in the wake
  Recirculation of plume material in cavity
  (Magnitude of effects depend on source location and height relative to the building)

## Slide 26: Building Influences/Downwash
Result: Potential for significantly higher short-term, ground-level concentrations near the source
*Much more on Building Downwash this afternoon

## Slide 27: Other important AERMOD capabilities
Urban Effects - nighttime boundary layer
NOx Chemistry
Wet / Dry Deposition
Low Wind / Meander conditions
Offshore releases / coastal impacts (COARE)
Roadway type (line) sources
Variety of Alpha / Beta options
  Building downwash improvements
  Roadway noise barriers / depressed roadways
  Buoyant line sources

## Slide 28: Important Documents (updated Nov 2024)
User's Guide for AERMOD
AERMOD Model Formulation
AERMOD Implementation Guide
User’s Guides for AERSURFACE, AERMET, AERMAP, and BPIPPRM
Model Change Bulletin (MCB) #18
https://www.epa.gov/scram/air-quality-dispersion-modeling

## Slide 29
End of Part 2