## Slide 1: AERMAP
Course MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Explain what AERMAP does and why it is needed
Describe AERMAP’s data requirements and where to get them
Describe the structure of AERMAP’s Control file

## Slide 3
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA
1 MINUTE ASOS DATA

## Slide 4: AERMAP—Purpose
Develop the hill height scale for every receptor
  Hill height scale – hc: The terrain height that has the greatest influence on dispersion for each receptor being modeled – receptor specific.
  Think of hc as the height of a conceptual hill on which the receptor being modeled is located.
  For each individual receptor, the hill height scale is the highest elevation that rises above a slope line of 10% starting at the receptor out to the end of the domain

## Slide 5
hc
Receptor
10° slope
Estimation of hill-height scale
AERMAP estimates hill-height scale in all directions
(every ten degrees azimuth) for each receptor

## Slide 6: AERMAP—Purpose
  This is done for all directions within a user defined search domain for each receptor - Independent of wind direction
  HCrit is calculated (in AERMOD) for each hc and ⸫ for each receptor
  The Hcrit, for each receptor, is used to determine the partitioning of plume mass between the horizontal and “terrain responding” plume states.
Develop terrain base elevations for every receptor and source

## Slide 7: AERMAP—Input Terrain Data
3DEP Seamless DEM/NED
  Only data presently available for AERMAP
  What are 3DEP Seamless DEM data?
    High resolution elevation data
    Available across the United States
    Provided in a seamless raster (pixel) format
    2-arc-second, 1-arc-second, and 1/3-arc-second
    60-meter, 30-meter, and 10-meter
  Format: GeoTiff

## Slide 8: AERMAP—Control File
Pathway/keyword structure is used
AERMAP pathways: CO, SO, RE, OU
The SO pathway:
  AERMAP will determine source base elevations if you choose. Then paste into AERMOD’s input file or if you have a large number of sources you could use an INCLUDE file.
The RE pathway:
  Mandatory for calculating hc
  Identify or construct the set of receptors to be modeled w/ their elevation

## Slide 9: AERMAP—Control Pathway
CO DOMAINXY
  Specifies the extent, in UTM coordinates, of the search domain
    DOMAINX Xdmin Ydmin Zomin Xdmax Ydmax Zomax
  Xdmin, Ydmin: Specifies the southwest (lower left) corner of the search domain
  Zonmin: UTM zone for the lower left corner
  Xdmax, Ydmax: Specifies the northeast (upper right) corner of the domain
  Zonmax: UTM zone for the upper right corner

## Slide 10: AERMAP—Control Pathway
CO ANCHORXY
  Defines the user-specified coordinate system for receptors in UTM format
    ANCHORXY Xauser Yauser Xautm Yautm Zautm NADA
  Xauser, Yauser: Location in the user’s coordinate system
  Xautm, Yautm: Location of the same point in the UTM coordinate system (i.e., the reference datum being used)
  NADA_value: North American Datum Anchor point—the horizontal datum used to establish the anchor point and range from zero to six; a value of 4 (which represents NAD83) should be used for Seamless DEM data

## Slide 11: Receptor Pathway Keywords
RE GRIDCART
  Gridded locations referenced to a Cartesian coordinate system
RE GRIDPOLR
  Gridded locations referenced to a polar coordinate system
RE DISCCART
  Repeatable discrete locations referenced to a Cartesian system
RE DISCPOLR
  Repeatable discrete locations referenced to a polar network
RE INCLUDED
  Include data from a separate file
    INCLUDED RecIncludeFile

## Slide 12: AERMAP—Output Pathway
OU RECEPTOR
  Identifies the output filename for the receptor data
    RECEPTOR Recfil
OU SOURCLOC
  Identifies the output filename for the source data
    SOURCLOC Srcfil

## Slide 13: AERMAP—Running AERMAP
AERMAP control file must be in same directory as the AERMAP executable
Control Filename: Either AERMAP.INP (default) or User Defined
Windows environment
  If you use the default name for the control file, then simply double-click aermap.exe
  Output filename  AERMAP.OUT