## Slide 1: AERMAP Hands-on
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Define the modeling domain
Download terrain data and uncompress it for use in AERMAP
Develop the input requirements needed to run AERMAP
Construct an AERMAP control file
Execute the AERMAP preprocessing program
Review AERMAP output

## Slide 3: Search Domain
Considerations for Defining the Domain:
  The area containing the sources to be modeled
  The full receptor area
  The area that contains all significant terrain elevations
This is called the Search Domain, because its primary purpose is to determine the proper hill height scale for each receptor
Can cross Universal Transverse Mercator (UTM) zones
All coordinates must be referenced to same zone

## Slide 4: Search Domain
How far should the search domain extend?
  No specific guidance
  Examine the region beyond the receptor network
  The domain needs to be large enough for the correct hc to be found for each receptor
  Include all terrain close enough to all receptors that can impact the flow in relation to the receptor
  Do not include extremely high but distant terrain

## Slide 5: AERMAP—Obtaining NED Data
It is recommended that the “3DEP Seamless Digital Elevation Model (DEM)” (NED) data be used for AERMAP
3DEP Seamless DEM data or (NED) can be obtained from:
  https://apps.nationalmap.gov/downloader/#/
  Use the following instructions to acquire the DEM Data:
In the left panel select the box, under Data, labeled “Elevation Products (3DEP)”
Check the box “1 arc-second DEM” and leave the box “Current”, under “1 arc-second DEM” checked.
Uncheck all other boxes and make sure radio button GeoTiff is selected
Type in Martins Creek in the last text box in the upper right corner of the map – This will take you the town of Martins Creek
Move NE along the Delaware River to the town of Belvidere. The power station is located approximately ½ way between Martins Creek and Belvidere on the PA side of the river. – move to that location.
Determine the size for your Search Domain and zoom out until your area on the screen is larger than the size of your Search Domain.
Scroll the left panel to the top and click on the icon “Extent”
Place the red dot curser beyond the NW corner of the search domain. Then continuing to hold the left mouse button down move the cursor to a point well beyond the SE corner of the search domain.
In the left panel click on “Search Products”
Two maps should appear in the left panel. Move the cursor over each to ensure that they cover the entire red box on the map.
For each map in the left panel click on the shopping cart icons. Then click the word cart at the top of the panel. This will show the maps in a different table
Click the phrase “Other Format (TIF)”, for each map, under the column Download and they will download to your computer (DON’T DOWNLOAD NOW).

## Slide 6: AERMAP—Obtaining NED Data
  The data that is downloaded from this site is compressed and can’t be used in AERMAP.
  The procedure needed to uncompress the terrain files is found in the following document:
  This file is located in the …\Presentations\ sub-directory
Go through how you would download but don’t actually download – data is provided in: \>MODL_301\Hands-On\AERMAP\Seamless_DEM\

## Slide 7: Limiting the Search Domain
Two Seamless DEM files were needed to cover the locations of our receptors and sources
Limiting the area that AERMAP has to search reduces run time
We decided to limit the search domain using the following keyword/parameters:
DOMAINXY 476000 4502000 18 506000 4529000 18
This search domain is approximately 10 km larger than the area covering the sources and receptors

## Slide 8: Defining Receptor Locations
Gridded receptors are easier to specify, because only parameters defining the starting point and node spacing are required
Without a graphical user interface (GUI), discrete receptors are more difficult to specify, especially if there are thousands of receptors
In our hands-on exercise we will be using discrete receptors

## Slide 9: Defining Receptor Locations
ANCHORXY 495510 4513680 495510 4513680 18 4

## Slide 10: Running AERMAP
AERMAP control file can be either user named (and therefore must be included on the command line), or use the default name aermap.inp (then only need to type the executable at the comanad line).
For this exercise we will use the user defined name of aermap_1deg.inp
To run AERMAP for this activity double click the .bat file
A command prompt window will open showing the progress of the program.

## Slide 11: AERMAP Output for Input to AERMOD
AERMAP produces several output files
  MC_nested_1deg.dat – This file contains all receptors that include receptor elevation and hc. This file is input to the AERMOD’s .inp file via the INCLUDE keyword.
  MC_src.src – This file contains the elevation for the sources that you could include using the INCLUDE keyword but we will just paste into AERMOD’s .inp file since only 3 sources

## Slide 12: Informational AERMAP Output
AERMAP produces several output files
  AERMAP.OUT: General summary of the run
  MAPDETAIL.OUT: Summary of information regarding each Seamless DEM file based on the results of the checking routines (for debugging problems)
  MAPPARAMS.OUT: Summary of the parameters for each Seamless DEM file, based on the contents of the header record; and documents the adjacency of the files within the application area (for debugging problems)