## Slide 1: BPIPPRM – building Profile Input Program FOR AERMOD/PRIME
Course #MODL301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2
AERMOD Modeling System
Input
Surface Characteristics AERSURFACE
Input
Meteorology AERMINUTE
Input
Terrain data
AERMAP
Input
Building data BPIPPRM
AERMOD
Compute PBL parameters
AERMET
Establish
Meteorology
Profiles
Compute
Concentrations

## Slide 3: Building Downwash
Cavity or
Near Wake
Far Wake
1-hr avg. NAAQS for SO2 and NO2

## Slide 4
Meteorological Wind Tunnel
(1974 – Present)
A controlled laboratory for studying the flow and pollutant dispersion within a simulated atmospheric boundary layer.
Primary research: To support development and evaluation of near-field, dispersion models
Flow around simple block buildings.
(First complete study in EPA tunnel, 1974-75)

## Slide 5
Wind Tunnel Simulations:
Cubical building (plan view) – Source on lee side near ground
Hosker (1979)
Modeling Building Wakes within a Steady-State Framework
1 – min avg
1 – hour avg

## Slide 6: DOWNWASH in AERMOD
Cavity
Far Wake

## Slide 7: DOWNWASH in AERMOD
Cavity
Far Wake

## Slide 8
Wind Tunnel – Neutral Stability
(non-buoyant smoke)
Smoke visualization 1
(to be shown in class)

## Slide 9
Wind Tunnel – Neutral Stability
(non-buoyant smoke)
Smoke visualization 2
(to be shown in class)

## Slide 10
Wind Tunnel – Neutral Stability
(non-buoyant smoke)
Smoke visualization 3
(to be shown in class)

## Slide 11: DOWNWASH in AERMOD
Major effects on plumes that interact with the building wake:
  Streamline suppression or enhancement of plume rise
  Plume material captured in the wake is partitioned between the cavity and far wake.
  Enhanced turbulence in both the near and far wakes (recirculation in the cavity)
  Reduced wind speed (advection downwind)
  Magnitude of effects depends on building size and location of source relative to the building.

## Slide 12: DOWNWASH in AERMOD
The building downwash algorithms incorporated into AERMOD were originally developed in the 1990s by a collaborations between EPRI and EPA.
Plume Rise Model Enhancements (PRIME)
AERMOD / PRIME

## Slide 13: AERMOD / PRIME
Determines the shape and size of the wake depending on the building shape and wind direction.
Considers the position of the stack release relative to the building (i.e. relative to the wake).
As the plume rises in the disturbed flow AERMOD determines if it is influenced by the building wake; if yes, then the model partitions the plume mass into that captured in the cavity (near wake) and the that in the far wake.
Cavity mass is mixed and then re-emitted into the far wake.

## Slide 14: AERMOD / PRIME
There is a distance downwind (~ 15 H) where the flow begins to return to ambient conditions.
Beyond this point, AERMOD estimates concentrations as a weighted sum of the downwash resultant concentrations and concentrations without the building. Therefore, concentrations slowly evolve back toward those in a no-building flow.

## Slide 15
BPIPPRM
(Building Profile Input Program for Prime)
Preprocessor for AERMOD that provides the appropriate building dimensions for each source and wind direction.
BPIPPRM first determines which building or combination of buildings most influences a particular source for each wind direction.
AERMOD’s formulations for wake size and shape are based on rectangular buildings with flow perpendicular to a building side; thus, for each source effected, BPIPPRM must provide an effective rectangular building for each wind direction.

## Slide 16: BPIPPRM
Structure Influence Zone (SIZ)
  The direction-specific region in which nearby structures or buildings have an influence on a particular stack/plume
L = the lesser of the building height and projected width

## Slide 17
1 – hour avg
Wind Tunnel Simulations (plan view)
BPIPPRM
Cubical Building – Perpendicular Flow

## Slide 18
Effect of wind angle on horizontal flow
(wind vectors and streamlines, plan view)
Rectangular building dimensions: H x H x 4H
Streamlines at height of 0.5 H
1:4
Y
60°
30°
0°
Snyder (1993)
FLOW
y
0°
30°
60°

## Slide 19: bpipprm
ACTUAL BUILDING
WIND

## Slide 20: bpipprm
EFFECTIVE BUILDING DIMENSIONS
WIND

## Slide 21
  Current BPIPPRM Effective Building for long narrow buildings may result in unrealistically large building wakes
Building
Current BPIPPRM
Effective
Building
Stack
Known problem with
elongated buildings
WIND

## Slide 22
  There is a proposed adjustment to the effective building in BPIPPRM using the along-wind dimension of the actual building at the source location.
Building
Current BPIPPRM
Effective
Building
Stack
Proposed
Effective
Building
Alpha Option
for elongated buildings
WIND

## Slide 23
Wind Tunnel Flow Vectors and Streamlines
(Effect of wind angle on horizontal flow)
There is an alpha option that accounts for what has been labeled as “sidewash” for these angled cases
1:4
Y
60°
30°
0°
Snyder (1993)
FLOW
y
0°
30°
60°

## Slide 24: AERMOD / PRIME
For complex industrial building arrays, storage tanks, and oil refinery structures, the Agency has allowed the effective building dimensions to be determined from wind tunnel studies.
Courtesy R. Petersen

## Slide 25: AERMOD / PRIME
For complex industrial building arrays, storage tanks, and oil refinery structures, the Agency has allowed the effective building dimensions to be determined from wind tunnel studies
Courtesy R. Petersen
However, ….. There was a case in Region 7 in 2011 where the use of a wind tunnel study was denied by the Model Clearinghouse.

## Slide 26: BPIPPRM
BUILDING: A surface-based structure with three or more vertices
TIER: A “sub-structure” that sits atop a building or another tier
  Tier vertices must be contained within the structure below it
Include each significant tier on a building, with the tier height referenced to the base elevation of the building (i.e., local elevation)
Tier 1
Tier 2
Building

## Slide 27
  BPIPPRM will combine structures if they are “sufficiently close” that their separate wakes can be considered as a single wake.
    “Sufficiently close”—closer than the greater of the two structure’s L (lesser of a structure’s height or projected width)
BPIPPRM
Combining Structures

## Slide 28
Gap between the two structures, for this wind direction, is less than L. The gap will be filled with a structure equal in height to the lower structure
BPIPPRM
L
Wind

## Slide 29
Gap between the two structures is treated as if the gap had been filled with a structure equal in height to the lower structure
BPIPPRM

## Slide 30
AERMOD applies Building Downwash only
to Point Sources
Documentation (BPIPPRM and BPIP)
Good Engineering Practice (GEP) Stack Height
BPIPPRM
Final thoughts:

## Slide 31: Downwash—GEP
Good engineering practice stack height (HGEP)
  HGEP is the stack height above which the effects from building downwash are thought to be insignificant
  HGEP = maximum of
    65 meters
    Hb + 1.5 L (a.k.a. EPA formula height)
      Hb = building height
      L = min(Hb, maximum projected building width)
  For stacks in existence on January 12, 1979, GEP is 2.5 times the height of any nearby influencing structure
  HGEP can also be determined via a wind tunnel study
Cannot give credit for a stack higher than GEP

## Slide 32
END