## Slide 1: BPIPPRM Hands-on
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Develop the required input to run BPIPPRM
Execute the BPIPPRM program
Interpret the results from the BPIPPRIM program
Import the results from BPIPPRIM into the AERMOD program

## Slide 3: Structure Diagram
Tier 1: 180m x 90m x 60m high
Tier 2: 80m x 60m x 100m high
Stack height = 183m
Stack is adjacent to Tier 1 face
*
Stack
N

## Slide 4: BPIPPRM—Hands-on
To develop the BPIPPM Control file you need the following data:
  Model Type: Prime Downwash
  Number of Buildings: 1
  Number of Tiers: 2
  Base Elevation: 0 meters
  Tier 1 coordinates (in meters):
    490992.0 4516280.0
    491034.0 4516200.0
    491195.0 4516281.0
    491153.0 4516361.0
  Tier 1 height: 60 meters
  Tier 2 coordinates (in meters):
    491108.912 4516271.644
    491081.474 4516324.737
    491153.000 4516361.000
    491181.029 4516307.682
  Tier 2 height: 100 meters
  Source Information:
    Source ID: MC12
    Stack elevation: 0 meters
    Stack height: 182.9 meters
    Location: 491020.0 4516237.0

## Slide 5: BPIPPRM—Hands-on Files
The BPIPPRM executable file and control file are the only files needed to complete this hands-on activity. They are in the following directory:
\>MODL_301\Hands-On\BPIPPRM\
  Bpipprm.exe: BPIPPRM program executable file
  MC_bpipprm.inp: control file

## Slide 6: BPIPPRM Example Input Control File
‘Martins Creek – MODL 301 Hands-On'  Title
‘P'  MODEL TYPE: USE ‘P’ FOR AERMOD
'Meters' 1.000  INPUT UNITS, CONVERSION FACTOR TO METERS
'UTMN' 0.0000  UTM FLAG, PLANT NORTH ANGLE
1  NUMBER OF BUILDINGS
‘BLDG1’ 2 0.000  FIRST BLDG NAME, NUMBER OF TIERS,
& BASE ELEVATION
4 60.000  NUMBER OF CORNERS, TIER HEIGHT
490992.0 4516280.0  X AND Y-COORDINATES OF CORNERS
491034.0 4546200.0 FOR FIRST BUILDING TIER
491195.0 4516281.0
491153.0 4516361.0
4 100.0
491108.9 4516271.6
491081.5 4516324.7
491153.0 4516307.7
491181.029 4516307.682
1  NUMBER OF STACKS
STACKID STACK ELEV. STACK HEIGHT STACK X-COORD STACK Y-COORD
‘MC12' 0.000 182.9 491020.0 4516237.0
Tier 1
Tier 2
Tier 2 Height
Tier 1 Height

## Slide 7: BPIPPRM—Output
buildwid

## Slide 8: Incorporating Results into AERMOD
Only one method
  Copy paste results from output_file into the AERMOD control file or a properly formatted file to include with the INCLUDED keyword
  The necessary records in the ouput_file begin after the processing information
  They meet all the AERMOD requirements except one
    In the output_file, the records start in column 6 with the pathway SO, whereas AERMOD requires that SO appear in the first two columns
    1234567890123456
    SO BUILDHGT Stk100 40.00 40.00 40.00 40.00 40.00 40.00
    SO BUILDHGT Stk100 40.00 40.00 40.00 40.00 40.00 40.00
    SO BUILDHGT Stk100 40.00 40.00 40.00 40.00 40.00 0.00
    SO BUILDHGT Stk100 40.00 40.00 40.00 40.00 40.00 40.00
    SO BUILDHGT Stk100 40.00 40.00 40.00 40.00 40.00 40.00
    SO BUILDHGT Stk100 40.00 40.00 40.00 40.00 40.00 0.00
    SO BUILDWID Stk100 66.61 81.19 93.30 102.58 108.74 111.60
    Remove the extra columns; otherwise AERMOD will generate error messages

## Slide 9: Running BPIPPRM
It’s best run in a batch file
Using a batch file
  Create a text file with the extension .bat
  Batch file should contain the following Line:
  bpipprm control_file output_file summary_file

## Slide 10: Running BPIPPRM
Navigate to the \>MODL_301\Hands-On\BPIPPRM\ directory
Double click on the .bat file
A command prompt window will open showing the progress of the program

## Slide 11: BPIPPRM—Example Output (ONE VALUE FOR EACH OF 36 WIND DIRECTIONS
SO BUILDHGT MC12 100.00 100.00 100.00 100.00 100.00 100.00
SO BUILDHGT MC12 100.00 100.00 100.00 60.00 60.00 60.00
SO BUILDHGT MC12 60.00 60.00 60.00 60.00 60.00 60.00
SO BUILDHGT MC12 100.00 100.00 100.00 100.00 100.00 100.00
SO BUILDHGT MC12 100.00 100.00 100.00 60.00 60.00 60.00
SO BUILDHGT MC12 60.00 60.00 60.00 60.00 60.00 60.00
SO BUILDWID MC12 91.14 91.14 91.14 87.23 77.06 64.55
SO BUILDWID MC12 68.89 80.34 89.36 179.22 191.99 198.93
SO BUILDWID MC12 199.82 194.65 183.56 191.10 200.09 203.00
SO BUILDWID MC12 91.14 91.14 91.14 87.23 77.06 64.55
SO BUILDWID MC12 68.89 80.34 89.36 179.22 191.99 198.93
SO BUILDWID MC12 199.82 194.65 183.56 191.10 200.09 203.00
SO BUILDLEN MC12 95.65 99.05 99.43 96.79 91.21 82.86
SO BUILDLEN MC12 87.72 95.08 99.56 199.74 190.42 175.30
SO BUILDLEN MC12 154.86 129.72 100.63 110.59 137.89 161.00
SO BUILDLEN MC12 95.65 99.05 99.43 96.79 91.21 82.86
SO BUILDLEN MC12 87.72 95.08 99.56 199.74 190.42 175.30
SO BUILDLEN MC12 154.86 129.72 100.63 110.59 137.89 161.00
SO XBADJ MC12 49.56 62.96 74.46 83.69 90.38 94.32
SO XBADJ MC12 87.77 75.78 61.47 -35.04 -41.02 -45.75
SO XBADJ MC12 -49.09 -50.94 -51.24 -71.03 -99.02 -124.00
SO XBADJ MC12 -145.21 -162.01 -173.89 -180.48 -181.59 -177.18
SO XBADJ MC12 -175.49 -170.86 -161.03 -164.70 -149.40 -129.55
SO XBADJ MC12 -105.78 -78.78 -49.39 -39.56 -38.87 -37.00
SO YBADJ MC12 -95.81 -77.45 -56.74 -34.31 -10.83 12.97
SO YBADJ MC12 36.59 58.85 79.32 55.60 66.02 74.42
SO YBADJ MC12 80.57 84.27 85.40 83.95 79.94 73.50
SO YBADJ MC12 95.81 77.45 56.74 34.31 10.83 -12.97
SO YBADJ MC12 -36.59 -58.85 -79.32 -55.60 -66.02 -74.42
SO YBADJ MC12 -80.57 -84.27 -85.40 -83.95 -79.94 -73.50