## Slide 1: AERMOD Setup
Course MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Explain AERMOD input requirements and output options
Develop a complete AERMOD control file without the use of a graphical user interface (GUI)

## Slide 3: Overview
This lesson introduces:
Source types processed by AERMOD
AERMOD data input requirements
  Meteorology, source parameters, emissions, building data, receptor data
Modeling options
Control file format and structure
  Pathways and keywords

## Slide 4
AERSURFACE
AERMINUTE
DEM DATA
BPIPPRM
LAND USE, CANOPY & IMPERVIOUS SURFACE DATA
1 MINUTE ASOS DATA

## Slide 5: Source Types
AERMOD Source Types:
Point
Area
Volume
Line
RLINE—Now a regulatory option
RLINEXT—Alpha option
Buoyant Line
Open Pit
Offshore Release – CORE now in AERMET

## Slide 6: Source Types
Point/stationary—stacks and isolated vents
  Point (POINT)
  Capped point (POINTCAP)
  Horizontal (POINTHOR)

## Slide 7: Source Types
Area—low-level and ground releases with no plume rise such as lagoons, storage piles, and mine tailings
  Rectangular (AREA)
  Irregular polygon (AREAPOLY)
  Circular (AREACIRC)

## Slide 8: Source Types
Volume—building roof monitors; windows, and other openings considered as a single source
Line—roadways, rail lines
Open Pit—surface mining sites
Buoyant Line – e,g., Aluminum smelter roof monitor emissions
Off-Shore Releases:
  Core now in AERMOD
  Downwash from off-shore platforms
  Impact on-shore - TIBL

## Slide 9: Data Input
Meteorology – from AERMET
  Boundary layer parameters calculated by AERMET (.sfc)
  Profile of atmospheric variables (.pfl)

## Slide 10: Data Input
Source Characteristics
  Source ID
  Source type
  Location (UTM or user-defined (local) coordinates)
    X, Y required; Z optional
    Line source defined by two end points
    AREAPOLY
      AREAVERT to define the vertices

## Slide 11: Data Input
Emission Parameters
  Emission Rate (Units are source type dependent)
    POINT, VOLUME: grams/second
    AREA, AREAPOLY, AREACIRC: grams/second/square meter
    OPENPIT: grams/second/square meter
    LINE: grams/second/square meter
    RLINE: grams/second/square meter
    BOUYANT LINE: grams/second/line
  For point sources: Ts, vs and IDs
  For line sources: Line width
  Release height
  HOUREMIS: file of hourly emission rates

## Slide 12: Data Input
Building Data
  As developed by BPIPPRM
  36 values per keyword (BUILDLEN, BUILDHGT, BUILDWID, XBADJ, YBADJ) usually 6 values per row
  Associated with source through the source ID

## Slide 13: Data Input
Receptor Data
  Gridded (Cartesian, polar)
  Discrete (Cartesian, polar)
  Can be developed from AERMAP
  Can use the INCLUDED keyword to specify a file to read the receptor data rather than explicitly adding the receptors to the control files
Terrain Data
  Sources: Base elevation only
  Receptors: elevation and hill height scale from AERMAP

## Slide 14: Modeling Options
Regulatory Modeling Options (MODELOPT)
  DEFAULT applies regulatory modeling options and overrides all non-DFAULT options (if any are specified)
  CONC to calculate concentration

## Slide 15: Modeling Options
Non-regulatory Modeling Options
  ALPHA: Research/experimental options provided for review and evaluation by the user community (e.g., LOW_WIND and PSDCREDIT)
  BETA: Options that have been vetted through the scientific community – awaiting proposal and promulgation (none included in AERMOD Version 24142 )

## Slide 16: New Regulatory Modeling Options That Were Beta Options prior to ver. 24142
RLINE:
  Simulates near-surface releases by numerically integrating point source emissions.
  Accounts for terrain elevation variations
  Includes vertical and lateral dispersion rates, based on field and wind tunnel studies, and horizontal meander.
COARE (in AERMET):
  Produces meteorology needed to model off-shore sources
  Processes observed or prognostic overwater data
  Replaces the need for the standalone AERCOARE processor

## Slide 17: New Regulatory Modeling Options That Were Beta Options prior to ver. 24142
GSRM:
  NO2 screening option
  Address photolytic conversion of NO2 to nitrogen oxide (NO)
  Address the time-of-travel necessary for NOX plumes to convert the NO portion of a plume to NO2 via titration and entrainment of ambient ozone

## Slide 18: Modeling Options
Pollutant IDs (POLLUTID)
  NO2
  SO2
  PM25
Pollutant Averaging times (AVERTIME)
  1, 2, 3, 4, 6, 8, 12, and/or 24 hours
  MONTH, ANNUAL, PERIOD

## Slide 19: Modeling for the NAAQS: SO2
1-hour standard: 99th percentile of the 1-hour daily maximum concentrations, averaged over 3 years
  Primary standard
  75 ppb or about 196 µg/m3
3-hour standard: not to be exceeded more than once per year
  High 2nd High
  A secondary standard
  0.5 ppm or about 1,309 µg/m3

## Slide 20: NAAQS Compliance: 1-Hour SO2 Standard
“Probabilistic”—percentile based on an average over several years. That is, with the predicted data for a given receptor over a given modeled year, construct a probability density function from which you choose the 99th percentile. This value may not be any specific value that you predict.
The modeled design value is based on the 99th percentile of the maximum daily 1-hour values averaged across:
  5 years if NWS data
  1-hour value for one year if site-specific data
  3 years if prognostic data
The fourth-highest of the daily maximum 1-hour values across a year is an unbiased surrogate for the 99th percentile

## Slide 21: Procedure for Finding the 99th Percentile Averaged over 3 yrs.
Find the max 1 hr. conc. For each day at each receptor
Then fine the 99th percentile conc, from the set of 365 concs, at each receptor – i.e. ≈ the 4th high at each receptor
Do this for each of 3 yrs. Which will result in 3 - 4th highs for each receptor.
Average the 3 numbers at each receptor
The design value is then the highest of the averages from across the receptor network

## Slide 22: Control File Structure
AERMOD uses a pathway/keyword structure to construct the analysis
Pathways—2-character
  CO: control—titles, modeling options, pollutant IDs, averaging times
  SO: source—source types, locations, and parameters/emissions, building parameters for downwash, and source groups
  RE: receptors—discrete and gridded receptor locations and elevations
  ME: meteorology—AERMET-generated input files
  OU: output—options for printing AERMOD output
  EV: event processing—analysis of source contributions

## Slide 23: Control Pathway Keywords
CO
  TITLE1: provides a way to identify the model run in the output file(s) (mandatory)
    TITLE1 title1
  MODELOPT: job controls and dispersion options (mandatory)
    MODELOPT list_of_model_options
  AVERTIME: averaging time(s) to process (mandatory)
  POLLUTID: identifies the pollutant to be modeled (mandatory)

## Slide 24: Control Pathway Keywords
CO
  RUNORNOT: instructs AERMOD to run or only check the processing setup without running (mandatory)
  DEBUGOPT: Allows the user to request detailed files of intermediate calculations. Essential to fully understand a concentration prediction e.g., understanding the contribution from each of the 5 plumes (Run only for a couple hour/receptor)

## Slide 25: Source Pathway Keywords
SO
  LOCATION: source type and location by source ID (mandatory)
    LOCATION SrcID Srctyp Xs Ys (Zs)
      Elevation (Zs) is optional

## Slide 26: Source Pathway Keywords
SO
  SRCPARAM: source characteristics – most source parameters are Type Dependent
  For a Point Source:
    SRCPARAM SrcID Emis Hgt Stktmp Stkvel Stkdiat
      SrcID: unique source identifier
      Emis: emission rate
      Hgt: release height above group
      Stktmp: stack exit gas temp
      Stkvel: stack exit gas velocity
      Stkdiat: inside stack diameter

## Slide 27: Source Pathway Keywords
SO
  Keywords and their associated parameters for Downwash (for each source):
    BUILDHG SrcID or SrcRange Dsbh(i), i=1,36 building heights
    BUILDWID SrcID or SrcRange Dsbw(i), i=1,36 building widths
    BUILDLEN SrcID or SrcRange Dsbl(i), i=1,36 building lengths
    XBADJ SrcID or SrcRange Xbadj(i), i=1,36 along-wind distances
    YBADJ SrcID or SrcRange Ybadj(i), i=1,36 cross-wind distances
  INCLUDED: include data from a separate file (optional)
    INCLUDED SrcIncludeFile
  SRCGROUP: groups sources (mandatory)
    SRCGROUP SrcGrpID SrcID's SrcRange's

## Slide 28: Receptor Pathway Keywords
RE GRIDCART
  gridded locations referenced to a Cartesian coordinate system
    Netid STA
      XYINC Xinit Xnum Xdelta Yinit Ynum Ydelta
    or
      XPNTS Gridx1 Gridx2 Gridx3 .... GridxN, and
      YPNTS Gridy1 Gridy2 Gridy3 .... GridyN
    ______________________________________________________________________________
      ELEV Row Zelev1 Zelev2 Zelev3 ... ZelevN
      HILL Row Zhill1 Zhill2 Zhill3 ... ZhillN
      FLAG Row Zflag1 Zflag2 Zflag3 ... ZflagN
      END

## Slide 29: Receptor Pathway Keywords
RE GRIDPOLR
  gridded locations referenced to a polar coordinate system
    Netid STA
    ORIG Xinit Yinit OR
        ORIG SrcID
    DIST Ring1 ... RingN
    DDIR Dir1 … DirN OR
        GDIR Dirnum Dirini Dirinc
    ___________________________________________________________________________________
    ELEV Dir Zelev1 ... ZelevN
    HILL Dir Zhill1 ... ZhillN
    FLAG Dir Zflag1 ... ZflagN
    END

## Slide 30: Receptor Pathway Keywords
RE DISCCART
  discrete locations referenced to a Cartesian system
    DISCCART Xcoord Ycoord (Zelev) (Zhill) (Zflag)
RE DISCPOLR
  discrete locations referenced to a polar network
    DISCPOLR Srcid Dist Direct (Zelev) (Zhill) (Zflag)
RE INCLUDED
  include data from a separate file
    INCLUDED RecIncludeFile

## Slide 31: Meteorology Pathway Keywords
ME
  SURFFILE: file with surface-based parameters from AERMET (mandatory) – located in AERMET directory
    SURFFILE Sfcfil
  PROFFILE: file with the profiles of atmospheric variables from AERMET (mandatory) – located in AERMET directory
    PROFFILE Prffil
  `

## Slide 32: Meteorology Pathway Keywords
ME
  SURFDATA: NWS surface meteorology station information (mandatory)
    SURFDATA Stanum Year (Name) (Xcoord Ycoord)
  UAIRDATA: upper air station information (mandatory)
    PROFDATA Stanum Year (Name) (Xcoord Ycoord)
  SITEDATA: surface meteorology station information (optional)
    SITEDATA Stanum Year (Name) (Xcoord Ycoord)

## Slide 33: Meteorology Pathway Keywords
ME
  STARTEND: specifies the start and end date to process; the default is to process all meteorological data (optional)
    STARTEND Strtyr Strtmn Strtdy (Strthr) Endyr Endmn Enddy (Endhr)
  PROFBASE: base elevation to use for computations of the potential temperature profile (in meters) (optional)
    PROFBASE BaseElev (Units)

## Slide 34: Output Pathway Keywords
OU
  RECTABLE: provides the highest, second highest and third highest values, etc., by receptor.(optional) – is found in the AERMOD.OUT file
    RECTABLE Aveper List of Highes
  MAXTABLE: provides a table of the overall maximum “n” number of values (optional) – is found in the AERMOD.OUT file
    MAXTABLE Aveper Maxnum
  SUMMFILE: a significantly shorter version of the AERMOD.OUT file except the values at all receptors for all source groups is not output
    SUMMFILE SummFilnam
  PLOTFILE: output file based on the averaging period and high value useful for plotting results (optional)
    PLOTFILE Aveper GrpID Hivalu Filnam (Funit)