## Slide 1: AERMOD Hands-On
Course : MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Run AERMOD on the example case
Review the Martins Creek output

## Slide 3: AERMOD Hands-on—Files
AERMOD program executable and 1-year hourly emissions from Martins Creek can be found in:
\>MODL_301\Hands-on\AERMOD\
  AERMOD_ 23132.EXE: AERMOD program executable file
  MARTIN.EMI: Martins Creek hourly emissions file
Two SO2 Scenarios: 1) 1-yr On-Site; 2) 5-yrs. NWS
Four modeling runs - 2 for each scenario:
  3-hour, 24-hour, Annual SO2 w/1-year site-specific and 1-min ASOS for substituting missing On-Site data
  1-hour SO2 w/1-year site-specific and 1-min ASOS for substituting missing On-Site data
  1-hour SO2 w/5 years 1-min ASOS data (single run)
  3-hour, 24-hour, Annual SO2 w/5 years 1-min ASOS data only (separate run for each year)
Notes: If you get stuck go to Completed_Run subdirectory
The program executables and the Martins Creek hourly emissions file are in \APTI423\Hands-on\AERMOD.
There are two executables one for a 32 bit machine and the other for a 64 bit machine
The meteorological data (output from AERMET) are in the folder in which you ran AERMET.
Four different scenarios will be modeled for the SO2 NAAQS for various averaging times using the 1 year of site-specific data supplemented with National Weather Service (NWS) data and 5 years of NWS data.
In general, we will model 1-hour, 3-hour, 24-hour, and annual SO2. Note that the 24-hour and annual SO2 standards were revoked in 2010 and usually no longer apply. However, some states might not have updated their regulations and might require modeling for these averaging periods. This was recently the case for Alaska. Also note the 3-hour standard is a secondary standard and might not require modeling. Regardless, we will look at these averaging periods as they relate to SO2 for demonstration purposes.
We will model each of these four averaging times using the 1 year of site-specific data (supplemented with NWS data) we previously processed with AERMET and using the 5 years of NWS data (without site-specific data) previously processed with AERMET. As is summarized on this slide, this will require four modeling scenarios to get the correct form of the design value from AERMOD for each of the averaging times.
The 5-year model runs take significant time to complete, so depending on available class time, it might be necessary to discuss results using the provided reference output files and leave it to you to run these at your leisure.

## Slide 4: AERMOD Hands-on—Files
Meteorology:
Surface and profile files are in: …\Hands-On\ AERMET \1-yr_Onsite\ and in …\Hands-On\ AERMET \5-yr_NWS\
Terrain/Receptors:
Receptor and source files are in …\Hands-On\AERMAP\
Building Data:
Data for pasting in AERMOD’s .inp file are in …\Hands-On\BPIPRM\
Hourly emissions for Scenario 1 (File name MARTIN.EMI):
Data is in …\Hands-On\AERMOD\
Notes: If you get stuck go to Completed_Run subdirectory
The program executables and the Martins Creek hourly emissions file are in \APTI423\Hands-on\AERMOD.
There are two executables one for a 32 bit machine and the other for a 64 bit machine
The meteorological data (output from AERMET) are in the folder in which you ran AERMET.
Four different scenarios will be modeled for the SO2 NAAQS for various averaging times using the 1 year of site-specific data supplemented with National Weather Service (NWS) data and 5 years of NWS data.
In general, we will model 1-hour, 3-hour, 24-hour, and annual SO2. Note that the 24-hour and annual SO2 standards were revoked in 2010 and usually no longer apply. However, some states might not have updated their regulations and might require modeling for these averaging periods. This was recently the case for Alaska. Also note the 3-hour standard is a secondary standard and might not require modeling. Regardless, we will look at these averaging periods as they relate to SO2 for demonstration purposes.
We will model each of these four averaging times using the 1 year of site-specific data (supplemented with NWS data) we previously processed with AERMET and using the 5 years of NWS data (without site-specific data) previously processed with AERMET. As is summarized on this slide, this will require four modeling scenarios to get the correct form of the design value from AERMOD for each of the averaging times.
The 5-year model runs take significant time to complete, so depending on available class time, it might be necessary to discuss results using the provided reference output files and leave it to you to run these at your leisure.

## Slide 5: AERMOD Hands-on—Files SO2
  …\1-yr_3-24hr-Ann_Site_Specific\
  AERMOD.INP
  RunMC.bat
  …\1-yr_1hr_Site_Specific\
  AERMOD.INP
  RunMC.bat
  …\5-yr_3-24hr_Ann_NWS\
  AERMOD_08.INP --- AERMOD_12.INP
  RunMC.bat
  …\5-yr_1hr_NWS\
  MCR_AERMOD.INP
  RunMC.bat
Notes: Templates of the control files for the four scenarios are in the four different subfolders beneath the APTI423\Hands-on\AERMOD\ directory, as shown here. For the most part, the control files are named identically (MCR_AERMOD.INP). The exception is the control files for the combined 3-hour, 24-hour, and annual model runs using the 5 years of NWS data (3-24-Ann_SO2_5-yr_NWS). For this scenario, each year should be modeled separately, and a year indicator is included in the filename.
Model results presented later in the hands-on exercises were obtained using completed control files found in the Complete Run subfolders for each scenario.

## Slide 6: SO2 standards
Averaging Time | Standard (µg/m3) | Form of the Standard
Annual Revoked | 20 | Annual arithmetic average (highest)
24-hour Revoked | 91 | Not to be exceeded more than once per year (H2H)
3-hour Secondary | 1309 | Not to be exceeded more than once per year (H2H)
1-hour | 196 | 3-year average of the annual 99th percentile of 1-hour daily maximum concentrations
Notes: As mentioned previously, the annual and 24-hour SO2 standards were revoked in 2010 and the 1-hour SO2 standard was added. The 3-hour standard is a secondary standard. We will still model each of these for demonstration purposes.
Notice the form of the annual standard. It is the highest annual arithmetic average. When modeling for a single year, the value that gets compared to the standard to determine compliance is the highest of the annual averages across all receptors. When modeling with 5 years of NWS data, it is the highest annual average across all receptors and years. It is not the 5-year mean of the highest annual average from each year (as with annual PM2.5).
The 3-hour and 24-hour standards are not to be exceeded more than once per year. Therefore, when modeling for a single year, the value that gets compared to the standard to determine compliance is the H2H 3-hour and H2H 24-hour average, respectively. When modeling 5 years, it is the maximum of the H2H value from each of the 5 years.
The 1-hour SO2 standard does not follow the deterministic H2H/not to be exceeded more than once per year. As seen on the slide, it is based on a 3-year average of the annual 99th percentile of the 1-hour daily maximum.
Although the 1-hour standard is based on a 3-year average, only 1 year of site-specific data is required. However, if more than one year is available, it should be used. Only complete years should be used to avoid any seasonal bias that could be introduced by using a fraction of an additional year. In this example, the site-specific data were from May 1, 2011–May 19, 2012. We did not process May 2012 through AERMET and AERMOD to avoid this situation. If site-specific data are not available and modeling is performed with NWS data, the form of the standard does not preclude the use of a minimum of 5 years of NWS data. Five years of NWS data are still required per Appendix W.

## Slide 7: Control File parameters Scenario 1 1-Year Site-specific; 3-Hour, 24-Hour, Annual
Model options: Default regulatory options, concentrations only
Averaging times: 3, 24, annual (run #1)
Averaging times: 1 (run #2)
Pollutant: SO2
Elevation units: Meters
Point sources:
Hourly emissions: MARTIN.EMI, apply to all point sources
Source groups: All sources as one single source group
ID | X | Y | Z | Emission Rate | Stack Height | Exit Temp | Exit Velocity | Inside Diam
 | meters | meters | meters | grams/ second | meters | K | meters/ second | meters
MC12 | 491020 | 4516237 | 71.53 | 0.0 | 182.9 | 0.0 | 0.0 | 5.3
ED2 | 493350 | 4528370 | 97.62 | 0.0 | 121.9 | 0.0 | 0.0 | 3.6
HL2 | 494050 | 4521040 | 97.40 | 0.0 | 59.4 | 0.0 | 0.0 | 2.7
Notes: Does the pollutant matter in this scenario? No; you could specify “Other,” because the SO2 standards for the averaging periods are deterministic.
Why are several parameters set to zero? We will be using an hourly emissions file that contains this information.
Do we need to set these parameters to zero? No, you can enter non-zero values, but the emissions file will override them.

## Slide 8: Control File Parameters—cont’d 1-Year Site-specific; 3-Hour, 24-Hour, Annual
Receptors: MC_nested_1deg.rec in the AERMAP folder
Meteorology: Files generated by AERMET, free format
SURFDATA: Station ID: 14737
UAIRDATA: Station ID: 54775
Profile base: 73.2 meters
Start date: May 1, 2011
End date: April 30, 2012
Recommended output:
  RECTABLE for first high and second high, 3- and 24-hour averages
  PLOTFILEs
  SUMMFILE
Notes: Shown here are more of the input parameters needed to complete the AERMOD control file.
For the output, enter the file types of your choosing. We have recommended a few here. There are place holders in the template as well, but the choice is yours.

## Slide 9: Running AERMOD Scenario 1: Run 1 1-Year Site-specific: 3-Hour, 24-Hour, Annual
To run the 1-year site-specific multi-average SO2 scenario:
Navigate to the …\Hands-on\AERMOD\1-yr_3-24hr-Ann_Site_Specific\ directory
A .bat file has been created that identifies where the AERMOD executable is located
Run AERMOD
Identify:
  H2H 3hr Ave
  H2H 24hr Ave
  Annual Ave
Notes: AERMOD accepts either the default AERMOD.INP (not case sensitive in a Windows environment) or a user-defined name. Although AERMOD recognizes AERMOD.INP as default, it is recommended that if you do not explicitly use a unique name when running AERMOD, you should save the original control file to some more meaningful unique filename—there is less risk of accidentally overwriting an existing control file.
Open a command prompt and set the working directory to the directory where the control file template is located: APTI423\Hands-on\AERMOD\3-24-Ann_SO2_1-yr_Site
Edit the template and copy the control file to AERMOD.INP or as uniquely defined name.
Start AERMOD at the command prompt by typing: ..\aermod or ..\aermod [unique name].
The 1-year modeling scenarios take from 5–10 minutes to run depending on the speed of your machine. You should see evidence that AERMOD is running, displaying the day and year currently processing (next slide).
If it looks like AERMOD attempted to run and failed with an error message, open “aermod.out” in a text editor, scroll to the bottom to see any error messages generated, and try to determine what caused the error.
Alternative to opening a command prompt: copy the executable to the folder APTI423\Hands-on\AERMOD\3-24-Ann_SO2_1-yr_Site and double-click on the executable you just copied.

## Slide 10: 1-Year Site-specific Results for SO2
Averaging Time | Standard (µg/m3) | Value (µg/m3)
Annual | 20 Annual arithmetic average (highest) | 
24-hour | 91 Not to be exceeded more than once per year (H2H) | 
3-hour | 1309 Not to be exceeded more than once per year (H2H) | 
1-hour | 196 3-year average of the annual 99th percentile of 1-hour daily maximum concentrations | ?
Notes: We now have modeled design values to compare to the 3-hour, 24-hour, and annual SO2 standards based on 1 year of site-specific data supplemented with NWS surface observations.
Next, we look more closely at the 1-hour standard.

## Slide 11: 1-Year Site-specific Results for SO2
Averaging Time | Standard (µg/m3) | Value (µg/m3)
Annual | 20 Annual arithmetic average (highest) | 9.5
24-hour | 91 Not to be exceeded more than once per year (H2H) | 101
3-hour | 1309 Not to be exceeded more than once per year (H2H) | 474
1-hour | 196 3-year average of the annual 99th percentile of 1-hour daily maximum concentrations | ?
Notes: We now have modeled design values to compare to the 3-hour, 24-hour, and annual SO2 standards based on 1 year of site-specific data supplemented with NWS surface observations.
Next, we look more closely at the 1-hour standard.

## Slide 12: Running AERMOD Scenario 1: Run 2 1-Year Site-specific: 1-Hour SO2
To run the 1-year site-specific scenario for 1-hour SO2:
Navigate to the where the control file is located: ….\Hands-on\AERMOD\ 1-yr_1hr_Site_Specific\
A .bat file has been created that identifies where the AERMOD executable is located
Run AERMOD
Identify the high 4th high
Notes: Open a command prompt and set the working directory to the directory where the control file template is located: APTI423\Hands-on\AERMOD\1hr_SO2_1-yr_Site.
Copy the control file to AERMOD.INP or a uniquely defined name.
Start AERMOD at the command prompt by typing: ..\aermod or ..\aermod [unique name.
The 1-year modeling scenarios take a few minutes to run.
If it looks like AERMOD attempted to run and failed with an error message, open “aermod.out” in a text editor, scroll to the bottom to see any error messages generated, and try to determine what caused the error.

## Slide 13: 1-Year Site-specific Results
Averaging Time | Standard (µg/m3) | Value (µg/m3)
Annual | 20 Annual arithmetic average (highest) | 
24-hour | 91 Not to be exceeded more than once per year (H2H) | 
3-hour | 1309 Not to be exceeded more than once per year (H2H) | 
1-hour | 196 3-year average of the annual 99th percentile of 1-hour daily maximum concentrations | ?
Notes: Now, we can complete our table of modeled values to compare to the SO2 NAAQS. The values in red exceed the SO2 NAAQS.
NOTE: Do not forget about background concentrations! In a modeling demonstration to support an air permit, you will typically need to add background concentrations, and include all “nearby” sources to your modeling analysis to get a final design concentration to compare to the NAAQS. Check with the permitting authority to obtain appropriate background concentrations, an inventory of “nearby” sources, and preferences for AERMOD setup. For demonstration purposes, we have ignored “nearby” sources and background concentrations. AERMOD has numerous options for applying varying background concentrations within the model (refer to the User’s Guide or Addendum), or if applying the same value for all hours modeled, the value can be added manually to the modeled concentration.
Next, we will look at modeling for the same standards using 5 years of NWS meteorological data without the use of site-specific data. This time we will start with the 1-hour SO2.

## Slide 14: 1-Year Site-specific Results
Averaging Time | Standard (µg/m3) | Value (µg/m3)
Annual | 20 Annual arithmetic average (highest) | 9.5
24-hour | 91 Not to be exceeded more than once per year (H2H) | 101
3-hour | 1309 Not to be exceeded more than once per year (H2H) | 474
1-hour | 196 3-year average of the annual 99th percentile of 1-hour daily maximum concentrations | 683
Notes: Now, we can complete our table of modeled values to compare to the SO2 NAAQS. The values in red exceed the SO2 NAAQS.
NOTE: Do not forget about background concentrations! In a modeling demonstration to support an air permit, you will typically need to add background concentrations, and include all “nearby” sources to your modeling analysis to get a final design concentration to compare to the NAAQS. Check with the permitting authority to obtain appropriate background concentrations, an inventory of “nearby” sources, and preferences for AERMOD setup. For demonstration purposes, we have ignored “nearby” sources and background concentrations. AERMOD has numerous options for applying varying background concentrations within the model (refer to the User’s Guide or Addendum), or if applying the same value for all hours modeled, the value can be added manually to the modeled concentration.
Next, we will look at modeling for the same standards using 5 years of NWS meteorological data without the use of site-specific data. This time we will start with the 1-hour SO2.

## Slide 15
Notes: This figure presents concentration isopleths of the 4th highest predicted 1 hr. concentration based on 1 yr. of site specific meteorological data. The concentrations in this figure are not coincident in time since the 4th highest 1 hr. concentration at each receptor would likely have occurred at different times through the year.
The red areas have concentrations above the standard while the green areas are below the standard.

## Slide 19: Modeling for the 1-Hour SO2 Standard Scenario 2: Run 3 5 Years, NWS Data Only
The following notes apply to this scenario
  AVERTIME must be 1 hour with no other averaging times specified
  The RECTABLE must include “4” or “4th” or “fourth”—this will calculate the first highest of the 5-year average of the maximum fourth highest maximum daily 1-hour value
  The POLLUTID is SO2
  If the STARTEND keyword is used, be sure the full 5 years is specified
  Adjust the starting year on the SURFDATA and UAIRDATA keywords as needed
Appendix W requires use of 5 years of NWS meteorological data
Notes: It is important to remember, for AERMOD to compute a 1-hour SO2 design value consistent with the form of the NAAQS, you must model the 1-hour by itself without specifying any other averaging periods with the AVERTIME keyword.
The pollutant ID must be specified as SO2.
In addition, you must tell AERMOD to use the fourth highest maximum daily 1-hour value (H4H) by specifying 4, 4th, or fourth on the RECTABLE keyword in the OU (Output) pathway. AERMOD will then output the highest of the 5-year average of the fourth highest maximum daily 1-hour values.

## Slide 20: Control File parameters 5-Year NWS Data only; 1-Hour
Model options: Default regulatory options, concentrations only
Averaging time: 1
Pollutant: SO2
Elevation units: Meters
Point sources:
Source groups: All, NC12, ED2, HL2
ID | X | Y | Z | Emission Rate | Stack Height | Exit Temp | Exit Velocity | Inside Diam
 | meters | meters | meters | grams/ second | meters | K | meters/ second | meters
MC12 | 491020 | 4516237 | 71.53 | 500 | 182.9 | 400 | 20.0 | 5.3
ED2 | 493350 | 4528370 | 97.62 | 400 | 121.9 | 400 | 15.0 | 3.6
HL2 | 494050 | 4521040 | 97.40 | 25 | 59.4 | 400 | 7.0 | 2.7
Notes: Does the pollutant matter in this scenario? Yes, because we are modeling the 1-hour SO2.

## Slide 21: Control File Parameters—cont’d 5-Year NWS Data only; 1-Hour
Receptors: MC_nested_1deg.rec
Meteorology: Files generated by AERMET, free format
SURFDATA: Station ID 14737
UAIRDATA: Station ID 54775
Profile base: 73.2 meters
Start date: January 1, 2008
End date: December 31, 2012
Recommended output:
  RECTABLE that includes the fourth highest
  PLOTFILEs
  SUMMFILE
  MAXDCONT
  MAXTABLE
Notes: Shown here are more of the input parameters needed to complete the AERMOD control file.

## Slide 22: Running AERMOD Scenario 2: Run 3 5-Year NWS: 1-Hour so2
By now, you should be able to run AERMOD for this scenario without instruction
The control file and the .bat file are located in:
  ….\Hands-on\AERMOD\ 5-yr_1hr_NWS\
  Run AERMOD
  Identify the 4th highest in the 5 yr period for comparison with NAAQS
Notes: To run AERMOD for the 1-hour SO2, 5-year scenario, follow the same steps used for the previous AERMOD runs. This run combines all 5 years into a single run so there is only one control file.
The 5-year simulation should take between 30–45 minutes depending on the speed of your machine.

## Slide 23: 3-Hour, 24-Hour and Annual SO2 Standard 5 Years, NWS Data Only
Based on the form of the standards, we can combine all three averaging periods
However, we will need to run each year separately
Recall:
  3-hour: Not to be exceeded more than once per year
    Get 3-hour H2H each year
    Find max value from the 5 yearly values
  24-hour:
    Same as procedure as 3-hour but with 24-hour H2H
  Annual: Highest annual arithmetic average
    Get max annual H1H each year
    Find max value from the 5 yearly values
Notes: Now let’s look at the 3-hour, 24-hour, and annual averages using 5 years of NWS data.
Like how we modeled for the 3-hour, 24-hour, and annual standard using a single year of site-specific meteorological data, we can specify all three averaging periods in the control file when using 5 years of NWS data. However, there is a significant difference in how we will set up AERMOD for this scenario. Rather than running all 5 years in a single simulation as we just did with the 1-hour SO2 standard, we will need to run each of the 5 years separately for the 3-hour, 24-hour, and annual standards.
Recall that the 3-hour and 24-hour standards are not to be exceeded more than once per year. Therefore, we need to get the H2H value for each year separately. Of those five values we need to identify the maximum and compare it to the standard. The annual standard is similar, but different in that it cannot be exceeded even once during the 5 years. Therefore, we need to get the H1H annual average for each year separately. Of those five values, we need to identify the maximum value and compare it to the annual standard.
Why can we NOT run all 5 years in a single AERMOD run? The answer for the annual standard is more straightforward, so we will consider the annual average first. When you specify ANNUAL on the AVERTIME keyword when running multiple years in a single simulation, you might expect that AERMOD will give you the H1H annual average across all years and all receptors in the same way it gives you the H1H 3-year average across all years and all receptors. However, this is not correct! When ANNUAL is specified, AERMOD computes the 5-year average of the H1H annual averages. AERMOD does this for each receptor, then reports the concentration and receptor pertaining to the maximum 5-year average. So, rather than the H1H of the annual values, we would get a maximum 5-year average of the annual values. If we specified PERIOD rather than ANNUAL, we would get the receptor and concentration pertaining to the highest 5-year average of the 1-hour predicted concentrations.
Regarding the 3-hour and 24-hour standards, the explanation is more difficult, because the form of the standard states there can be no more than one exceedance each year. Values at each receptor need to be ranked separately for each year to find the H2H that occurs each year. This determines whether the standard is exceeded for an individual year. If the year that has the maximum H2H value of the yearly values does not exceed the standard, then it follows that the other 4 years would not exceed the standard, because each of the H2H values are lower than the maximum H2H.
If we ran all 5 years at once, rather than getting the H2H value for each year, we would get the single H2H value for all receptors across all years. In other words, all 3-hour and 24-hour values for the entire 5 years would be ranked for each receptor. The H2H for the 5 years might be the H1H for a single year, rather than the H2H for that year. This means the H2H when modeling all 5 years in a single simulation might give us a different answer from the maximum H2H value from the 5 years modeled separately.

## Slide 24: Running AERMOD Scenario 2: Run 4 5-Year NWS: 3-Hour, 24-Hour, Annual
Batch file to simplify running 5 years individually
The control files and batch file are in:
  ….\Hands-on\AERMOD\3-24hr_Ann_SO2_5-yr_NWS\
Navigate to the directory above
Double click on the .bat file
Notes: Because we are running each of the 5 years separately, a batch file (RunMC.bat) that will run each year in sequence is provided to simplify the model runs. You might want to open the batch file in a text editor to see what it is doing. For each year, it renames the appropriate control file to aermod.inp, calls the AERMOD executable, renames aermod.out to a unique name that identifies the applicable year, then deletes aermod.inp.
  To run the batch, open a command prompt and set the working directory to the directory where the batch file is located, shown on the slide in blue text (APTI423\Hands-on\AERMOD\3-24hr_Ann_SO2_5-yr_NWS\). At the command prompt, type: RunMC (not case sensitive).
  It might take as long as 40–60 minutes to run depending on the speed of your machine.

## Slide 25: 3-Hour, 24-Hour, and Annual Results 5-Year NWS
Year | Annual—H1H (µg/m3) | 24-hour—H2H (µg/m3) | 3-hour—H2H (µg/m3)
2008 |  |  | 
2009 |  |  | 
2010 |  |  | 
2011 |  |  | 
2012 |  |  | 
Notes: To get the results, you will need to open the five “.out “or “.sum” files in a text editor and find the summary tables near the bottom of the file. There should be a separate summary table for the 3-hour, 24-hour, and annual results as we have seen in previous model runs.
The results are displayed here by year, and the maximum of the 5 yearly values for each averaging period is identified with red text.
Remember, for each year we are interested in the H1H annual average and the H2H 3-hour and 24-hour average.
The next slide summarizes our 1-hour, 3-hour, 24-hour, and annual results using 5 years of NWS data compared to the SO2 NAAQS.

## Slide 26: 3-Hour, 24-Hour, and Annual Results 5-Year NWS
Year | Annual—H1H (µg/m3) | 24-hour—H2H (µg/m3) | 3-hour—H2H (µg/m3)
2008 | 14.7 | 99 | 610
2009 | 14.4 | 108 | 663
2010 | 16.5 | 142 | 657
2011 | 15.4 | 123 | 599
2012 | 15.5 | 128 | 711
Notes: To get the results, you will need to open the five “.out “or “.sum” files in a text editor and find the summary tables near the bottom of the file. There should be a separate summary table for the 3-hour, 24-hour, and annual results as we have seen in previous model runs.
The results are displayed here by year, and the maximum of the 5 yearly values for each averaging period is identified with red text.
Remember, for each year we are interested in the H1H annual average and the H2H 3-hour and 24-hour average.
The next slide summarizes our 1-hour, 3-hour, 24-hour, and annual results using 5 years of NWS data compared to the SO2 NAAQS.

## Slide 27: 5-Year NWS Results
Averaging Time | Standard (µg/m3) | Value (µg/m3)
Annual | 20 Annual arithmetic average (highest) | 16.5
24-hour | 91 Not to be exceeded more than once per year (H2H) | 142
3-hour | 1309 Not to be exceeded more than once per year (H2H) | 711
1-hour | 196 3-year average of the annual 99th percentile of 1-hour daily maximum concentrations | 1224
Notes: Here we show a completed table of modeled values using 5 years of NWS data compared to the SO2 NAAQS.
The values in red exceed the SO2 NAAQS.
Although the form of the standard is the 3-year average, we use all 5 years in estimating the impact.
NOTE: Do not forget about “nearby” sources that might need to be included in the modeling and background concentrations! In a modeling demonstration to support an air permit, you will typically need to include “nearby” sources in your modeling run and add background concentrations to your modeled concentration to get a final design concentration to compare to the NAAQS. Check with the permitting authority to obtain an appropriate “nearby” source inventory and background concentrations and preferences for AERMOD setup. For demonstration purposes, we have ignored “nearby” sources and background concentrations. AERMOD has numerous options for applying varying background concentrations within the model (refer to the User’s Guide or Addendum), or if applying the same value for all hours modeled, the value can be added manually to the modeled concentration.

## Slide 28: 1-Year Site and 5-Year NWS Results
Avg Time | Standard (µg/m3) | 1-year Site Value (µg/m3) | 5-year NWS Value (µg/m3)
Annual | 20 Annual arithmetic average (highest) | 9.5 | 16.5
24-hour | 91 Not to be exceeded more than once per year (H2H) | 101 | 142
3-hour | 1309 Not to be exceeded more than once per year (H2H) | 474 | 711
1-hour | 196 n-year average of the annual 99th percentile of 1-hour daily maximum concentrations | 683 | 1224
Notes: Here we show the table of modeled values using 1 year of site-specific data and 5 years of NWS data compared to the SO2 NAAQS.
The values in red exceed the SO2 NAAQS.
Although the form of the standard is the 3-year average, we use the single year for the modeling conducted with site-specific data and 5 years for the modeling conducted with NWS data.
An important question to ask is whether the higher concentrations predicted with the 5 yrs. of NWS data is due to the longer met data record or if the NWS data is biased high because it is not representative. That is, if we were to run 5 yrs. of site specific data would the results be similar to NWS results.

## Slide 31
Notes: Comparing this figure to the 1 yr. site specific figure we see that the area of predicted non-attainment is considerably larger when 5 yrs. of NWS data are used.

## Slide 33: Next Exercise 3