## Slide 1: EXERCISE 3
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Exercise 3
Re-Run AERMET for the …\Sec-3_Run\1-yr_Onsite case but this time double the Zo to examine the sensitivity of certain estimated PBL parameters. These parameters will be found in AERMET’s output surface file (.sfc). Procedure follows:
  a. Double the Zo values (by hand) in the file: \Hands_On\AERSURFACE\MC\MC_2001_Imp_Can.sfc;
  b. Save the file as Double_Zo.sfc. Leave the new file in the same sub-directory \Hands_On\AERSURFACE\MC\

## Slide 3: Exercise 3
  Copy the following 5 files from:
  \AERMET\1-yr_Onsite\
  to the empty subdirectory labeled:
  \AERMET\1-yr_Onsite\Exercise_3\
    MCR_ST2.INP
    ONSITE_QAOUT.TXT
    RunMC - Stage II.bat
    SURFACE_QAOUT.TXT
    UPPER_QAOUT.TXT

## Slide 4: Exercise 3
  Edit the input file …\Exercise_3\ MCR_ST2.INP
    To properly reference the location of all files located in other directories
    Change output file names to Met_Double_Zo.sfc & Met_Double_Zo.pfl
    Assign …\AERSURFACE\MC\Double_Zo.sfc to the keyword aersurf (no need to change the parameter associated with the keyword aersurf2)
    Edit the .bat file to move back 2 levels instead of 1.
  Run AERMET by double clicking the .bat file

## Slide 5: Exercise 3
Question:
  What parameters in the AERMET’s Met_Double_Zo.sfc file would you expect to change?
  Compare files, have they changed?
  In general, how much have they changed?
  What is the reason that explains the changes?