## Slide 1: EXERCISE 4
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Exercise 4
Purpose:
The purpose of this exercise is to compare the 1 & 3-hr max concentrations for the “20m_Low_Buoy” case from Exercise_1(Base Case) with the concentrations produced from running the same case with Zo doubled for the same hours and receptors where the 1 & 3 hr max concentrations occurred in the Base Case.

## Slide 3: Exercise 4
  Procedure:
  Identify the concentrations of the 1-hr and 3-hr max from the “20m_Low_Buoy” case in Exercise_1. Also, identify the hours and receptors where they occurred. This information can be found in the AERMOD output file from the “20m_Low_Buoy” case.
  A sub-directory named …\Exercise_4\ is in the sub-directory …\Sec-3_Run\Exercise_1\ 20m_Low_Buoy\
  In the …\Exercise_4\ sub-directory there are two empty sub-directories named …\1-hr_max\ and …\3-hr_max\

## Slide 4: Exercise 4
  Copy the following into …\Exercise_4\1-hr_max\ and …\3-hr_max\:
    Input file from …\Sec-3_Run\Exercise_1\20m_Low_Buoy\
    Met_Double_Zo.sfc & .pfl from …AERMET\1-yr_Onsite\Exercise_3\
    The .bat file from …\Sec-3_Run\
    Surface_File_Header.sfc from …\Sec-3_Run\
  Edit the input file & the .bat file as discussed on the next 2 slides

## Slide 5: Exercise 4
For the two runs, make sure that each run models only the one hour of meteorology and the one location (receptor) for the 1-hr. max case; and the 3 hours and the one receptor for the 3-hr. max case. To do this you will need to edit the input file such as:
  To run a single receptor the RE pathway will look as follows:
  To run a single hour, or only 3 hours you will have to use two additional keywords in the ME pathway. That is:
  Change AVERTIME to 1 for the 1hr max and 3 for the 3hr max
RE
DISCCART x-coordinate y-coordinate
RE
ME
STARTEND YY MM DD HH YY MM DD HH
ME

## Slide 6: Exercise 4
  4) Under the OU pathway include only the first keyword “RECTABLE”
  Finally, under the ME pathway include the met data files for the double Zo case (i.e., Met_Double_Zo.sfc & Met_Double_Zo.pfl)
  Save input file in both 1-hr max and 3-hr max directories as:
  AERMOD_Sec-3_Run_20m_Low_Buoy.inp
  Edit the batch file to ensure that the model is found in the right directory and the .inp filename is correct. Save

## Slide 7: Exercise 4
  Re-Run the “20m_Low_Buoy” case with the doubled Zo meteorology for the 1-hr max case and then repeat for the 3-hr max case
  Once the two runs are completed compare the results against the original 20m_Low_Buoy case for both the 1-hr and 3-hr re-runs.
  Suggest some explanation for the differences in concentration with the doubling of Zo.

## Slide 8
    To understand the effects of doubling Zo on concentrations, examine the differences in met. parameters:
      For each run identify H, U*, L, Zim & u.
      For the Base Case run these parameters can be found in the file “Surface_Met.sfc” in the …\Sec-3_run\
      For the Double Zo case these met parameters can be found in the file “Met_Double_Zo.sfc” which is located in …\AERMET\1-yr_Onsite\Exercise_3\.
      Fine each of the hours you need in the these .sfc files and use Surface_File_Header.sfc to identify the met parameters.