## Slide 1: Exercise 5
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System
Examine the effects of Building Downwash
on short, low-buoyancy stacks

## Slide 2: Exercise 5
We will repeat the Sec-3 / Exercise 1 / low-stack, low-buoyancy case BUT with the 20-m high stack placed adjacent to the two-tiered building at Martin’s Creek.
We will then compare the results of this downwash case with the Exercise 1 low buoyancy case where no building was present.
Stack Height = 20 m
Exit Velocity = 5.8 m/s
Exit Temp = 350 K
Flat Terrain, Polar Grid (100m to 10,000m)

## Slide 3: Stack / Building configuration
Tier 1: 60m high
Tier 2: 100m high
Stack height = 20m
Stack is adjacent to Tier 1 face
*
Stack
N

## Slide 4: Exercise 5 (cont.)
You will find all the files** that you need to run this case in a subdirectory labeled:
Hands-on \ Sec-3_run \ Exercise1 \ 20m_Low_Buoy \ Exercise 5:
  AERMOD.exe
  AERMOD_Sec_3_run.inp
  MC_bpipprm.out
  Surface_Met.sfc
  Profile_Met.pfl
  ** there will be no need for any ..\

## Slide 5: Exercise 5 (cont.)
Steps for this exercise
Go to directory: Hands-on / Sec-3_run / Exercise1 / 20m_Low_Buoy / Exercise 5
In MC_BPIPPRM.OUT (which came from our run of BPIPPRM for Martin’s Creek yesterday) copy the building data into the clipboard (data in the last 30 lines of file where each line starts with SO)
Paste building data into the AERMOD_Sec-3_Run.inp file immediately after the SRCPARAMS and before SRCGROUP. Delete (manually) the first five spaces in each line of the building data so that SO appears in the first column.

## Slide 6: Exercise 5 (cont.)
Steps for this exercise (continued)
In the lines labeled LOCATION and SRCPARAM, change “STACK” to “MC12” for consistency with the building data
Save the file as AERMOD.INP
To run AERMOD on this case: Simply Double-click on aermod_24142.exe
Run should take less than a minute or two.

## Slide 7: Exercise 5 (cont.)
Steps for this exercise (continued)
In AERMOD.OUT file, locate the maximum 1-hr, 3-hr, and 24-hr concentrations and their locations.
Compare to the same results for the Exercise 1 / low-stack, low-buoyancy case with no downwash (AERMOD.out file located in Hands-on / Sec-3_run / Exercise1 / 20m_Low_Buoy directory)

## Slide 8: Effects of downwash on short stacks
Averaging Time | No Building (µg/m3) | With Downwash (µg/m3) | Downwash / No Downwash
1-hour |  |  | 
3-hour |  |  | 
24-hour |  |  |