## Slide 1: AERSCREEN
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Understand AERSCREEN Fundamentals
Describe the input data requirements of AERSCREEN
Input data from other associated programs needed to run AERSCREEN
Run the AERSCREEN program
Interpret the results from AERSCREEN

## Slide 3: Overview
AERSCREEN Fundamentals
Screening w/ AERMOD:
  AERSCREEN (Prompt-driven)
  Running MAKEMET then AERMOD using the SCREEN keyword
AERSCREEN Inputs:
  Sources
  Meteorology
  Downwash
  Receptors
  Terrain
  Other Options
AERSCREEN Receptor Network
Running AERSCREEN & Reviewing its Output

## Slide 4: AERSCREEN Fundamentals
Two ways to perform screening modeling:
  Using AERSCREEN system in a prompt-response interactive mode to generate all or most of the necessary input – single line of receptors
  OR
  Developing meteorology with MAKEMET and then run AERMOD in its screening mode – allows total flexibility in defining the receptor grid
  Focus will be on “AERSCREEN Interactive”
Notes: If you use AERSCREEN, a DOS-based interface will prompt for a variety of inputs for options, source, receptor, terrain, downwash, and meteorology.
There are a few places where the user can specify an existing file in lieu of responding to a series of prompts. One example is building downwash information. The user can either respond to several building-related prompts (to run BPIPPRM) or enter the name of an existing file created by BPIPPRM external to AERSCREEN.
In the prompt-response method, a program known as MAKEMET generates the screening meteorology. This same program can be used stand-alone to create the screening meteorology that is input into a full AERMOD run (with the SCREEN model option specified). This is useful if you need to specify a grid of receptors (versus a line in AERSCREEN).

## Slide 5: AERSCREEN Fundamentals
AERSCREEN can be run for only a single source
Concentrations are presented on the plume’s centerline only defined as 270o (arbitrary direction)
Meteorological data is generated through MAKEMET.
Calculates only 1-hour averages (not probabilistic); then scales to 3hr, 8hr, 24 hr, and annual.
Includes calls to MAKEMET, BPIPPRM, and AERMAP to generate necessary AERMOD input
3 options for entering Surface Characteristics
Notes: AERSCREEN is an interface that runs AERMOD in screening mode as well as several of the preprocessors used with the AERMOD system.
A great advantage of using AERSCREEN is the fact that the user does not need 5 years of National Weather Service (NWS) or 1-year-old site-specific meteorological data. AERSCREEN develops the meteorology using MAKEMET based on the user responses to a series of prompts.
AERSCREEN runs AERMOD for a single source with limited input and only calculates 1-hour averages. Scaling factors are applied to estimate 3-hour, 8-hour, 24-hour, and annual averages (0.9, 0.7, 0.4, 0.08, respectively).
AERSCREEN runs in a Windows Command Prompt (DOS-prompt). It is a prompt-driven interface that, in addition to running AERMOD in screening mode, runs MAKEMET, BPIPPRM, and AERMAP to generate or process the necessary meteorology, building, and elevation data required by AERMOD.
AERSCREEN does not run AERSURFACE but requires surface characteristics like AERMET with multiple options for user input.

## Slide 6: AERSCREEN Fundamentals
Ability to model NOX to NO2 conversion is limited to :
  Ozone Limiting Method (OLM) or Plume Volume Molar Ratio (PVMRM)
    NO2/NOX in-stack ratio (0.0–1.0)
    Input representative background ozone
    NO2/NOX ambient equilibrium ratio is set to 0.9 and cannot be overridden
Notes: See the AERSCREEN User’s Manual for more information on the specific source prompts.
Unlike AERMOD, AERSCREEN can model flares as a point source after making the exit velocity 20 m/s and exit temperature 1,273 K (as was done in SCREEN3). A stack diameter and effective stack height are calculated.
AERSCREEN can incorporate input data needed to use OLM or PVMRM when modeling NO2.
OLM: Ozone Limiting Method
PVMRM: Plume Volume Molar Ratio Method
To use OLM or PVMRM, the user is prompted to enter the NO2/NOX in-stack ratio and a representative background concentration. AERSCREEN sets the NO2/NOX ambient equilibrium ratio to the default value of 0.90.

## Slide 7: AERSCREEN Fundamentals: Programs Used by AERSCREEN
AERSCREEN will use the programs:
  MAKEMET
  AERMAP
  BPIPPRM
  AERMOD
  If the executable files are not located in the working directory, you will be prompted to enter the path and filename (Recommend: copy all files to working dir.)
Terrain Processing: The file “demlist.txt” (which includes the NED files) is needed for terrain processing - must be located in the working directory
Notes: AERSCREEN calls the programs listed as needed.
MAKEMET is used to generate screening meteorology.
AERMAP extracts terrain elevations for sources and receptor locations and determines receptor hill height scales. AERMAP is not called if terrain is not considered (flat terrain).
BPIPPRM generates building parameters required for building downwash.
AERMOD is called and run in screening mode.
AERSCREEN searches the current working directory for these program executable files. If it cannot find the executables in the working directory, AERSCREEN will prompt the user to enter their location. Both the path and filename of the executables must be entered.
“demlist.txt” is required if terrain processing is performed. It should be stored either in the folder where the AERSCREEN executable is stored or in the current working directory.
“demlist.txt” names: 1) the location of the NADGRID files required for datum conversion and 2) the path and filenames of the terrain elevation files.

## Slide 8: AERSCREEN Inputs: Sources
AERSCREEN can only model one source at a time
Source types
  POINT, including capped and horizontal
  AREA, including AREACIRC but not AREAPOLY
    Unlike emission rate entered as g/s/m2 in AERMOD, enter as g/s in AERSCREEN (or lb/hr, depending on units entered at the prompt)
  VOLUME
  OPENPIT
  FLARE
  LINE, BUOYLINE, and RLINE, new in AERMOD since 2017 (presently not available in AERSCREEN)
Notes: Whereas multiple sources and a mixture of source types can be modeled simultaneously in AERMOD, AERSCREEN can only model a single source during a simulation. If more than one source needs to be modeled, then a full screening AERMOD run with screening meteorology could be performed apart from the AERSCREEN interface. Consult with the regulatory agency for additional guidance if necessary.
Be aware that unlike AERMOD, AERSCREEN requires the AREA source emission rate to be entered as g/s or lbs/hr, depending on how the units of measure were specified near the beginning of the prompts. DO NOT enter AREA emission rate as rate per unit area (g/s-m2).
In addition to the source types available in AERMOD, AERSCREEN can model flares as a point source after making the exit velocity 20 m/s and exit temperature 1,273 K (as was done in SCREEN3). A stack diameter and effective stack height are calculated.
Note: At the time this course was developed, the new LINE, RLINE, and BUOYLINE sources in AERMOD are not available in AESCREEN.

## Slide 9: AERSCREEN Inputs: Meteorology
MAKEMET—generates a matrix of meteorology in the form of AERMOD’s .sfc &.pfl files
  Based on:
    Looping through a range of u, cc, Ta, solar elevation angle & w* for user specified surface characteristics (Zo, Bo and r) which can vary by sector and time periods (e,g., seasonal or monthly)
    For stable conditions it calculates Zim from u* and then loops through Zim factors for smoothing Zim
    Calculating u*, L and Zim for each combination in the matrix
Notes: MAKEMET is called by AERSCREEN to generate screening meteorology without the need for 1 year of site-specific data or 5 years of NWS data. MAKMET generates a matrix of meteorological conditions in the file formats required by AERMOD. Based on user input, it is possible to generate input files that have more records than a standard year of NWS data (8760 hours).
MAKEMET can also be run as a stand-alone program if there is a need to run AERMOD in screening mode outside of the AERSCREEN interface due to the limitations imposed by the interface.
MAKEMET requires surface characteristic like AERMET. As mentioned previously, AERSCREEN does not call or use AERSURFACE (i.e., does not execute AERSURFACE); therefore, surface characteristics must be input to AERSCREEN by the user.
AERSCREEN provides three options for specifying surface characteristics:
User-specified without spatial or temporal variation. This is a good way to examine the sensitivity of sfr char.
  One value for albedo, one for Bowen ratio, and one for roughness length—i.e., single sector for all hours modeled.
  Seasonally varying for a generic land use based on tables in the AERMET User’s Guide.
  Seasonal values for albedo, Bowen ratio, and roughness length based on the user-response for a dominant land cover as defined in the AERMET User’s Guide.
  Seasons are Winter (Dec–Feb), Spring (Mar–May), Summer (June–Aug), and Autumn (Sept–Nov).
Input path and filename of an AERSURFACE output file containing the characteristics; allows for temporal and spatial variations.
  User runs AERSURFACE outside of AERSCREEN and supplies the resulting filename to AERSCREEN.
  AERSCREEN automatically informs MAKEMET to generate meteorology for a single wind direction, 270 degrees, to accommodate a single line of receptors.

## Slide 10: AERSCREEN Inputs: Meteorology
  When using AERSCREEN a pair of files is created for each temporal period/spatial sector combination
  Convention: year = 10; hours = 01-11 (stable hours), 12-24 (convective hours)
In each file all wind directions are set to 270. Although the met files show a constant 270 direction the appropriate direction is used for each sector when considering a variety of sectors for surface characteristics, &/or downwash &/or terrain
Notes: MAKEMET is called by AERSCREEN to generate screening meteorology without the need for 1 year of site-specific data or 5 years of NWS data. MAKMET generates a matrix of meteorological conditions in the file formats required by AERMOD. Based on user input, it is possible to generate input files that have more records than a standard year of NWS data (8760 hours).
MAKEMET can also be run as a stand-alone program if there is a need to run AERMOD in screening mode outside of the AERSCREEN interface due to the limitations imposed by the interface.
MAKEMET requires surface characteristic like AERMET. As mentioned previously, AERSCREEN does not call or use AERSURFACE (i.e., does not execute AERSURFACE); therefore, surface characteristics must be input to AERSCREEN by the user.
AERSCREEN provides three options for specifying surface characteristics:
User-specified without spatial or temporal variation. This is a good way to examine the sensitivity of sfr char.
  One value for albedo, one for Bowen ratio, and one for roughness length—i.e., single sector for all hours modeled.
  Seasonally varying for a generic land use based on tables in the AERMET User’s Guide.
  Seasonal values for albedo, Bowen ratio, and roughness length based on the user-response for a dominant land cover as defined in the AERMET User’s Guide.
  Seasons are Winter (Dec–Feb), Spring (Mar–May), Summer (June–Aug), and Autumn (Sept–Nov).
Input path and filename of an AERSURFACE output file containing the characteristics; allows for temporal and spatial variations.
  User runs AERSURFACE outside of AERSCREEN and supplies the resulting filename to AERSCREEN.
  AERSCREEN automatically informs MAKEMET to generate meteorology for a single wind direction, 270 degrees, to accommodate a single line of receptors.

## Slide 11: AERSCREEN Input: Meteorology
Prompts for Running MAKEMET
  Minimum temperature (default: 250 K)
  Maximum temperature (default: 310 K)
  Minimum wind speed (default: 0.5 m/s)
  Anemometer height (default: 10 meters)
  Options for specifying surface characteristics:
    1) Single user-specified values for albedo, Bowen ratio, and surface roughness length
    2) AERMET seasonal tables
    3) Specify AERSURFACE output file
Notes: The parameters required to run MAKEMET are listed here, which include climatology data (temperature and wind speed), theoretical anemometer height, and surface characteristics.
Minimum and maximum temperature and minimum wind speed should be entered based on the known local climatological conditions.
Surface Characteristics
User-specified without spatial or temporal variation.
  One value for albedo, one for Bowen ratio, and one for roughness length—i.e., single sector for all hours modeled.
Seasonal values for albedo, Bowen ratio, and roughness length based on the user-response for a dominant land cover (as defined in the AERMET User’s Guide) and climatology type (moisture conditions).
Input a name of an AERSURFACE output file containing the characteristics; allow for temporal and spatial variations.
  User runs AERSURFACE outside of AERSCREEN and supplies the resulting filename to AERSCREEN.

## Slide 12: AERSCREEN Input: Surface Characteristics
Surface Characteristics:
  Option 1:
    Albedo
    Bowen ratio
    Surface roughness, in meters
  Option 2:
    You choose: 1) A Land use type and an average moisture climatology
    AERSCREEN produces thru MAKEMET a set of .sfc and .pfl for each of 4 seasons.
  Option 3:
    Output file from AERSURFACE (provided by user)
    AERSCREEN produces, thru MAKEMET “x” sets of .sfc & .pfl files,
    where x= (# of time periods – max is 12 months ) x (# of sectors max is 12)
    AERSCREEN does not call AERSURFACE
Notes: This slide lists the parameters required to input surface characteristics required by MAKEMET. The number in parentheses indicates the input option specified by the user.
Surface Characteristics
User-specified without spatial or temporal variation.
  One value for albedo, one for Bowen ratio, and one for roughness length—i.e., single sector for all hours modeled.
Seasonal values for albedo, Bowen ratio, and roughness length based on the user-response for a dominant land cover (as defined in the AERMET User’s Guide) and climatology type (moisture conditions).
Seasons are Winter (Dec–Feb), Spring (Mar–May), Summer (June–Aug), and Autumn (Sept–Nov).
  Land cover categories
    Water
    Deciduous forest
    Coniferous forest
    Swamp
    Cultivated land
    Grassland
    Urban
    Desert shrubland
  Climatology profile
    Average moisture
    Wet conditions
    Dry Conditions
Input a name of an AERSURFACE output file containing the characteristics; allow for temporal and spatial variations.
  This option requires the user to run AERSURFACE outside of AERSCREEN and supply the resulting filename to AERSCREEN.

## Slide 13: AERSCREEN Input: Downwash
AERSCREEN runs BPIPPRM for point sources and flares if the downwash option is elected (single building only)
Two options
  Respond to a series of prompts for a single building
  Use existing BPIPPRM output for a more refined analysis
Notes: If the downwash option is specified, AERSCREEN prompts for building information and calls BPIPPRIM.
AERSCREEN provides two options for providing building information:
Respond to a series of prompts for a single 1-tiered, rectangular building.
Enter the path and filename of an existing BPIPPRM output file if there are multiple buildings and/or buildings with multiple tiers or complex shapes. This, of course, requires BPIPPRM to be run separately, apart from the AERSCREEN interface.
If you select the first option, respond to the prompts for a single building. You are asked for the building height and the maximum and minimum horizontal dimensions.

## Slide 14: AERSCREEN Input: Building Downwash
AERSCREEN provides two choices: (considers 36 directions in each case)
  Prompts: Simple rectangular building:
    Building height
    Maximum horizontal building dimension
    Minimum horizontal building dimension
    Angle, in degrees from N, of the max horizontal dimension (0-179)
    Angle, in degrees from north, of the stack relative to building center (0–359)
    Distance from stack to center of building
  More complex building structure
    Specify BPIPPRIM output file
Notes: For building downwash, the user has the option to enter building information for a simple, rectangular one-tier building or specify an existing BPIPPRM output file.
If the user chooses the option to enter an existing BPIPPRM output file, the user is prompted for the filename. If the file is not in the working folder, then the path needs to be included. For a path and/or filename with embedded spaces, place quotation marks around the entire name.
This slide lists the parameters for which the user is prompted when the user chooses to enter building parameters for a simple rectangular building. Values should be entered with respect to the units of measure specified by the user in an earlier prompt.
Building height: Height of the top of the building above the ground.
Maximum horizontal building dimension: Longest side of the rectangular building; not the longest projected length.
Minimum horizontal building dimension: Shortest side of the rectangular building.
Angle, in degrees from north, of the maximum horizontal dimension: Angle from north (in a clockwise direction) between a vector pointing north from the center of the building and the longest side of the building. Limited from 0 to 179 degrees.
Angle, in degrees from north, of the stack relative to the building: Angle from north (in a clockwise direction) between a vector pointing north from the center of the building and a line from the center of the building to the stack. From 0 to 360 degrees.
Distance from the stack to the center of the building.
A simple example of these parameters is illustrated on the next slide.

## Slide 15: AERSCREEN Input: Simple Rectangular Building
Notes: Illustration is from the AERSCREEN User’s Guide.

## Slide 16: AERSCREEN Input: Receptors
AERSCREEN creates a regularly spaced line of receptors at discrete distances out to the “probe” distance
  Probe distance is the maximum downwind distance to estimate impacts
User must specify a probe distance or use defaults:
5,000 m (no terrain) or 10,000 m (with terrain)
Receptor placement begins at fence line and every 25 m beginning with the next multiple of 25, out to 5,000 m
If the probe distance exceeds 5,000 m, the incremental distance between receptors changes
  Increment = Probe Distance – 5,000)/100 (min increment = 25m)
Notes: AERSCREEN generates an automated line of receptors from the fence line out to the probe distance.
The fence line distance (or distance from the source to the ambient air) and the probe distance are entered by the user.
AERSCREEN has built-in default probe distances, dependent on whether terrain effects are included: 5,000 m without terrain effects or 10,000 m with terrain effects.
Receptor placement is at the fence line then every 25 meters beginning with the next multiple of 25, out to 5,000 meters. Beyond 5,000 meters, the increment is determined by the following equation:
Increment = (Probe Distance – 5,000)/100)
An example of a line of receptors with an ambient boundary of 85 meters from the source, no terrain and default probe distance of 5,000 m:
1st receptor is at the ambient boundary
2nd receptor is at 100 meters
3rd receptor is at 125 meters
.
.
.
Nth receptor is at the probe distance

## Slide 17: AERSCREEN Input: Receptors
A file with up to 10 discrete receptors can be input
  Sensitive populations or other locations of interest
  Only processes receptors that are between the ambient air boundary and probe distance
  Discrete distances must be entered in a separate file
  Format of the file
units: METERS
160
215
Notes: As indicated previously, up to 10 user-defined discrete receptors can be specified by distance from the source. These are typically for the purpose of representing sensitive populations such as a school, daycare, hospital, nursing home, or other location of interest.
AERSCREEN only processes receptors that are between the ambient boundary (fence line) and the probe distance.
Discrete distances must be listed in an external file in the format shown. The first record defines the unit of measure of the distances. Distances can be entered as:
FEET or FT for feet
METERS for meters
KILOMETERS, KILO-METERS, or KM for kilometers
MILES for miles
Unit of measure is NOT case sensitive.
If including discrete receptors, user is prompted to enter the path and filename of the discrete receptor file.

## Slide 18: AERSCREEN Input: Terrain
Prompts for terrain effects
  Include terrain processing: (y(es) = include terrain, n(o) = do not include terrain effects)
  Probe distance (meters) – maximum downwind distance
  Source elevation or use AERMAP to determine source and elevations
The following prompts are displayed if the response to including terrain effects is “yes”
  Source coordinates (geographic latitude/longitude or Universal Transverse Mercator (UTM))
  UTM zone (if UTM coordinates entered)
  North American Datum (NAD) datum (NAD 27 or 83)
Notes: The default probe distance (the maximum receptor distance) depends on whether terrain effects are considered. If there are no terrain effects, the default probe distance is 5,000 meters; if there are terrain effects, the default probe distance is 10,000 meters. The user has the option to override the default value.
When the probe distance is entered, AERSCREEN checks if the probe distance is a multiple of 25 meters. If the distance is not a multiple of 25, the probe distance is reset to the next distance that is greater than the entered probe distance and is a multiple of 25. For example, if the entered probe distance is 1,031 m, AERSCREEN will reset the distance to 1,050 m.
If the response to including terrain effects is “no,” or the source type is a rectangular area source, a source elevation can be entered. The default value is 0 meter.
Valid NADA values are 1 and 4 for North American Datum of 1927 (NAD27) and North American Datum of 1983 (NAD83), respectively.

## Slide 19: AERSCREEN Input: Terrain
DEMLIST.TXT
  Must be included in working directory
  Identifies location of elevation data file(s)
  Must reside in working directory or the directory with the AERSCREEN executable
  Also, must include location of datum shift files (conus.las and conus.los) – although not necessary these files must be included.
Source elevation and terrain elevations can be derived by AERMAP
Notes: When terrain effects are considered, AERSCREEN calls AERMAP to extract terrain elevations and derive hill height scales for the receptors and source.
The user must identify the elevation data file(s) to be used by AERMAP in a text file named DEMLIST.TXT. The elevation files are identified by path and filename. DEMLIST.TXT must reside in either the working directory or the directory where the AERSCREEN executable is located, if the two directories are different. If DEMLIST.TXT is not found in either directory, AERSCREEN will report the error and abort processing.
The location of the .los and .las files required to compute datum shift, when needed, is also stored in the DEMLIST.TXT.
Reminder: For any path/filename that contains spaces, enclose it the path/filename in quotation marks.
Terrain elevations are derived for all sources except rectangular area sources.
The format of DEMLIST.TXT will be discussed later.

## Slide 20: AERSCREEN Input—Terrain
DEMLIST.TXT format
  Example:
Record | Contents
1 | Data file type (NED or DEM)
2 | Delineator between file type and list (a series of dashes)
3 | Location of conus.las and conus.los files (provided)
4 | Location of Terrain files
NED
----------------------------------------------------
NADGRIDS: .\
..\AERMAP\Seamless_DEM\NED_75872377.tiff
Notes: Other valid entries for National Elevation Data (NED) file terrain units are FEET; DECI-FEET or DECIFEET; DECA-FEET or DECAFEET; DECI-METERS or DECIMETERS; or DECA-METERS or DECAMETERS.
For Digital Elevation Model (DEM) files, the terrain units cannot be included.

## Slide 21: AERSCREEN Input: Receptors
Option to specify up to 10 discrete receptor locations (e.g., schools, hospital, other distance of interest) in a text file
Option to specify flagpole height for all receptors
Three main routines for processing receptors:
  PROBE
  FLOWSECTOR
  REFINE
Notes: In addition to the automated line of receptors, up to 10 discrete receptor distances can be specified. These distances must be indicated in a text file (discrete receptor file) for which the user must enter the path and filename where the file is located.
The units of measure for the distances specified must also be included in the discrete receptor file. Units can be FEET or FT; METERS; KILOMETERS, KILO-METERS, or KM; or MILES (not case sensitive).
AERSCREEN will prompt whether to use flagpole heights for ALL receptors.

## Slide 22: Receptor Processing
PROBE: Executed when there is no source-receptor directional dependency (i.e., no downwash and no terrain)
  Probe executes AERMOD for each combination of temporal period and spatial sector).
    The # of receptors is “Pb”; where Pb = # of receptors on the line out to the Probe distance
    The # of concentrations calculated by AERMOD =
    Pb x (# of Land use temporal periods) x (# of Zo sectors)
  Then the highest concentration from the set of receptors located at each distance out to the probe distance, for each sector and time period is stored by AERSCREEN for refinement by REFINE.
  Therefore, AERMOD could be executed a max of 144 times

## Slide 23: Receptor Processing
FLOWSECTOR: Executed when considering Downwash and/or Terrain
  Executed when there is a directional dependency on source receptor relationships
  FLOWSECTOR arranges receptors along 36 radials from the source (every 10o). Then AERMOD is executed for each Zo sector and land use time frame along each flow vector
  The # of receptors = Pb x 36
  The # of concentrations calculated = Pb x 36 x (the # of Zo sectors) x (the # of land use time frames)

## Slide 24: Receptor Processing
    TERRAIN:
      The terrain receptor grid domain is calculated as 1.1 x the probe distance (i.e., the area from which hc is determined)
      AERSCREEN finds the elevation and the hc for all receptors
      Then the highest concentration from the set of receptors, located at each distance, is stored by AERSCREEN for refinement by REFINE
    BUILDING DOWNWASH
      The projected building parameters, calculated by BPPIPRM, for each of the 36-flow direction are included in the AERMOD run
      As with terrain all receptors are modeled using AERMOD
      Then the highest concentration from the set of receptors, located at each distance, is stored by AERSCREEN for refinement by REFINE

## Slide 25: Receptor Processing
REFINE: Finds the Max Conc, its’ associated dist. & date that was output from PROBE or FLOWSECTOR and places new receptors around the Cmax at 1, 2, or 5 meters (depending on dist. to max) to increase the spatial resolution and refine the output.
  For PROBE Output:
    REFINE uses the met files appropriate for the Zo sector & time frame of the Max Conc.
  For FLOWSECTOR Output:
    REFINE finds the upwind Zo sector and direction of max concentration
    REFINE then used the met files appropriate for that sector

## Slide 26: Receptor Processing REFINE (cont.)
  For Downwash Cases : Building dimensions for the flow direction having the Max Conc is used when running AERMOD for the new receptors
  For complex terrain:
    REFINE will rerun AERMAP with the new receptors in the flow direction of the max concentration output from FLOWSECTOR.
    REFINE will also create an appropriate domain, for use in AERMAP to determining an appropriate hc for each new receptor.
  Finally REFINE runs AERMOD using the new receptors, appropriate meteorology, building & terrain data.

## Slide 27: AERSCREEN Options
Adjust u* to address potential overpredictions under stable low wind conditions
Rural/Urban
Distance to fence line (ambient air)
Flagpole receptors
Can consider “inversion break-up fumigation”
Can consider “shoreline fumigation”
Can produce additional information if DEBUG is used.
Notes: AERSCREEN contains an option to adjust U* to address issues related to potential overpredictions under stable low wind conditions.
AERSCREEN will calculate fumigation due to inversion break-up and coastal fumigation for point sources with release heights (above ground level) 10 m or more in height. The fumigation equations are taken from SCREEN3 (U.S. EPA, 1995) and follow the methodology of Turner (1970).
The inputs to AERSCREEN.INP are:
Calculate inversion break-up fumigation (Y = calculate fumigation, N = do not calculate fumigation).
Calculate shoreline fumigation (Y = calculate fumigation, N = do not calculate fumigation).
Minimum distance to shoreline in meters (less than 3,000 m).
Optional direction to shoreline from source (0–360 degrees or -9 for no specified direction).
For shoreline fumigation, the user also enters the minimum distance to the shoreline from the source. The user also has the option to specify the direction from the source to the shoreline when using spatially varying surface characteristics for MAKEMET. This option allows AERSCREEN to use appropriate surface characteristics corresponding to the upwind direction from the source to shoreline. For the fumigation options, the source is considered rural, no downwash effects are included, and no terrain effects are included.
AERSCREEN allows for the option to output a debug file that contains all intermediate output from the stages of AERSCREEN (PROBE and FLOWSECTOR). See Section 3.5 and 3.6 of the AERSCREEN User’s Guide for further details. When fumigation options are selected, the debug option will also output the meteorological variables and iterations of the fumigation calculations.

## Slide 28: AERSCREEN Output
AERSCREEN generates many output files
  The output files include:
    AERSCREEN.OUT – source info, building downwash para, meteorology, max1hr & scaled 3, 8 & 24 hr & annual,The scaling factors are: 1.0, 0.9, 0.6, and 0.1 (respectively)
    AERSCREN.LOG – surface chara & met files to be produced
    AERSCREEN.INP – used for restart
    AERMAP.LST – all receptors (x,y,z & hc)
Notes: If the user enters an output filename in response to a prompt and omits the extension, AERSCREEN will re-prompt the user for a filename.
The meteorological parameters listed in the output file include a summary of the several parameters that went into MAKEMET (min/max temperature, minimum wind speed, anemometer height, surface characteristics), the conditions associated with the overall maximum impact, and the conditions associated with the ambient boundary impact.
In addition, a final non-downwash plume height is listed for the latter two sets of meteorological parameters.
The impact summary includes the maximum impact and the impact at the ambient boundary.
AERSCREEN computes the 1-hour concentration, then applies the scaling factors to the 1-hour concentration to obtain the 3-hour, 8-hour, 24-hour, and annual values. Compare these to SCREEN3: 0.90, 0.70, 0.40, 0.08, respectively.

## Slide 29: AERSCREEN Output (cont.)
    Metfile_xx_yy.sfc & .pfl – xx=time period, yy=sector or direction
    BPIPPRM.out – building dim by direction
    MAKEMET.LOG – summary of inputs, # of met data combinations
    max_conc_distance.txt – output from REFINE, max conc for a dist + met
    concentrations.txt - output from PROBE &/or FLOWSECTOR, i.e., predicted concentration at all receptors with all met combinations (only produced if DEBUG is selected)
Notes: If the user enters an output filename in response to a prompt and omits the extension, AERSCREEN will re-prompt the user for a filename.
The meteorological parameters listed in the output file include a summary of the several parameters that went into MAKEMET (min/max temperature, minimum wind speed, anemometer height, surface characteristics), the conditions associated with the overall maximum impact, and the conditions associated with the ambient boundary impact.
In addition, a final non-downwash plume height is listed for the latter two sets of meteorological parameters.
The impact summary includes the maximum impact and the impact at the ambient boundary.
AERSCREEN computes the 1-hour concentration, then applies the scaling factors to the 1-hour concentration to obtain the 3-hour, 8-hour, 24-hour, and annual values. Compare these to SCREEN3: 0.90, 0.70, 0.40, 0.08, respectively.