## Slide 1: AERSCREEN Hands-on
Course #423
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System
Day 4 Morning

## Slide 2: Learning Objectives
At the end of this lesson the student should be able to:
Respond to the prompts for an interactive session with AERSCREEN
Produce output and know where to find the results
Rerun AERSCREEN without responding to all the prompts again
Run AERSCREEN on Martins Creek with Allentown met
Compare results for 3, 24, and annual averages from our 5yr runs with the AERSCREEN results

## Slide 3: Application To Be Run
Martins Creek main stack only
Surface Characteristics from the Allentown airport
Terrain from Martins Creek area included
Downwash from Martins Creek’s 2-tiered bldg.
Perform screening analysis of Hands-On analysis we completed in last presentation
Compare screening results to refined analysis

## Slide 4: Running AERSCREEN
We will be running two options:
Using look-up tables to define surface characteristics for each season;
Re-run using the surface characteristics produced in the AERSURFACE Hands-On exercise
Notes: When AERSCREEN starts, you will be prompted to enter specific information to set up the simulation.
First, enter a Title. Unlike AERMOD, which allows two titles, AERSCREEN allows only one.
Next, indicate if you will enter values in English or Metric units. For this activity, enter “M” for metric.
Enter the source type. The valid source types are shown; you only need to enter a single letter, as identified in the parentheses. Enter “P” for point source.
With AERSCREEN, you can model flares (the F). The option to model a flare is not available in AERMOD as a distinct source type.

## Slide 5: Files Needed in the AERSCREEN Working Directory
These files are already in the AERSCREEN Option_1_run directory:
  Aerscreen_21112.exe
  aermap.exe
  aermod.exe
  bppiprm.exe
  conus.las
  conus.los
  demlist.txt
  makemet.exe
  MC_bpipprm.inp

## Slide 6: Before Running AERSCREEN
Since we are considering terrain, we need to create the following file and place it in AERSCREEN’s working directory:
demlist.txt
NED
----------------------------------------------------------
NADGRIDS .\
..\..\AERMAP\Seamless_Dem\MC_NED_76_1deg_NC.tiff
..\..\AERMAP\Seamless_Dem\MC_NED_75_1deg_NC.tiff

## Slide 7: Steps for Running AERSCREEN
AERSCREEN will be run interactively for the Option_1_run (no need for a control file)
To run AERSCREEN, you will navigate to the directory that contains the AERSCREEN executable (the working directory)
….\Hands-On\AERSCREEN\Option_1_run\
You will double-click on aerscreen.exe to open a command window and execute AERSCREEN
The program will pause at the first prompt waiting for your input
Notes: We will run AERSCREEN in the prompt-driven interactive mode, so a control file has not been provided for this hands-on activity.
To run AERSCREEN for this activity, navigate to the working directory where the executable is located, and the output will reside, and double-click on AERSCREEN.EXE. A DOS command window will open, AERSCREEN will start to run, and pause at the first prompt for input.

## Slide 8: Running AERSCREEN Option 1
Open directory ..\Option_1_run & double click on AERSCREEN_21112.exe
Enter Title (e.g., AERSCREEN Hands-on): Option_1_run
Next indicate if you are working in English or Metric units—enter “M” (or “m”) for Metric
Enter the source type—enter “P” for point source
Notes: When AERSCREEN starts, you will be prompted to enter specific information to set up the simulation.
First, enter a Title. Unlike AERMOD, which allows two titles, AERSCREEN allows only one.
Next, indicate if you will enter values in English or Metric units. For this activity, enter “M” for metric.
Enter the source type. The valid source types are shown; you only need to enter a single letter, as identified in the parentheses. Enter “P” for point source.
With AERSCREEN, you can model flares (the F). The option to model a flare is not available in AERMOD as a distinct source type.

## Slide 9: Running AERSCREEN
The screen will clear and prompts for a point source are displayed—we will use physical parameters like values for one of the stacks modeled with AERMOD
Enter 500 for emission rate (in grams/second)
Enter 182.9 (meters) for the stack height
Enter 5.3 (meters) for the inside stack diameter
Enter 400 (kelvin) for exit temperature
Enter 1 for the option to enter the exit velocity in meters/second
Enter 20.0 (meters/second) for the exit velocity
Enter R for rural land use
Notes: As you are prompted by AERSCREEN, enter the values displayed for the associated parameters.
These should be self-explanatory.

## Slide 10: Running AERSCREEN
Enter 170 (meters) for the distance to ambient air
The next prompt is for NO2 chemistry; because we are not using the Ozone Limiting Model (OLM) nor Plume Volume Ratio Method (PVMRM), enter 1 (no chemistry)
Notes: If there is a question as to whether the area is considered rural or urban, you might need to perform an analysis on the surrounding land use. For guidance, see papers such as Auer, 1978 (“Correlation of Land Use and Cover with Meteorological Anomalies,” Journal of Applied Meteorology, 17, 636–643) and Section 7.2.1.1 of Appendix W ((Guideline on Air Quality Modeling), Federal Register Notice vol. 82, No. 10, January 17, 2017).
In the diagram that follows, the minimum distance from the source to the fence line is about 170 meters. This is our distance to ambient air.

## Slide 11: Running AERSCREEN—Buildings
The screen will clear, and you are prompted on whether to include building downwash—enter “Y” or “y” to include downwash
You are given the option to use a pre-existing BPIPPRM input file or enter the input via prompts; for this hands-on activity, we will be using the BPIPPRM “MC_BPIPPRM.inp” input file we created previously
Notes: We can only represent a single-tiered rectangular building, unless we run BPIPPRM outside of AERSCREEN and reference the BPIPPRM output file. Thus, for the purposes of this hands-on activity, we are only going to represent the bottom tier (Tier 1) as a demonstration of the AERSCREEN inputs.
You might want to separately try to figure out these parameters for the smaller, taller tier or re-run AERSCREEN using the BPIPPRM output file generated in the BPIPPRM hands-on activity.
If you remember, Tier 1 is 180 m × 90 m × 60 m high with the longer side oriented southwest-northeast. The stack is located on the southwest end of the building. (See next slide.)
Those dimensions are the first three building parameters.

## Slide 12: Structure Diagram—Bottom Tier
S
C
240°
65°
S = Stack
C = Building Center
N
Tier 1
N
Tier 2
Notes: This slide, similar to the slide shown the BPIPPRM presentation, illustrates the building we are representing in the AERSCREEN hands-on activity.
Two angles that are required as input:
  Maximum building dimension angle to true north (65 degrees), and
  Direction of the stack from building center (240 degrees).
The red “S” marks the approximate location of the stack, and the blue “C” marks the approximate center of Tier 1. Three dashed arrows originate from the center of the building. One points northward (0 degrees). Going in a clockwise direction, the second arrow is parallel to the building along the maximum dimension showing the longer side of the building is oriented at 65 degrees from north (#1). Continuing in a clockwise direction, the third arrow points toward the stack, which is 240 degrees from north (#2).
The distance from the stack to the center of the building is 90 meters.

## Slide 13: Running AERSCREEN—Terrain/Receptors/Source
The next prompt is whether to include terrain—respond with Y (Yes)
The next set of prompts define receptors and source location
  Maximum distance (in meters) to probe: the default value will depend on the application—we will use 10,000 meters
  Include up to 10 optional discrete receptors: N (No)
  Flagpole receptors: N (No)
  Source elevation: press the “Enter” key to let AERMAP derive the elevation
Notes: FLAT terrain is a non-default option in AERMOD (and therefore AERSCREEN). Unless the FLAT option can be justified, the effects of terrain should be included.
The maximum distance to probe matches the distance from the facility to the edge of our receptor boundary in the AERMOD example.
We will not model:
  Optional discrete receptors but could if we know the locations of sensitive populations, or
  Flagpole receptors.
The source elevation can be entered directly or derived from AERMAP (which AERSCREEN will run). We will let AERSCREEN derive the elevation.

## Slide 14: Running AERSCREEN—Terrain/Receptors/Source
  Coordinate type: Universal Transverse Mercator (UTM) coordinates
  Easting: 491020 meters
    Northing: 4516237 meters
    Zone: 18
    UTM datum: 4
Notes: For our example, we will not enter any discrete receptors. If you answer “Yes” to the prompt, you will be asked to provide the name of the file with the locations of the discrete receptors.
Nor will we use flagpole receptors.
Unless you know the elevation of your source, it is easiest to let AERMAP determine the source elevation. Although we have the elevation from our AERMOD modeling run, we will allow AERMAP to recompute it.
Because we are working in Universal Transverse Mercator (UTM) coordinates, respond with UTM coordinates, entered in meters, and the corresponding UTM zone.
The zone is important, because there are 60 zones around the world (6 degrees latitude for each) and the coordinates do repeat across the zones for a given longitude.
There are only two choices for the datum: 1 (for the 1927 North American Datum) and 4 (for the 1983 North American Datum).

## Slide 15: Running AERSCREEN Surface Characteristics, Meteorology & Concentrations
The next set of prompts is for meteorological input
  Minimum and maximum ambient temperature: accept the default values (250–310 kelvin) by pressing ENTER
  Minimum wind speed: accept the default value of 0.5 m/s
  Anemometer height: accept the default value of 10 meters
  There are three options for the surface characteristics—select option 2 (use the following slide to help in making you selection):
    You have a choice of 1 to 8 land use type. Check Exercise 3 to decide which land use type you will use – choose a land use type
    Next you will be asked about moisture Climatology: choose either average, moist, or dry
Notes: AERSCREEN runs a program called MAKEMET to develop the screening meteorology. Based on user responses, it will generate the files of hourly meteorology (SFC and PFL) needed by AERMOD.
Default minimum and maximum ambient temperatures are 250 kelvin (-10°F) to 310 kelvin (98°F). Minimum wind speed is 0.5 meter/second. Accept the default values.
The lowest level in the site-specific data is 10 meters.
For the three surface characteristics, we use an approximate average of the characteristics found in the AERMET Stage 3 run.

## Slide 16
Allentown Airport
(Google Earth)

## Slide 17: Running AERSCREEN—Additional Options
Adjust U* to address potential overpredictions under stable low wind conditions: N
Estimate concentrations if the condition of “inversion break-up fumigation” occurs: N
Estimate concentrations under conditions of shoreline fumigation: N
Turn on the debug option? If yes enter Y, if no press <enter>: Enter Y
Notes: AERSCREEN contains an option to adjust U* to address issues related to potential overpredictions under stable low wind conditions.
AERSCREEN will calculate fumigation due to inversion break-up and coastal fumigation for point sources with release heights (above ground level) 10 m or more in height. The fumigation equations are taken from SCREEN3 (U.S. EPA, 1995) and follow the methodology of Turner (1970).
The inputs to AERSCREEN.INP are:
Calculate inversion break-up fumigation (Y = calculate fumigation, N = do not calculate fumigation).
Calculate shoreline fumigation (Y = calculate fumigation, N = do not calculate fumigation).
Minimum distance to shoreline in meters (less than 3,000 m).
Optional direction to shoreline from source (0–360 degrees or -9 for no specified direction).
For shoreline fumigation, the user also enters the minimum distance to the shoreline from the source, and the user has the option to specify the direction from the source to the shoreline when using spatially varying surface characteristics for MAKEMET. This option allows AERSCREEN to use appropriate surface characteristics corresponding to the upwind direction from the source to shoreline. For the fumigation options, the source is considered rural, no downwash effects are included, and no terrain effects are included.
AERSCREEN allows for the option to output a debug file that contains all intermediate output from the stages of AERSCREEN (PROBE and FLOWSECTOR). See Section 3.5 and 3.6 of the AERSCREEN User’s Guide for further details. When fumigation options are selected, the debug option will also output the meteorological variables and iterations of the fumigation calculations.

## Slide 18: Running AERSCREEN—Output Filename
AERSCREEN prompts for the output filename
  Use any name or use the default aerscreen.out—for this exercise, use the default name
Notes: AERSCREEN prompts for the name of the output file or you can forego entering a name and press the “Enter” key to accept the default name “aerscreen.out.”

## Slide 19: Running AERSCREEN—Validation/Edit
After choosing the filename, a menu appears providing the categories of input data that can be examined and, if necessary, you can edit AERSCREEN’s input before it runs
The menu contains eight categories of input information from which to choose
Once you are satisfied with the input press enter to run AERSCREEN

## Slide 20: AERSCREEN—Output
Based on the responses to the prompts, AERSCREEN generated 296 (i.e., Pb=296) receptors along a single line out to 10 kms
To determine the max 1 hr concentration, the following # of concentrations were calculated using:
  296 receptor distances,
  36 directions
  650 met data combinations from MAKEMET - resulting in 2,670 hrs. resulting from:
    4 seasons
    3 Zo sectors
Therefore, the # of concentrations predicted were: 28,451,520

## Slide 21: AERSCREEN.LOG
** BUILDING DATA **
User defined BPIPPRM input file:
MC_bpipprm.inp
** TERRAIN DATA **
Input coordinates are UTM
Source Longitude: -75.10645 deg 491020. Easting
Source Latitude: 40.79708 deg 4516237. Northing
UTM Zone: 18 Reference Datum: 4 (NAD 83)
Source elevation will be determined by AERMAP
Probe distance: 10000. meters 32808. feet
No flagpole receptors
No discrete receptors used
** METEOROLOGY DATA **
Min/Max Temperature: 250.0 / 310.0 K -9.7 / 98.3 Deg F
Minimum Wind Speed: 0.5 m/s
Anemometer Height: 10.000 meters
Dominant Surface Profile: Cultivated Land
Dominant Climate Type: Average Moisture
Surface friction velocity (u*): not adjusted
Notes: Shown here are the first 20 or so lines and last 10 lines of the log file.
The log file consists of (not all shown here):
  The data validation that was displayed prior to AERSCREEN performing the calculations (shown above).
  Summary of the surface characteristics.
  Summary of the AERMAP run.
  AERMOD processing for each flow sector.
  Running AERMAP and AERMOD for the refined run for those receptors in the direction of the maximum concentration (a more refined receptor spacing).
  The number of receptors skipped (shown above).
  The date and time the run ended (shown above).

## Slide 22: AERSCREEN.LOG
SURFACE CHARACTERISTICS & MAKEMET
Obtaining surface characteristics...
Using AERMET seasonal surface characteristics for Cultivated Land with Average Moisture
Season Albedo Bo zo
Winter 0.60 1.50 0.010
Spring 0.14 0.30 0.030
Summer 0.20 0.50 0.200
Autumn 0.18 0.70 0.050
Creating met files aerscreen_01_01.sfc & aerscreen_01_01.pfl
Creating met files aerscreen_02_01.sfc & aerscreen_02_01.pfl
Creating met files aerscreen_03_01.sfc & aerscreen_03_01.pfl
Creating met files aerscreen_04_01.sfc & aerscreen_04_01.pfl
Notes: Shown here are the first 20 or so lines and last 10 lines of the log file.
The log file consists of (not all shown here):
  The data validation that was displayed prior to AERSCREEN performing the calculations (shown above).
  Summary of the surface characteristics.
  Summary of the AERMAP run.
  AERMOD processing for each flow sector.
  Running AERMAP and AERMOD for the refined run for those receptors in the direction of the maximum concentration (a more refined receptor spacing).
  The number of receptors skipped (shown above).
  The date and time the run ended (shown above).

## Slide 23: AERSCREEN.OUT
AERSCREEN 21112 / AERMOD 24142 05/19/25
15:04:05
TITLE: Option_1_run
-----------------------------------------------------------------------------
***************************** STACK PARAMETERS ****************************
-----------------------------------------------------------------------------
SOURCE EMISSION RATE: 500.0000 g/s 3968.254 lb/hr
STACK HEIGHT: 182.90 meters 600.07 feet
STACK INNER DIAMETER: 5.300 meters 208.66 inches
PLUME EXIT TEMPERATURE: 400.0 K 260.3 Deg F
PLUME EXIT VELOCITY: 20.000 m/s 65.62 ft/s
STACK AIR FLOW RATE: 934931 ACFM
STACK BASE LONGITUDE: -75.1065 deg 491020. Easting
STACK BASE LATITUDE: 40.7971 deg 4516237. Northing
STACK BASE UTM ZONE: 18
REFERENCE DATUM (NADA): 4
STACK BASE ELEVATION: 71.53 meters 234.68 feet
RURAL OR URBAN: RURAL
DIGITAL ELEVATION MAP(S) ..\..\AERMAP\Seamless_Dem\MC_NED_76_1deg_NC.tiff
..\..\AERMAP\Seamless_Dem\MC_NED_75_1deg_NC.tiff
INITIAL PROBE DISTANCE = 10000. meters 32808. feet
Notes: The file AERSCREEN.OUT (recall we opted to use the default filename) contains the following:
  Stack parameters (because we modeled a point source).
  Urban/Rural.
  Digital elevation files.
  Probe distance.
(Continued on the next slide)

## Slide 24: AERSCREEN.OUT
-----------------------------------------------------------------------------
*********************** BUILDING DOWNWASH PARAMETERS **********************
-----------------------------------------------------------------------------
USER DEFINED BPIPPRM INPUT FILE: MC_bpipprm.inp
MAXIMUM BUILDING HEIGHT: 100.0 meters 328.1 feet
MAXIMUM BUILDING LENGTH: 199.7 meters 655.3 feet
MINIMUM BUILDING WIDTH: 64.6 meters 211.8 feet
Notes: The file AERSCREEN.OUT (cont'd)
  Building downwash parameters.
(Continued on the next slide)

## Slide 25: AERSCREEN.OUT
************************** FLOW SECTOR ANALYSIS ***************************
25 meter receptor spacing: 170. meters - 5000. meters
50 meter receptor spacing: 5050. meters - 10000. meters
-----------------------------------------------------------------------------
MAXIMUM IMPACT RECEPTOR
FLOW BUILD BUILD 1-HR CONC DIST HEIGHT TEMPORAL
SECTOR WIDTH LENGTH XBADJ YBADJ (ug/m3) (m) (m) PERIOD
----------------------------------------------------------------------------------
10 91.14 95.65 49.56 -95.81 527.3 2825.0 37.90 WIN
20 91.14 99.05 62.96 -77.45 527.0 2825.0 32.48 WIN
30 91.14 99.43 74.46 -56.74 526.2 2825.0 13.39 WIN
40 87.23 96.79 83.69 -34.31 526.5 2825.0 22.75 WIN
50 77.06 91.21 90.38 -10.83 526.6 2825.0 24.58 WIN
60 64.55 82.86 94.32 12.97 526.8 2825.0 28.74 WIN
70 68.89 87.72 87.77 36.59 526.8 2800.0 29.61 WIN
80 80.34 95.08 75.78 58.85 527.0 2850.0 34.49 WIN
90 89.36 99.56 61.47 79.32 918.4 4375.0 229.60 WIN
100 179.22 199.74 -35.04 55.60 1504. 3950.0 261.80 WIN
110 191.99 190.42 -41.02 66.02 1225. 4950.0 278.59 WIN
120 198.93 175.30 -45.75 74.42 1479. 3475.0 258.06 WIN
130 199.82 154.86 -49.09 80.57 1740. 3250.0 271.90 WIN
140* 194.65 129.72 -50.94 84.27 2134. 2975.0 286.35 WIN
150 183.56 100.63 -51.24 85.40 1998. 3025.0 255.47 WIN
160 191.10 110.59 -71.03 83.95 1577. 3475.0 250.12 WIN
170 200.09 137.89 -99.02 79.94 1153. 4000.0 227.21 WIN
180 203.00 161.00 -124.00 73.50 603.6 5700.0 204.97 WIN
190 91.14 95.65 -145.21 95.81 623.8 7700.0 242.82 WIN
200 91.14 99.05 -162.01 77.45 526.1 2825.0 6.14 WIN
210 91.14 99.43 -173.89 56.74 526.6 2825.0 26.00 WIN
220 87.23 96.79 -180.48 34.31 524.9 2700.0 0.38 WIN
230 77.06 91.21 -181.59 10.83 526.4 2825.0 20.64 WIN
240 64.55 82.86 -177.18 -12.97 527.4 2825.0 39.59 WIN
250 68.89 87.72 -175.49 -36.59 526.5 2825.0 23.41 WIN
260 80.34 95.08 -170.86 -58.85 526.7 2825.0 26.71 WIN
270 89.36 99.56 -161.03 -79.32 526.9 2825.0 31.92 WIN
280 179.22 199.74 -164.70 -55.60 528.1 2850.0 49.06 WIN
290 191.99 190.42 -149.40 -66.02 532.8 2850.0 88.55 WIN
300 198.93 175.30 -129.55 -74.42 537.2 2900.0 119.74 WIN
310 199.82 154.86 -105.78 -80.57 531.0 2850.0 75.79 WIN
320 194.65 129.72 -78.78 -84.27 532.1 2925.0 92.13 WIN
330 183.56 100.63 -49.39 -85.40 527.8 2775.0 45.20 WIN
340 191.10 110.59 -39.56 -83.95 532.6 2900.0 92.46 WIN
350 200.09 137.89 -38.87 -79.94 533.1 2850.0 90.24 WIN
360 203.00 161.00 -37.00 -73.50 530.9 2850.0 75.38 WIN
* = worst case flow sector

## Slide 26: AERSCREEN.OUT
-----------------------------------------------------------------------------
********************** MAKEMET METEOROLOGY PARAMETERS *********************
-----------------------------------------------------------------------------
MIN/MAX TEMPERATURE: 250.0 / 310.0 (K)
MINIMUM WIND SPEED: 0.5 m/s
ANEMOMETER HEIGHT: 10.000 meters
SURFACE CHARACTERISTICS INPUT: AERMET SEASONAL TABLES
DOMINANT SURFACE PROFILE: Cultivated Land
DOMINANT CLIMATE TYPE: Average Moisture
DOMINANT SEASON: Winter
ALBEDO: 0.60
BOWEN RATIO: 1.50
ROUGHNESS LENGTH: 0.010 (meters)
SURFACE FRICTION VELOCITY (U*) NOT ADUSTED Continued on next slide

## Slide 27: AERSCREEN.OUT
METEOROLOGY CONDITIONS USED TO PREDICT OVERALL MAXIMUM IMPACT
-------------------------------------------------------------
YR MO DY JDY HR
-- -- -- --- --
10 04 25 25 01
H0 U* W* DT/DZ ZICNV ZIMCH M-O LEN Z0 BOWEN ALBEDO REF WS
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
-3.99 0.058 -9.000 0.020 -999. 160. 4.6 0.010 1.50 0.60 2.00
HT REF TA HT
- - - - - - - - - - -
10.0 310.0 2.0
WIND SPEED AT STACK HEIGHT (non-downwash): 3.9 m/s
STACK-TIP DOWNWASH ADJUSTED STACK HEIGHT: 182.9 meters
ESTIMATED FINAL PLUME RISE (non-downwash): 91.3 meters
ESTIMATED FINAL PLUME HEIGHT (non-downwash): 274.2 meters
********************** AERSCREEN MAXIMUM IMPACT SUMMARY *********************
-----------------------------------------------------------------------------
MAXIMUM SCALED SCALED SCALED SCALED
1-HOUR 3-HOUR 8-HOUR 24-HOUR ANNUAL
CALCULATION CONC CONC CONC CONC CONC
PROCEDURE (ug/m3) (ug/m3) (ug/m3) (ug/m3) (ug/m3)
--------------- ---------- ---------- ---------- ---------- ----------
ELEVATED TERRAIN 2135. 2135. 1921. 1281. 213.5
DISTANCE FROM SOURCE 2970.00 meters directed toward 140 degrees
RECEPTOR HEIGHT 285.40 meters

## Slide 28: AERSCREEN to 5yr-AERMOD Prediction Comparison Option_1_run (Cultivated Land – Ave Moisture Climatology Selected)
Averaging Time | AERSCREEN (µg/m3) | AERMOD (µg/m3) | AERSCREEN/ AERMOD
1-hour | 2134* | 1225+ | 1.7
3-hour | 2134 | 711 | 3.0
24-hour | 1280 | 142 | 9.0
Annual | 213 | 16.5 | 13.0
* 1-hour Max screening concentration
+ High 4th High averaged over 5 years – Probabilistic Std.

## Slide 29: Running AERSCREEN Option_2
To use the restart option AERSCREEN looks for the file aerscreen.inp
This file was created only because we selected the default AERSCREEN output filename (aerscreen.out)
The file aerscreen.inp has been added to the directory ..\Option_2_run
Go to directory Option_2_run
Double click on aerscreen_21112.exe
Since the file aerscreen.inp is in the directory, AERSCREEN asks if you want to use the restart file – enter Y
Now you are given the option of changing inputs for the Option_2_run
In our case we will change only two inputs
Notes: You can restart (or rerun) AERMOD without having to walk through each of the prompts by using the restart file, aerscreen.inp. The restart only works with a filename of aerscreen.inp. If you entered something other than accepting the default, for example MyTest.out, then AERSCREEN will not ask if you want to use the restart file, unless …
You can, however, copy or rename the filename to aerscreen.inp and run AERSCREEN to use the restart option.
This option can be useful if you only want to change one or two parameters to see the effect on the output. If you are doing this, be careful not to overwrite output from previous runs you intended to keep.
The first part of AERSCREEN.INP is shown next, followed by the prompt to use the restart option. If you use the restart option, the validation screen is displayed, allowing you to make changes to one or more parameters. The options to change a stack parameter are shown after the restart prompt.

## Slide 30: Option_2_run of AERSCREEN— Use of Output from AERSURFACE
To accomplish this, we will use AERSCREEN’s restart option.
All files needed to run the 2nd option have been placed into a separate directory (..\Option_2_run)
Double click on the AERSCREEN executable
It will prompt you to enter either restart or start a new run
Type y to restart
Select 6 to change Title : Option_2_run
Then type 4 to change meteorological data
Select 6 to use the output from AERSURFACE
Select Opt 3 and enter the AERSURFACE output file name (KABE_2011_Imp_Can.sfc)
Hit Enter twice to run AERSCREEN
Notes: AERSCREEN runs a program called MAKEMET to develop the screening meteorology. Based on user responses, it will generate the files of hourly meteorology (SFC and PFL) needed by AERMOD.
Default minimum and maximum ambient temperatures are 250 kelvin (-10°F) to 310 kelvin (98°F). Minimum wind speed is 0.5 meter/second. Accept the default values.
The lowest level in the site-specific data is 10 meters.
For the three surface characteristics, we use an approximate average of the characteristics found in the AERMET Stage 3 run.

## Slide 31: AERSCREEN—Output
As with the first run, AERSCREEN generated 296 receptors along a single line out to 10 kms
To determine the max 1 hr concentration, the following # of concentrations were calculated using:
  296 receptor distances,
  36 directions
  641 met data combinations from MAKEMET - resulting in ≈ 92,304 hrs. resulting from:
    12 months
    12 Zo sectors
Therefore, the # of concentrations predicted were: 983,591,424

## Slide 32: AERSCREEN.LOG
** BUILDING DATA **
User defined BPIPPRM input file:
MC_BPIPPRM.INP
** TERRAIN DATA **
Input coordinates are UTM
Source Longitude: -75.10645 deg 491020. Easting
Source Latitude: 40.79708 deg 4516237. Northing
UTM Zone: 18 Reference Datum: 4 (NAD 83)
Source elevation will be determined by AERMAP
Probe distance: 10000. meters 32808. feet
Probe distance: 10000. meters 32808. feet
No flagpole receptors
No discrete receptors used
** METEOROLOGY DATA **
Min/Max Temperature: 250.0 / 310.0 K -9.7 / 98.3 Deg F
Minimum Wind Speed: 0.5 m/s
Anemometer Height: 10.000 meters
Using surface characteristics in file:
KABE_2011_Imp_Can.sfc
Surface friction velocity (u*): not adjusted
Notes: Shown here are the first 20 or so lines and last 10 lines of the log file.
The log file consists of (not all shown here):
  The data validation that was displayed prior to AERSCREEN performing the calculations (shown above).
  Summary of the surface characteristics.
  Summary of the AERMAP run.
  AERMOD processing for each flow sector.
  Running AERMAP and AERMOD for the refined run for those receptors in the direction of the maximum concentration (a more refined receptor spacing).
  The number of receptors skipped (shown above).
  The date and time the run ended (shown above).

## Slide 33: AERSCREEN.LOG
SURFACE CHARACTERISTICS & MAKEMET
Obtaining surface characteristics...
Using monthly surface characteristics for 3 spatial sector(s)
Sector Start End
1 60 235
2 235 320
3 320 60
Month Sector Albedo Bo zo
January 1 0.18 0.90 0.025
January 2 0.18 0.90 0.015
January 3 0.18 0.90 0.018
February 1 0.47 0.49 0.017
February 2 0.47 0.49 0.009
February 3 0.47 0.49 0.011
March 1 0.47 0.49 0.017
March 2 0.47 0.49 0.009
March 3 0.47 0.49 0.011
.
.
.
.
September 1 0.17 0.67 0.036
September 2 0.17 0.67 0.027
September 3 0.17 0.67 0.029
October 1 0.18 0.90 0.025
October 2 0.18 0.90 0.015
October 3 0.18 0.90 0.018
November 1 0.18 0.90 0.025
November 2 0.18 0.90 0.015
November 3 0.18 0.90 0.018
December 1 0.18 0.90 0.025
December 2 0.18 0.90 0.015
December 3 0.18 0.90 0.018
Notes: Shown here are the first 20 or so lines and last 10 lines of the log file.
The log file consists of (not all shown here):
  The data validation that was displayed prior to AERSCREEN performing the calculations (shown above).
  Summary of the surface characteristics.
  Summary of the AERMAP run.
  AERMOD processing for each flow sector.
  Running AERMAP and AERMOD for the refined run for those receptors in the direction of the maximum concentration (a more refined receptor spacing).
  The number of receptors skipped (shown above).
  The date and time the run ended (shown above).

## Slide 34: AERSCREEN.LOG
Creating met files aerscreen_01_01.sfc & aerscreen_01_01.pfl
Creating met files aerscreen_01_02.sfc & aerscreen_01_02.pfl
Creating met files aerscreen_01_03.sfc & aerscreen_01_03.pfl
Creating met files aerscreen_02_01.sfc & aerscreen_02_01.pfl
Creating met files aerscreen_02_02.sfc & aerscreen_02_02.pfl
Creating met files aerscreen_02_03.sfc & aerscreen_02_03.pfl
Creating met files aerscreen_03_01.sfc & aerscreen_03_01.pfl
Creating met files aerscreen_03_02.sfc & aerscreen_03_02.pfl
Creating met files aerscreen_03_03.sfc & aerscreen_03_03.pfl
.
.
.
Creating met files aerscreen_10_01.sfc & aerscreen_10_01.pfl
Creating met files aerscreen_10_02.sfc & aerscreen_10_02.pfl
Creating met files aerscreen_10_03.sfc & aerscreen_10_03.pfl
Creating met files aerscreen_11_01.sfc & aerscreen_11_01.pfl
Creating met files aerscreen_11_02.sfc & aerscreen_11_02.pfl
Creating met files aerscreen_11_03.sfc & aerscreen_11_03.pfl
Creating met files aerscreen_12_01.sfc & aerscreen_12_01.pfl
Creating met files aerscreen_12_02.sfc & aerscreen_12_02.pfl
Creating met files aerscreen_12_03.sfc & aerscreen_12_03.pfl
Notes: Shown here are the first 20 or so lines and last 10 lines of the log file.
The log file consists of (not all shown here):
  The data validation that was displayed prior to AERSCREEN performing the calculations (shown above).
  Summary of the surface characteristics.
  Summary of the AERMAP run.
  AERMOD processing for each flow sector.
  Running AERMAP and AERMOD for the refined run for those receptors in the direction of the maximum concentration (a more refined receptor spacing).
  The number of receptors skipped (shown above).
  The date and time the run ended (shown above).

## Slide 35: AERSCREEN.OUT
AERSCREEN 21112 / AERMOD 24142 05/20/25
06:29:07
TITLE: Option_2_run
-----------------------------------------------------------------------------
***************************** STACK PARAMETERS ****************************
-----------------------------------------------------------------------------
SOURCE EMISSION RATE: 500.0000 g/s 3968.254 lb/hr
STACK HEIGHT: 182.90 meters 600.07 feet
STACK INNER DIAMETER: 5.300 meters 208.66 inches
PLUME EXIT TEMPERATURE: 400.0 K 260.3 Deg F
PLUME EXIT VELOCITY: 20.000 m/s 65.62 ft/s
STACK AIR FLOW RATE: 934931 ACFM
STACK BASE LONGITUDE: -75.1065 deg 491020. Easting
STACK BASE LATITUDE: 40.7971 deg 4516237. Northing
STACK BASE UTM ZONE: 18
REFERENCE DATUM (NADA): 4
STACK BASE ELEVATION: 71.53 meters 234.68 feet
RURAL OR URBAN: RURAL
DIGITAL ELEVATION MAP(S) ..\..\AERMAP\Seamless_Dem\MC_NED_76_1deg_NC.tiff
..\..\AERMAP\Seamless_Dem\MC_NED_75_1deg_NC.tiff
INITIAL PROBE DISTANCE = 10000. meters 32808. feet
Notes: The file AERSCREEN.OUT (recall we opted to use the default filename) contains the following:
  Stack parameters (because we modeled a point source).
  Urban/Rural.
  Digital elevation files.
  Probe distance.
(Continued on the next slide)

## Slide 36: AERSCREEN.OUT
-----------------------------------------------------------------------------
*********************** BUILDING DOWNWASH PARAMETERS **********************
-----------------------------------------------------------------------------
USER DEFINED BPIPPRM INPUT FILE: MC_bpipprm.inp
MAXIMUM BUILDING HEIGHT: 100.0 meters 328.1 feet
MAXIMUM BUILDING LENGTH: 199.7 meters 655.3 feet
MINIMUM BUILDING WIDTH: 64.6 meters 211.8 feet
Notes: The file AERSCREEN.OUT (cont'd)
  Building downwash parameters.
(Continued on the next slide)

## Slide 37: AERSCREEN.OUT
-----------------------------------------------------------------------------
************************** FLOW SECTOR ANALYSIS ***************************
25 meter receptor spacing: 170. meters - 5000. meters
50 meter receptor spacing: 5050. meters - 10000. meters
-----------------------------------------------------------------------------
MAXIMUM IMPACT RECEPTOR
FLOW BUILD BUILD 1-HR CONC DIST HEIGHT TEMPORAL
SECTOR WIDTH LENGTH XBADJ YBADJ (ug/m3) (m) (m) PERIOD
----------------------------------------------------------------------------------
10 91.14 95.65 49.56 -95.81 542.7 2500.0 35.77 JAN
20 91.14 99.05 62.96 -77.45 542.6 2525.0 33.97 JAN
30 91.14 99.43 74.46 -56.74 541.5 2550.0 11.53 JAN
40 87.23 96.79 83.69 -34.31 541.9 2525.0 21.63 JAN
50 77.06 91.21 90.38 -10.83 542.2 2525.0 27.28 JAN
60 64.55 82.86 94.32 12.97 555.8 2525.0 26.90 JAN
70 68.89 87.72 87.77 36.59 556.0 2525.0 30.73 JAN
80 80.34 95.08 75.78 58.85 555.9 2525.0 29.06 JAN
90 89.36 99.56 61.47 79.32 927.5 4375.0 229.60 APR
100 179.22 199.74 -35.04 55.60 1552. 4225.0 285.64 JAN
110 191.99 190.42 -41.02 66.02 1242. 4750.0 268.01 JAN
120 198.93 175.30 -45.75 74.42 1490. 3475.0 258.06 FEB
130 199.82 154.86 -49.09 80.57 1759. 3200.0 269.70 JAN
140* 194.65 129.72 -50.94 84.27 2160. 2975.0 286.35 FEB
150 183.56 100.63 -51.24 85.40 1973. 3050.0 258.05 APR
160 191.10 110.59 -71.03 83.95 1572. 3475.0 250.12 FEB
170 200.09 137.89 -99.02 79.94 1144. 4000.0 227.21 FEB
180 203.00 161.00 -124.00 73.50 617.7 5700.0 204.97 APR
190 91.14 95.65 -145.21 95.81 623.5 7700.0 242.82 FEB
200 91.14 99.05 -162.01 77.45 550.6 2500.0 21.06 JAN
210 91.14 99.43 -173.89 56.74 550.9 2525.0 25.70 JAN
220 87.23 96.79 -180.48 34.31 550.2 2525.0 1.02 JAN
230 77.06 91.21 -181.59 10.83 550.6 2525.0 20.59 JAN
240 64.55 82.86 -177.18 -12.97 542.0 2550.0 25.51 JAN
250 68.89 87.72 -175.49 -36.59 542.0 2525.0 24.20 JAN
260 80.34 95.08 -170.86 -58.85 542.3 2525.0 29.98 JAN
270 89.36 99.56 -161.03 -79.32 542.2 2525.0 28.21 JAN
280 179.22 199.74 -164.70 -55.60 542.5 2525.0 32.59 JAN
290 191.99 190.42 -149.40 -66.02 543.5 2550.0 45.01 JAN
300 198.93 175.30 -129.55 -74.42 544.3 2725.0 81.50 JAN
310 199.82 154.86 -105.78 -80.57 543.1 2550.0 41.02 JAN
320 194.65 129.72 -78.78 -84.27 542.9 2525.0 37.84 JAN
330 183.56 100.63 -49.39 -85.40 543.1 2525.0 40.58 JAN
340 191.10 110.59 -39.56 -83.95 544.0 2550.0 50.76 JAN
350 200.09 137.89 -38.87 -79.94 544.5 2550.0 54.98 JAN
360 203.00 161.00 -37.00 -73.50 545.5 2525.0 62.27 JAN
* = worst case flow sector
Notes: AERSCREEN.OUT (cont'd)
Meteorological parameters used by MAKEMET.
Meteorological conditions associated with the overall maximum impact.
(Continued on the next slide)

## Slide 38: AERSCREEN.OUT
-----------------------------------------------------------------------------
********************** MAKEMET METEOROLOGY PARAMETERS *********************
-----------------------------------------------------------------------------
MIN/MAX TEMPERATURE: 250.0 / 310.0 (K)
MINIMUM WIND SPEED: 0.5 m/s
ANEMOMETER HEIGHT: 10.000 meters
SURFACE CHARACTERISTICS INPUT: KABE_2011_Imp_Can.sfc
DOMINANT SECTOR: 3 (320 60)
DOMINANT MONTH: February
ALBEDO: 0.47
BOWEN RATIO: 0.49
ROUGHNESS LENGTH: 0.011 (meters)
SURFACE FRICTION VELOCITY (U*) NOT ADUSTED Continued on next slide
Notes: AERSCREEN.OUT (cont'd)
Meteorological parameters used by MAKEMET.
Meteorological conditions associated with the overall maximum impact.
(Continued on the next slide)

## Slide 39: AERSCREEN.OUT
METEOROLOGY CONDITIONS USED TO PREDICT OVERALL MAXIMUM IMPACT
-------------------------------------------------------------
YR MO DY JDY HR
-- -- -- --- --
10 04 24 24 01
H0 U* W* DT/DZ ZICNV ZIMCH M-O LEN Z0 BOWEN ALBEDO REF WS
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
-4.08 0.059 -9.000 0.020 -999. 164. 4.7 0.011 0.49 0.47 2.00
HT REF TA HT
- - - - - - - - - - -
10.0 310.0 2.0
WIND SPEED AT STACK HEIGHT (non-downwash): 3.9 m/s
STACK-TIP DOWNWASH ADJUSTED STACK HEIGHT: 182.9 meters
ESTIMATED FINAL PLUME RISE (non-downwash): 90.3 meters
ESTIMATED FINAL PLUME HEIGHT (non-downwash): 273.2 meters
-----------------------------------------------------------------------------
********************** AERSCREEN MAXIMUM IMPACT SUMMARY *********************
-----------------------------------------------------------------------------
MAXIMUM SCALED SCALED SCALED SCALED
1-HOUR 3-HOUR 8-HOUR 24-HOUR ANNUAL
CALCULATION CONC CONC CONC CONC CONC
PROCEDURE (ug/m3) (ug/m3) (ug/m3) (ug/m3) (ug/m3)
--------------- ---------- ---------- ---------- ---------- ----------
ELEVATED TERRAIN 2166. 2166. 1949. 1300. 216.6
DISTANCE FROM SOURCE 2965.00 meters directed toward 140 degrees
RECEPTOR HEIGHT 284.40 meters
Notes: AERSCREEN.OUT (cont'd)
Meteorological conditions used to predict Boundary Impacts.
(Continued on the next slide)

## Slide 40: AERSCREEN to 5yr-AERMOD Prediction Comparison Using Opt. 3 Surface Chara. (Cultivated Land – Ave Moisture Climatology Selected)
Averaging Time | AERSCREEN (µg/m3) | AERMOD (µg/m3) | AERSCREEN/ AERMOD
1-hour | 2166* | 1225+ | 1.8
3-hour | 2166 | 711 | 3.0
24-hour | 1300 | 142 | 9.2
Annual | 216.6 | 16.5 | 13.1
* 1-hour Max screening concentration
+ High 4th High averaged over 5 years – Probabilistic Std.
Notes: AERMET and AERMOD were rerun using the same values that were input to AERSCREEN, e.g., the surface characteristics and the single point source parameters. The table shows the high-first-high for AERMOD concentration estimates. As we can see in the last column, AERSCREEN’s results are from a factor of 2 to 22 higher for our example.
If AERSCREEN modeling demonstrates that the screening results show compliance with ambient air quality standards, can you stop and skip refined modeling with AERMOD? Possibly, but it will depend on the application and what the regulatory agency requires.

## Slide 41: Next Exercise 6