## Slide 1: EXERCISE 6
Course: MODL 301
Air Pollution Dispersion Models:
Applications with the AERMOD Modeling System
Notes: Model runs are in AERSURFACE\MC\Day 3 Assignment
And In AERMET\1-yr_Onsite\Day 3 Assingment

## Slide 2: Exercise 6
Run AERSCREEN on the Sec-3_run and compare the results to the actual Sec-3 AERMOD run.
  Using AERSCREEN’s restart from the Option_1_run, change those parameters that are needed to replicate the Sec-3 case.
  The procedure for accomplishing this is as follows:
    In the ..\AESCREEN directory you will find the ..\Exercise_6 sub-directory
    All the files you need to run Exercise_6 as a restart of the Option_1_run have been copied to ..\Exercise_6. These files are: All executable files plus: aerscreen.inp; conus.las; conus.los; demlist.txt & MC_bpipprm.inp from the ..\Option_1_run to ..\Exercise_6
    Double click on the AERSCREEN executable and select restart

## Slide 3: Exercise 6
    Change the following source data to replicate the Sec-3 AERMOD run:
      Emission rate = 100 g/s
      Stack height = 100 m
      Stack gas temperature = 416 K
      Exit gas velocity = 18.8 m/s
      Inside stack diameter = 4.6 m
    No Building Downwash
    No Terrain
    Change surface characteristics from the Allentown Airport to the area surrounding Martins Creek
      For selecting surface characteristics in AERSCREEN choose Opt 2 (monthly tables form AERMET)

## Slide 4: Exercise 6
      Determine what land use category and moisture level you should choose from the Land-Use tables. The albedo, Bowen ratio & Zo, that best represents the area around the MC Met tower, are selected from 1 of 8 categories and 1 of 3 moisture levels.
      To determine which category and moisture level to choose, compare the surface characteristics found in "MC_surface.sfc" to the values in the tables.
      These tables come from the AERMET User's Guide and can be found in the file ..\Surface Characteristics Tables from the AERMET User.docx that is supplies in the Exercise_6 sub-directory.

## Slide 5: Exercise 6
Once you have completed the run
  Compare the 1, 3, 24 and annual averaged calculated by AERMOD in the Sec-3_run to those estimated by AERSCREEN.
  Were the AERSCREEN results conservative?
  If so, how many times higher were the AERSCREEN results?

## Slide 6: Comparison of Sec-3 Results From AERMOD To The Sec-3 Results From AERSCREEN
Averaging Time | AERSCREEN (µg/m3) | AERMOD (µg/m3) | AERSCREEN/ AERMOD
1-hour |  |  | 
3-hour |  |  | 
24-hour |  |  | 
Annual |  |  | 
Notes: AERMET and AERMOD were rerun using the same values that were input to AERSCREEN, e.g., the surface characteristics and the single point source parameters. The table shows the high-first-high for AERMOD concentration estimates. As we can see in the last column, AERSCREEN’s results are from a factor of 2 to 22 higher for our example.
If AERSCREEN modeling demonstrates that the screening results show compliance with ambient air quality standards, can you stop and skip refined modeling with AERMOD? Possibly, but it will depend on the application and what the regulatory agency requires.