## Slide 1: State Implementation Plan
101
vr 1a

## Slide 2: Tell us about yourself!
Name
Organization
How long have you been in Air Quality and/or working on SIPs?

## Slide 3: Goals of the Class
Understanding of what a State Implementation Plan is
Your role
The steps and various information that goes in a plan – the who, what, when, where and why!

## Slide 4: Agenda
Welcome, Logistics and Introductions
Details we won’t cover
  Clean Air Act/National Ambient Air Quality Standards (NAAQS) - detail
  Area designation processes – detail
What we will cover
  Overview of SIPs
  Types of SIPs
  SIP components
    State and EPA staff and roles and responsibilities
    Technical data needed
  SIP Preparation and Submittal
What happens after a SIP is submitted to EPA
Resources
Debrief

## Slide 5: Overview
Overview

## Slide 6: What is a State Implementation Plan
State Implementation Plans from Terms of Environment
  EPA approved state plans for the establishment, regulation, and enforcement of air pollution standards.
Purpose
  A plan that is designed by a state to implement and meet federal Clean Air Act requirements.
Commitments
  The plan documents the State/Local/Tribal commitments to implement programs and controls.
Legally Binding
  The commitments and controls committed to within the plan must be enforceable.
Where can you find federally approved plans?
  (demo) https://www.epa.gov/air-quality-implementation-plans/approved-air-quality-implementation-plans
Overview

## Slide 7: Interesting Tidbits
Original SIPs were approved by EPA
  all 50 states, 4 U.S. Territories, and Washington D.C.
  May 31, 1972 (37 FR 10842) –also known as the “mother” SIPs.
Technically, all SIPs after 1972 are SIP revisions.
Overview

## Slide 8: SIP starting points
Current Reference(s):
CFR 40, Parts 51 and 52
CAA Title I, Part A, Sec. 110 (Implementation plans)
CAA Title I, Part D, Sec. 171-192(Plan Requirements for Nonattainment Areas)
  https://www.epa.gov/clean-air-act-overview/clean-air-act-text
  https://www.epa.gov/environmental-topics/air-topics
  https://www.epa.gov/air-research
  https://www.epa.gov/air-quality-implementation-plans
Overview

## Slide 9: Triggers for SIPs or SIP amendments
Depends on type of SIP (different types to be discussed later)
New or revised NAAQS/call for designations
New or revised federal requirements/programs
Local programs/areas - update emissions, update models
Commitments in current SIP
Overview

## Slide 10: Reminder about Designation Definitions
Attainment
  Area that meets the NAAQS
Nonattainment
  Area that does not meet primary and secondary NAAQS for a specific pollutant
Unclassifiable
  Area with insufficient data to determine the status for that area
Overview

## Slide 11: Just a reminder – Nonattainment Classifications
Ozone
  Marginal
  Moderate
  Serious
  Severe
  Extreme
Carbon Monoxide (CO) and PM2.5
  Moderate
  Serious
PM10
  All nonattainment areas originally Moderate
  If missed attainment deadline, reclassified as Serious
Other NAAQS (Lead, SO2)
  Nonattainment
Overview

## Slide 12: How designations are done for new nonattainment areas - simplified
Monitoring Data
  All monitoring data is uploaded to EPA: https://www.epa.gov/aqs
  Exceptional Events are important to document - data waived for classification purposes if EPA approves exceptional event determination
Area Boundaries
  States make recommendations on classifications throughout the state including potential nonattainment boundaries - EPA determines final classifications and boundaries for nonattainment areas
  EPA often relies on jurisdictional boundaries for nonattainment - counties very large in western states
  Data will be needed if smaller size area is warranted/needed - takes time to gather
Overview

## Slide 13: Timelines/Clocks
Clean Air Act sets timelines by pollutant
Can have overlapping timelines if more than one pollutant involved
  Changing standards increases complexity
Overview

## Slide 14: Due Date Timeframes – Infrastructure SIP
Program | Infrastructure SIP Due | Due Date to EPA | Attainment
Criteria Pollutant | Promulgation of NAAQS + 3 years | Designation date + 18 - 48 months | Designation date + up to 5 (or more) years
Regional Haze | n/a | 2008, 2021 and 2028 and every 10 years after (reasonable progress demos) | 2064 (natural conditions)
Exceptional Events Plan | n/a | Prior to attainment deadline | n/a
Ozone (and PM2.5) Advance Plan | n/a | Prior to nonattainment designation | n/a
Overview

## Slide 15: Best chance for success – Time Management: keeping track, managing, and communicating
Understanding both state and federal timelines and processes
Tools for calculating (demonstration - example tool)
What can you do with the time you have available
Key: Communicating your timeframes (within and without)
Overview

## Slide 16: Consequences of not doing a SIP or EPA not approving a SIP
Clean Air Act and EPA rules have specific consequences for failure to meet its requirements, depending on the type of SIP
Consequences usually 'kick in' upon failure to comply with an EPA action
  Ex: 2 to 1 emission offsets; 18 months after EPA issues failure to submit
  Ex: Federal Highway Fund sanctions; 6 months after date of offset sanctions
  Ex: Federal Implementation Plan (FIP); 2 years after EPA determines a failure to submit or disapproves a SIP
    More on FIPs in SIP Submittal Section
Overview

## Slide 17: Misc. or on-going issues with SIPs in general
Exceptional events demonstrations can waive data from designation/attainment (can’t meet attainment)
  https://www.epa.gov/air-quality-analysis/final-2016-exceptional-events-rule-supporting-guidance-documents-updated-faqs
Exceptional Event Demonstration and Mitigation Plan
  Currently applicable to Ozone and PM.
  Provides that states can demonstrate that monitoring values that contributed to a violation of the NAAQS could not have been avoided.
  Result from unusual or naturally occurring events that cannot be reasonably controlled.
    Ex: fireworks, volcanic eruptions, wildfires, natural dust
  If EPA concurs with the state’s argument/demonstration, the monitoring values are removed from the calculation to determine attainment.
Overview

## Slide 18: Relief from Nonattainment SIPs
Advance Program
  Applies in Ozone and PM2.5 Attainment Areas
  Provides a tool for working with communities to put into place actions/programs that can help avoid a nonattainment designation
  www.epa.gov/advance
Overview

## Slide 19: Relief from Nonattainment SIPs
Clean Data Finding
  When a nonattainment area monitors attainment prior to the SIP submittal deadline or the CAA deadline.
    Three years of violation-free monitored data required.
  Finding may be initiated via state request or EPA initiation.
  Relieves the state from some SIP requirements, such as Reasonable Further Progress (RFP) and Attainment Demonstration.
  Area retains a nonattainment designation status.
  https://www.epa.gov/ground-level-ozone-pollution/redesignation-and-clean-data-policy-cdp
Overview

## Slide 20: SIP Types & Their Basic Requirements
Infrastructure (I-SIP)
Attainment
Maintenance
Transport/Good Neighbor
Conformity
Control Measure
Regional Haze
Tribal Implementation Plan (TIP)
Overview

## Slide 21: Infrastructure SIP (I-SIP); CAA 110(a)(2)
Required from all States and U.S. Territories within three years after promulgation of a new or revised NAAQS.
  DC Circuit Court decision means a NAAQS is promulgated on the date it was signed by the EPA Administrator and made publicly available.
  Other SIP-related effective dates are tied to Federal Register actions.
Overview-Type of SIP

## Slide 22: Basic I-SIP requirements
What air quality monitoring program is in place for the NAAQS?
What authority and resources the state has for jurisdiction over air quality.
Information about the state’s technical programs, such as data collection/analyses/modeling systems.
What authority the state has for developing, implementing, and enforcing control measures.
  I-SIP does not address what control measures will be needed to attain the NAAQS.
What public review process(es) the state uses.
Overview-Type of SIP

## Slide 23: Attainment Demonstration SIP
A collection of documents that demonstrate what the state plans to do that will result in an area attaining the NAAQS. Plans are due to EPA 18+ months after the effective date of the NAAQS designation, depending on the severity of designation.
Plan includes:
  Monitoring data
  Emissions inventories
  Modeling
  Control strategies (could include RACT, RACM, BACT, BACM, PSD, NSR)
  Compliance & enforcement
  Administrative requirements, such as public notice and comment
Overview-Type of SIP
A
T
T
A
I
N
M
E
N
T
S
I
P

## Slide 24: Rate of Progress (ROP) SIP (Ozone only)
1990 Clean Air Act Amendments required for moderate and above Ozone nonattainment areas.
15% ROP Plan
  Due to EPA in 1996 to reduce VOC emissions by at least 15% from a 1990 baseline.
Post-1996 ROP Plan
  Reduce VOC emissions by a minimum of a 3% average per year, across 3-year running averages beginning November 1996 until the ozone attainment date is reached.
  NOx emission reductions can be substituted for VOC reductions.
  Emission reductions from some motor vehicles control programs are excluded from the ROP plan.
Overview-Type of SIP
A
T
T
A
I
N
M
E
N
T
S
I
P

## Slide 25: Reasonable Further Progress (RFP) SIP
Ozone moderate or higher designated areas
  If attainment date is <= 5 years from designation, RFP is met by attainment demonstration SIP emissions reductions and no additional SIP is required.
  If attainment date is > 5 years from designation, the RFP SIP provides 15% NOx or VOC emissions reductions within 6 years of designation; proportional reductions between the end of the first increment and attainment.
PM requires quantitative milestones be identified that will be achieved every 3 years until attainment.
Overview-Type of SIP
A
T
T
A
I
N
M
E
N
T
S
I
P

## Slide 26: Ozone Rural Transport Areas (CAA 182h)
New (old) option with 2015 Ozone NAAQS.
  Four areas were classified for 1979 1-hour ozone NAAQS.
Applicable for areas designated nonattainment that are not part of or adjacent to a metropolitan statistical area (MSA).
State must complete a marginal area attainment demonstration SIP to show that local NOx and VOC sources don’t contribute significantly to high ozone in the rural transport area or other areas.
If EPA approves, area can be redesignated to attainment.
Overview-Type of SIP
A
T
T
A
I
N
M
E
N
T
S
I
P

## Slide 27: Wrap-up: Attainment SIPs
Avoid if at all possible
  SIPs are expensive, especially nonattainment SIPs
  Once a nonattainment area, some control measures and requirements NEVER go away, even when area reaches attainment
  Nonattainment to full Attainment takes 20 + years
  Try to be proactive to prevent nonattainment
A
T
T
A
I
N
M
E
N
T
S
I
P
Overview-Type of SIP

## Slide 28: Maintenance SIP (CAA 175A)
Applies to any NAAQS.
Reinforces that area will remain in attainment for at least 20 years after redesignation to attainment.
  1st SIP covers 10 years.
  2nd SIP covers additional 10 years after the end of the first maintenance period.
Overview-Type of SIP

## Slide 29: Transport/Good Neighbor SIP
Reference(s):
  CAA, Title I, Part A, 110(a)(2)(D)(i)(l)
  CAA, Title I, Part D, 176A
States must show their emissions do not contribute significantly to “downstream” areas or if they do, what measures will be put in place to reduce the applicable emissions.
The CAA 176A allows for transport regions to be created – the Ozone Transport Commission was formed to address northeast U.S. issues.
Overview-Type of SIP

## Slide 30: International Transport – (CAA 179b)
For areas that would attain an Ozone, CO or PM10 NAAQS but for emissions emanating from outside the U.S.
State must prepare and submit a SIP with relevant technical work and control measures developed for the area.
Nonattainment designation remains, but attainment deadline doesn’t apply.
Overview-Type of SIP

## Slide 31: Conformity SIPs
Activities funded by or approved by federal agencies must conform to a state’s attainment or maintenance area SIP.
“Conform” is defined as: activities that will not cause or contribute to new air quality violations, worsen existing violations, or delay attainment of air quality standards.
Overview-Type of SIP

## Slide 32: Transportation Conformity
Transportation Conformity requires SIP commitments and infrastructure regulations that layout interagency consultations, how disputes are resolved and provides specific definitions for air agencies and transportation agencies to follow.
Applies only to nonattainment or maintenance areas; and
"Regionally Significant" transportation projects located outside of nonattainment or maintenance areas that could potentially impact the nonattainment or maintenance area.
Primarily FHWA funding or FHWA/DOT actions
More details later.
  https://www.epa.gov/state-and-local-transportation/general-information-transportation-and-conformity
  https://www.epa.gov/state-and-local-transportation/transportation-conformity
Overview-Type of SIP

## Slide 33: General Conformity (SIP requirements revised in 2010)
Applies to nonattainment and maintenance areas.
Federal Agencies typically involved: HUD, FAA, Corp of Engineers, etc.
Three exceptions:
  Actions covered by the transportation conformity rule.
  Actions with associated emissions below specified de minimis levels. BEWARE - consultation with local air agencies are only required for projects that exceed de minimis and require a general conformity determination. Federal agency often makes de minimis determination. BE INVOLVED –Ask for documentation of how de minimis was determined.
  Other actions that are either exempt or presumed to conform.
Overview-Type of SIP

## Slide 34: General Conformity, cont.
In an area with an approved SIP, conformity can be demonstrated by one of the following:
  Showing that the emission increases caused by an action are included in the SIP.
  Demonstrating that the state agrees to include the emission increases in the SIP.
  Offsetting the action’s emissions in the same or nearby areas.
  Taking mitigation actions to reduce the emission increase.
  Air quality modeling demonstration.
Overview-Type of SIP

## Slide 35: General Conformity, cont.
In an area without an approved SIP, a federal action can be shown to “conform” by demonstrating there will be no increase in emissions in the NAA or maintenance area from the federal agency action that could cause new violations of the NAAQS and/or no increase in the frequency or severity of previous violations.
https://www.epa.gov/general-conformity
Overview-Type of SIP

## Slide 36: Control Measure SIP
Some control strategies are complex enough to warrant their own SIP Revision
  Ex: Vehicle Inspection and Maintenance
  Ex: Prevention of Significant Deterioration/New Source Review
  Ex: Minor Source Permit Program
  Ex: Clean Fuel Program
Overview-Type of SIP

## Slide 37: Control Measure SIP, cont.
Vehicle Inspection and Maintenance
  Required in Ozone moderate and above areas (CAA 182(b) and (c)), CO moderate and serious areas (CAA 187)
    For serious areas, state must submit biennial report to EPA administrator summarizing emission reductions
Clean Fuel Programs required in Ozone and CO serious and above areas
More in Technical Data Needed Section about PSD, NSR and Title V
Overview-Type of SIP

## Slide 38: Regional Haze SIP – CAA 169A
All states are required to show progress toward natural visibility conditions in Class I areas by 2064.
Class I areas are national parks, wilderness areas, national forests and monuments.
Reasonable Progress: SIPs required every 10 years; interim progress report every 5 years.
Round 1 SIP included consideration of retrofit controls on existing large stationary sources: BART (Best Available Retrofit Technology).
Natural and Hazy Conditions
Overview-Type of SIP
Image credit: Denali NPP, ©Alaska Division of Tourism

## Slide 39: Tribal Implementation Plan (TIP)
Tribes have similar authority as states in the CAA.
Although not a requirement, Tribes can be the authority for the air quality program within their own boundaries.
The Tribal Authority Rule (TAR) provides regulatory framework for developing TIPs.
Like SIPs, TIPs must demonstrate that Tribes have the necessary resources and authority.
Overview-Type of SIP
Photo: EPA https://www.epa.gov/tribal-air

## Slide 40: Roles and Requirements
Roles & Requirements

## Slide 41: How to put together a SIP
I don’t know where to start!
So many burning questions:
  What is required?
  Where do I find detailed information and data?
  Who is involved?
  How do I bring it together?
  What can I expect?
Roles & Requirements

## Slide 42: Understand the Requirements
Federal Requirements
  Clean Air Act
  Federal Register
  Guidance Documents
  EPA Tools
Specific State Issues
  Statutes or rules that may impact development
Important to start work early with the regional EPA staff and EPA checklists
  What is new on this type of SIP from EPA?
  What are they looking for and expecting to see in this SIP?
  More on this later in the course....
Roles & Requirements

## Slide 43: Roles
Identify who needs to be involved and who will be impacted by this SIP
There are many people, organizations, and roles that play a part within the SIP development, review/approval, and implementation process
Figure out who is or should be "playing in the sandbox" with you!
  Internal technical staff
  Internal policy and decision makers
  Staff from other governmental organizations
  Elected officials
  External Stakeholders
Roles & Requirements

## Slide 44: SIP Roles in Air Quality Management
Roles & Requirements

## Slide 45: External Stakeholders
Public
  Anyone, anyplace.
  Procedures must be in place to provide the public an opportunity to review a SIP before submission to EPA.
  Public notice, public hearing and 30-day comment period.
Stakeholders (often involved during the development phase)
  Those who may have vested interest in the outcome – i.e., potentially regulated sources, local communities, other states (especially those contributing emissions to the nonattainment area).
  Environmental/public interest organizations.
National, regional or local organizations (ex: Ozone Transport Commission).
Roles & Requirements

## Slide 46: State/Tribe
Where the rubber meets the road – overall responsibility for the air quality program development, implementation and enforcement.
Needs to understand the source/fate/transport/background of air pollution within the agency’s jurisdiction in the context of Federal air pollution laws and regulations.
Responsible for source category inventories, modeling and control measure development, within the agency’s jurisdiction.
Issues and enforces permits.
Is the center of communication for stakeholder processes.
Roles & Requirements

## Slide 47: Local Units
In some areas, local units have jurisdiction to develop and implement SIPs
  Ex: California air quality districts
  Ex: Maricopa County, Arizona (by law)
  Ex: Memorandums of Understanding between State and Local Unit
In some areas, local units may need to develop control strategies
In some areas, organizations within local units may need to be involved
  Ex: Metroplitan Planning Organizations (MPOs) regarding emission budgets/transportation measures
Roles & Requirements

## Slide 48: EPA
May provide assistance throughout the SIP development process through rules, guidance documents memos, attending meetings.
  Participation can increase a SIP’s chance of ultimate approval.
Must review and take action on submitted SIPs (CAA (110(k)).
  Within 6 months of SIP submittal, EPA must take action or SIP is deemed complete (but not approved).
Official actions are documented in the Federal Register (FR) and codified in the Code of Federal Regulations (CFR).
Responsible for developing a Federal Implementation Plan (FIP) if SIP not timely submitted or disapproval not addressed by state.
Roles & Requirements

## Slide 49: Important Roles for Two Unique SIPs
Transportation Conformity
  Metropolitan Planning Organization (MPO) for communities with a population of over 50,000 as determined by the U.S. Census.
  Department of Transportation
    Work to increase their knowledge regarding the tie-in between Air Quality and Transportation
    There could be opportunities for funding assistance
Regional Haze
  Federal Land Managers
  Tribes
  Small communities
Roles & Requirements

## Slide 50: Transportation Conformity Roles and Responsibilities
US DOT (FHWA/FTA) | Approves conformity determinations on transportation plans, transportation improvement plans (TIPs), and projects
Metropolitan Planning Organizations (MPOs) | Prepares the conformity determination for transportation plans and Transportation Improvement Plans (TIPs)
State Dept. of Transportation and Transit Agencies | Prepares project-level conformity determination
State and Local Air Agencies | Develops the motor vehicle emissions budget (MVEB); consults on conformity determinations
EPA | Consults on the conformity process; conformity regulations and guidance
Roles & Requirements

## Slide 51: Regional Haze SIP Roles
Same as previous SIPs discussed
  Public
  Stakeholders (Sources, etc.)
  States and Tribes
  Locals
  EPA
+
  Regional Planning Organizations
    May help with technical work, data analysis, monitoring
  Federal Land Managers
    As managers of Class I Areas, interested in seeing progress in visibility
Roles & Requirements
Notes: Western States - WRAP
SE States - VISTAS

## Slide 52: Environmental Justice Communities/Populations
Environmental justice (EJ) is the fair treatment and meaningful involvement of all people regardless of race, color, national origin, or income with respect to the development, implementation and enforcement of environmental laws, regulations and policies.
Fair treatment means no group of people should bear a disproportionate share of the negative environmental consequences resulting from industrial, governmental and commercial operations or policies.
Meaningful involvement means:
  People have an opportunity to participate in decisions about activities that may affect their environment and/or health;
  The public's contribution can influence the regulatory agency's decision;
  Community concerns will be considered in the decision-making process; and
  Decision makers will seek out and facilitate the involvement of those potentially affected.
Roles & Requirements

## Slide 53: Environmental Justice Communities/Populations
EPA Resources
  https://www.epa.gov/external-civil-rights
  https://19january2021snapshot.epa.gov/ejscreen_.html (archived site)
State Specific Programs and Requirements (examples)
  Arizona: https://www.azdeq.gov/MyCommunity
  California: https://calepa.ca.gov/envjustice/
  Colorado: https://cdphe.colorado.gov/environmental-justice
  Hawaii: https://health.hawaii.gov/epo/ej/
  Oregon: https://www.oregon.gov/deq/about-us/pages/environmental-justice.aspx
  Maryland: https://mde.maryland.gov/Environmental_Justice/Pages/Landing%20Page.aspx
  Minnesota: https://www.pca.state.mn.us/about-mpca/environmental-justice
  New Mexico: https://www.env.nm.gov/general/environmental-justice-in-new-mexico/
  New York State: https://www.dec.ny.gov/public/333.html
  Utah: https://deq.utah.gov/general/environmental-justice-in-utah
  Washington State: https://ecology.wa.gov/About-us/Who-we-are/Environmental-Justice
  West Virginia: https://dep.wv.gov/environmental-advocate/Pages/default.aspx
Roles & Requirements

## Slide 54: Hands On Learning – Examples and Tools
How to proactively analyze stakeholder interest and influence
Alaska case study – early public engagement
Developing communication plans for SIP projects
Hands On Exercise/Tools

## Slide 55: Identifying Stakeholders
Key stakeholders must be at least minimally satisfied
Create and sustain coalitions of stakeholders
Stakeholder analysis helps us to figure out how to frame the key challenges
Stakeholders can be organized in terms of their presumed INTEREST in decision making to achieve better outcomes and their POWER to help to produce the outcomes
Example(s) of ways to analyze and organize (Activity)
Hands On Exercise/Tools

## Slide 56: Stakeholders Exercise
Discuss some SIPs you are working on
Select a SIP project (or work through a couple SIP projects)
Identify Stakeholders (5-10)
  Internal
  External
What are your Stakeholders Interests?
What do you need from your Stakeholders?
What power/influence does a Stakeholder have?

## Slide 57: Alaska Case Study – A tool to generate interest
Moderate SIP to Serious SIP effort
Released Preliminary Draft documents on initial data gathered
Spurred local Stakeholder effort
Gathered additional data as affected sectors checked the data presented
Approach did not require response to comments
Public opportunity to see full picture prior to formal public process
EPA given opportunity to see and comment on data informally
https://dec.alaska.gov/air/anpms/communities/fbks-pm2-5-sip-development/
Hands On Exercise/Tools

## Slide 58: Developing Communication Plans
Identify audiences/stakeholders
What methods of outreach would be effective to reach audiences?
What messages do you need or want to convey?
When do you need to communicate?
How can you communicate the messages?
What resources do you have or need to implement the plan?
Hands On Exercise/Tools

## Slide 59: Technical Data Needed
Technical Data Needed

## Slide 60: Identifying Technical Information Needs (depends on SIP type)
SIP Technical/Regulatory Components
  Ambient Air Quality Monitoring
  Emissions Inventories & Modeling
  Air Quality Modeling
  Control Strategies & Permits
What Not to put in a SIP
  Programs/regulations you do not want EPA to enforce
Technical Data Needed

## Slide 61: Precursor Pollutants
Fine Particulate Matter – direct PM2.5 and indirect PM2.5
  Nitrogen oxides
  Sulfur dioxide
  Ammonia
  Volatile Organic Compounds
Ozone
  Nitrogen oxides
  Volatile Organic Compounds
  Carbon Monoxide

## Slide 62: What is AQ monitoring data used for and why
National Air Quality Standards (NAAQS)
Design Values and Progress Trends
Public Health Announcements
Validating Models and Effectiveness of Control Strategies
Precursor Demonstrations
Research
Citizen Science
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 63: What is AQ monitoring data and how to find it
CAA Section 319
  Requires an air quality monitoring system throughout the U.S. to meet multiple objectives and provide recordkeeping with respect to such monitoring data
  Supports periodic analysis and reporting to the general public by the Administrator with respect to air quality trends
  https://www.epa.gov/outdoor-air-quality-data
  https://www.airnow.gov/
  https://www.epa.gov/aqs
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 64: 40 CFR Parts 53 and 58
The “Home” of requirements for:
  Method approvals
  Sampling frequency
  Network design
  Annual plans and Network assessments
  Monitoring location
  Quality Assurance
  Data reporting
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 65: Ambient Air Quality Monitoring
Objectives of the National Air Quality Monitoring Network:
  Supports compliance with the NAAQS
  Provides timely air quality data to the public
  Supports air pollution research studies
  Validates emissions models and verifying control strategy effectiveness
Network Operators: Federal and State, Tribe and/or Local agencies
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 66: Ambient Air Quality Monitoring, cont.
Reference(s):
  AirKnowledge Ambient Air Monitoring (AMBM) e-learning: https://airknowledge.gov/AMBM-SI.html
  EPA Managing Air Quality - Ambient Air Monitoring: https://www.epa.gov/air-quality-management-process/managing-air-quality-ambient-air-monitoring
  Ambient Air Monitoring Technical Information Center: https://www.epa.gov/amtic
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed
Monitoring Shed

## Slide 67: Definitions
Monitor: A device used to measure air quality, typically automated continuous gases such as Ozone (O3) and Carbon Monoxide (CO).
Sampler: A device that supports manually operated, filter-based methods, typically for particles and/or air toxics measurements
Station: a physical monitoring location (with a building or platform) that houses monitors and samplers
Network: A collection of monitoring stations of a given type or types.
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 68: SLAMS Network State and Local Air Monitoring Stations (SLAMS)
Ozone, CO, SO2, NOx
Air Toxics
NCore (National core monitoring sites – multi-pollutant high spatial and temporal resolution monitors)
PM10 and PM2.5
Chemical Speciation
Lead Monitoring
Meteorological Measurements
Near-road CO, NO2, and PM2.5 Monitoring
Susceptible and Vulnerable Populations - NO2 Monitoring
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 69
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 70: Surface Air Quality Data
EPA Air Quality System (AQS) is the repository for SLAMS and other network data
Surface Air Quality Data has historically covered urban areas
  Stations in rural areas becoming more frequent
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 71: Surface Air and Ozone
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 72: EPA AQS Surface Air Quality Data
Data included in the AQS
  Hourly O3, NO2, NOx, CO, PM10, and PM2.5
  Federal Reference Method (FRM) measures 24-hour total PM2.5 mass every 1-3 days
Chemical Speciation Network (CSN) measures 24-hour average speciated PM2.5, including SO4, NO3, NH4, EC, OC, and elements every 1-6 days
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 73: AirNow Data
For ozone and PM2.5
Provides ability to compare recent air quality data not yet available from AQS with historic levels.
  AQI data are not fully verified and validated through the quality assurance procedures and, therefore, cannot be used to formulate or support regulation, guidance or any other Agency decision or position.
  https://www.epa.gov/outdoor-air-quality-data
AQS data, as it becomes available, replaces any AirNow data.
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 74: CSN - Chemical Speciation Network
PM2.5 Chemical Speciation Network (CSN) consisting of Speciation Trends Network (STN) sites and supplemental speciation sites
Established in late 1990s.
Teflon filters are analyzed for 33 elements, nylon filters are analyzed for ions and quartz filters are analyzed for carbon.
https://www.epa.gov/amtic/chemical-speciation-network-csn
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 75: NCore - National Core Monitoring Network
Multi pollutant network that integrates several advanced measurement systems for particles, pollutant gases and meteorology.
Network started January 1, 2011.
Measures: PM2.5 speciation, PM2.5 FRM mass, continuous PM2.5 mass, PM10-2.5 mass, O3, CO, SO2, NO, total reactive nitrogen (NOy), surface meteorology.
The requirements for NCore monitoring can be found in 40 CFR part 58 Appendix D
https://www.epa.gov/amtic/ncore-monitoring-network
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 76: Non-AQS Aerometric Monitoring Networks Interagency Monitoring of Protected Visual Environments (IMPROVE)
Primarily located in rural Class I areas at National Parks, Wilderness Areas, and Fish & Wildlife Refuges – critical for Regional Haze SIPs
Measures 24-hour average PM2.5, PM10 mass, and speciated PM2.5, including SO4, NO3, EC, and OC every 1-3 days
http://vista.cira.colostate.edu/Improve/
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 77: Non-AQS Aerometric Monitoring Networks Clean Air Status and Trends Network (CASTNet)
Established to assess trends in pollutant concentrations, atmospheric deposition, and ecological effects due to changes in air pollutant emissions. Sites are mainly in rural areas
Measures hourly O3, temperature, wind speed/direction, potential temperature, solar radiation, relative humidity, precipitation, and surface wetness
Measures weekly samples of SO2, HNO3, and speciated PM2.5, including SO4, NO3, NH4
https://www.epa.gov/castnet
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 78: Non-AQS Aerometric Monitoring Networks National Acid Deposition Program (NADP)
Sites in mainly rural areas away from large point sources
Measures weekly samples of SO4, NO3, NH4 wet deposition and SO4 and NO3 dry deposition
Some sites include NH3 measurements
Some sites include Hg measurements
http://nadp.slh.wisc.edu/
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 79: Other Monitoring Data
Research/Sensor Studies
  Satellites
      NASA’s Tropospheric Emission Monitoring of Pollution (TEMPO) mission: https://tempo.si.edu/
Citizen monitoring data
  Purple Air and other common sites
      https://map.purpleair.com
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 80: What are monitored data used for in the SIP?
Design values are calculated from regulatory monitoring data based on the pollutant and form of the standard.
Developing design values for the NAAQS - four parts:
  Indicator
    e.g., ozone, PM2.5
  Averaging period
    e.g., 1 hour, 8-hours, 24-hours, annual
  Statistical form
    e.g., three-year average of 4th highest daily maximum 8-hour concentration
  Level (the concentration)
Design values are compared to the NAAQS to determine attainment status
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 81: Example: PM2.5 Design Values – Fairbanks, AK
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 82: Example: PM2.5 Design Values – Fairbanks, AK
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 83: Networking with Air Monitoring Staff
Get to know your Air Monitoring Staff!
You will need them!
Usually overworked and understaffed, need a lot of advanced notice of what is needed if they haven't supported a SIP before.
Questions – discussions?
AQ
M
O
N
I
T
O
R
I
N
G
Technical Data Needed

## Slide 84: Emission Inventories & Modeling
Reference(s):
  AirKnowledge e-learning: https://airknowledge.gov/EMIS-SI.html
  Technical Work: https://www.epa.gov/air-emissions-inventories
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 85: Clean Air Act Requirements for Emissions Inventories
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 86: Air Emissions Reporting Requirements (AERR)
EPA promulgated the AERR in December 2008.
  The AERR consolidated and streamlined previous requirements of several older rules for states and local air pollution control agencies to submit emissions inventories for criteria pollutants to EPA's Emissions Inventory System (EIS)
  Many of the states also voluntarily report air toxics that are also used in building the NEI
  https://www.epa.gov/air-emissions-inventories/air-emissions-reporting-requirements-aerr
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 87: What is an Emissions Inventory?
Current comprehensive listing by sources of air pollutant emissions in a geographical area during a specific time period
The basis for numerous efforts including trends analysis, regional, and local scale air quality modeling, regulatory impact assessments, and human exposure modeling
Pollutants:
  Criteria Air Pollutants (CO, NOx, SO2, NH3, VOC, PM2.5 and PM10)
  Hazardous Air Pollutants (e.g., Benzene, Acetaldehyde)
  Greenhouse Gases (e.g. CO2, CH4, N2O)
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 88: Sectors and Source types
Point sources
Area sources
Nonpoint sources
  Onroad and
  Nonroad Mobile sources
Event/Natural sources
  Biogenic
  Wildfire/Dust
  Emergency Releases
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 89: Source Classification Codes (SCC)
SCCs are important to ensuring an accurate emission inventory
EPA uses SCCs and area and mobile source (AMS) codes to classify different types of anthropogenic emission activities.
SCCs are either 8 or 10 digits long. Most point source SCCs are 8 digits long, with exceptions to a handful of point SCCs, such as aircraft exhaust and airport ground support equipment, which are 10 digits long and included in the point inventory because they are developed at discrete locations. Nonpoint, mobile, and events codes are 10 digits long.
Emission pre-processors, like SMOKE, use the SCC in characterizing the emission source.
Look up SCC on EPA's website at: https://sor-scc-api.epa.gov/sccwebservices/sccsearch/
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 90: Emission Inventory Compilation Steps
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 91: Types of Air Pollution Emissions Inventories
National Emissions Inventory (NEI)
  SIP Planning Inventory
  Periodic NAA inventory
  ROP/RFP NAA inventory
  Maintenance NAA inventory
SIP Modeling Inventory
  Modeled attainment demonstrations
  EPA rule making
  Global modeling
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 92: Types of Air Pollution Emissions Inventories, cont.
Projection/Future-year Inventory
  Estimate of future emissions with growth and controls
  Growth based on models (IPM, ERTAC), industry surveys, transportation plans, linear extrapolation, and other methods
  Controls
    On the books: currently promulgated rules and other enforceable mechanisms that will phase in through time
    On the way: controls that are speculated to be promulgated
  Brute-force projections may include across-the-board changes (i.e. 50% NOx reduction) to test the model and simulated air quality response
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 93: National Emissions Inventory (NEI)
The best and most complete estimates of Criteria Air Pollutant (CAP) and Hazardous Air Pollutant (HAP) emissions prepared by EPA
  Must be done every three years
  Based on S/L/T agency work that is submitted to EPA
Helps S/L/Ts meet CAA requirement that SIPs include emissions data and related information
Also helps S/L/Ts obtain emission data and information about other states to support modeled attainment demonstrations
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 94: Uses of the NEI
Regional- and local-scale air quality & human exposure modeling
Control strategy analysis
Regulatory impact analysis
Risk assessment studies
Emission trends and program accountability
Public reporting
International reporting
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 95: What is in the NEI?
Geographic Coverage
  Entire U.S.
  Individual process level inventory for point sources
  County level inventory for non-point and mobile sources
Pollutants coverage:
  Criteria Air Pollutants (CAPs)
CO, NOx, VOC, NH3, SO2, PM10, PM2.5
Ozone precursors: VOC, NOx ,CO
Direct PM emissions: PM10, PM2.5
PM precursors: VOC, NOx, SO2, NH3
  Hazardous Air Pollutants
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 96: NEI Data Resources
S/L/T air agencies
EPA Data Systems
  Emissions Inventory System (EIS)
  Emissions Trading Program
  Toxic Release Inventory (TRI)
EPA data collection programs
  MACT compliance data
  Information Collection Review (ICR) for NAAQS development
  Clean Air Markets Division (CAMD) for large point sources
  https://www.epa.gov/airmarkets
Data developed by EPA
  Mobile Source models
  EIAG data augmentation
Industry
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 97: Use of NEI by EPA
Emissions Modeling Platforms (EMPs)
  EPA OAQPS develops EMPs with the best available inventories to support rulemaking
  Combination of all available inventories
Purpose: Support Federal NAAQS revisions, SIP calls, and rulemakings
Base and future year emissions
Includes ancillary emissions data, modeling tools, and technical support documentation
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 98: Use of NEI by S/L/T
Required by CAA sections 172(c)(3) and 182(a)(1) for Attainment Demonstration and Rate of Progress/Reasonable Further Progress SIPs
Assessment of adequacy of Maintenance Plan 10-year life cycle
Development of control strategies, modeling
Develop base year and future year emissions
Covers Criteria Air Pollutants (CAPs)
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 99: Use of NEI by Regional Planning Organizations (RPOs)/ Multijurisdictional Organizations (MJOs)
Develop multi-state inventories for the Regional Haze Program
In some regions, RPOs also develop for PM and Ozone SIP control strategy modeling
Assists with Inter-RPO cooperation and data sharing
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 100: Modeling Inventory
Modeling inventories have specific requirements
  Geographically resolved emissions (gridded or specific dimensions) - spatial allocation of emissions
  Hourly time resolution - temporal allocation of emissions
  Pollutant species (“model species”) to meet needs of AQ model chemical/physical algorithms
  Quality Assurance/Quality Control of data
  All sources (area/mobile/point/biogenic) represented
Can be a combination of several inventory sources (NEI, Periodic inventory, RPO Inventory)
Used for both SIP and non-SIP emissions modeling
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 101: RPO Inventory
Regional Planning Organizations (RPOs) may work with states in their region as well as across RPOs to leverage resources and ensure consistent emission estimates for use in regional haze and other planning efforts.
Important to be able to understand how adjoining states are estimating emissions to avoid anomalies from different approaches when modeling regional emissions.
Example:
  VISTAS https://www.metro4-sesarm.org/content/vistas-regional-haze-program
  WRAP EIs and Database at https://westar.org/
  CENSARA Regional Haze Committee: https://www.censara.org/
  MARAMA: https://marama.org/ and MANEVU: https://otcair.org/manevu
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 102: EPA Inventory Guidance
Emissions Inventory Guidance for Implementation of Ozone and Particulate Matter National Ambient Air Quality Standards (NAAQS) and Regional Haze Regulations
US EPA, May 2017
https://www.epa.gov/air-emissions-inventories/air-emissions-inventory-guidance-documents
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 103: Emission Inventory Development
Data from source-specific emission tests (source tests) or continuous emission monitors are usually preferred for estimating a source’s emissions because those data provide the best representation of the tested source’s emissions.
Emissions Factors (EFs) are a representative value that attempts to relate the quantity of a pollutant released to the atmosphere with an activity associated with the release of that pollutant.
E= (A x EF) x (1-ER/100)
E = Emissions (e.g. tons/year) is equal to the A = Activity (e.g. # hours, miles, etc. /year) multiplied by the EF and ER = emission reduction efficiency
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 104: AP-42 Compilation of Air Pollutant Emissions Factors
Published since 1972 as the primary compilation of EPA’s emission factors
Emissions factor and process information for >200 air pollution source categories
Compiled from source test data, material balance studies, and engineering estimates
Fifth Edition published in January 1995, updated with supplements and updates
https://www.epa.gov/air-emissions-factors-and-quantification/ap-42-compilation-air-emissions-factors
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 105: Webfire Compilation of Air Pollutant Emissions Factors
Online database of emissions factors for CAPs and HAPs
Industrial and non-industrial processes
Includes descriptive information on industry and source types, control device information, pollutants emitted, and supporting documentation
https://cfpub.epa.gov/webfire/
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 106: Collecting Activity Data
What data sources already exist?
  Census
  EPA
  Other
What data sources are needed for your effort?
  Surveys
  Travel logs
  Observation
Actuals from Specific Sources, where available
  Timely request for information (at beginning)
  Develop forms for data response (make it easier for them - and for you to post process)
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 107: Emissions Inventory System (EIS)
Provides access to emissions inventory data
  Use by everyone during EI development results in more accurate and comprehensive NEI
  Reduces the time it takes to develop the NEI
  Makes the NEI development process more transparent
  Builds automated and robust quality assurance (QA) steps into the NEI process
Includes public and industry access to the historic and current emission inventory data
https://www.epa.gov/air-emissions-inventories
Technical Data Needed
E
M
I
S
S
I
O
N
I
N
V
E
N
T
O
R
Y

## Slide 108: Emissions Modeling
Puts emissions in temporal and spatial allocations and speciation depending on pollutant
Emissions Models are “process-based” software that estimate emissions
  Examples: MOVES (onroad mobile), BEIS (biogenics)
Emissions Processors are software that convert inventories to the terms/formats required by air quality models
  Example: SMOKE
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 109: Emissions Inventories and Modeling Resources
Clearinghouse for Inventories & Emissions Factors (CHIEF)
  https://www.epa.gov/chief
National Emissions Inventory (NEI) and Emissions Factors
  https://www.epa.gov/air-emissions-inventories
Emissions Inventory System (EIS)
  https://www.epa.gov/air-emissions-inventories
Electric Generating Unit (EGU) Continuous Emissions Monitoring Systems (CEMS)
  https://epa.gov/emc/
  https://www.epa.gov/emc/emc-continuous-emission-monitoring-systems
  https://www.epa.gov/airmarkets/power-sector-emissions-data
Motor Vehicle Emissions Simulator (MOVES)
  https://www.epa.gov/moves
Sparse Matrix Operator Kernel Emissions (SMOKE) model
  https://www.cmascenter.org/smoke/
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 110: Emissions Models Software to Estimate Emissions
MOtor Vehicle Emission Simulator (MOVES)
  Developer: EPA OTAQ
  Current Version: MOVES5 (2024)
  O/S: Windows, Linux
  Software for estimating emissions from on-road mobile sources, including both on- (roadway) and off- (starts/stops/idling) network sources
  Includes a database on fleet, fuels, control programs, and activities
  Prescribed by EPA for use in SIP modeling and transportation conformity
http://www.epa.gov/otaq/models/moves/
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 111: Emissions Models Software to Estimate Emissions
NONROAD
  Was a standalone model – now integrated in MOVES5
  Software for estimating emissions from nonroad mobile sources and engines (construction, mining, ag, lawn/garden, recreational marine)
  Includes a database on engine populations, activities, horsepower, load factors, and controls
  Many of the NONROAD technical reports still apply to the nonroad inputs and algorithms used in MOVES:
    https://www.epa.gov/moves/nonroad-technical-reports
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 112: Emissions Models Software to Estimate Emissions
Biogenic Emission Inventory System (BEIS)
  Developer: EPA ORD (Office of Research and Development)
  Current Version: 4.0 (2014)
  O/S: Linux (Integrated in SMOKE and CMAQ)
  Software for estimating VOC and NO emissions from vegetation and soils
  Includes a gridded North American landcover database (BELD) and emissions factors for >200 plant species
https://www.epa.gov/air-emissions-modeling/biogenic-emission-sources
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 113: Emissions Models Software to Estimate Emissions
Model of Emissions of Gases and Aerosols from Nature (MEGAN)
  Developer: NOAA, WSU, ENVIRON/Ramboll, Inc.
  Current Version: 2.10 (2014)
  O/S: Linux (Integrated in WRF-Chem)
  Software for estimating VOC and NO emissions from vegetation and soils
  Includes global gridded leaf area index, plant types, and emissions factors
http://lar.wsu.edu/megan
https://cfpub.epa.gov/si/si_public_record_report.cfm?Lab=CEMM&dirEntryId=353283
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 114: Emissions Models Software to Estimate Emissions
Integrated Planning Model (IPM)
  Developer: ICF Consulting, Inc.
  Current Version: EPA's Power Sector Modeling Platform v6 Using IPM
  O/S: Windows
  Power demand model that determines low-cost means of meeting electric generation energy and capacity demand while complying with specific constraints, including emissions controls
  Integrated into the EPA Power Sector Modeling Platform for analyzing the impacts of emissions policies on US electricity generation sector
https://www.epa.gov/power-sector-modeling
https://www.epa.gov/power-sector-modeling/post-ira-2022-reference-case
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 115: Emission Processors Software to Prepare Emission Inputs to Air Quality Models
Sparse Matrix Operator Kernel Emissions (SMOKE)
  Developer: UNC Institute for the Environment
  Current Version: 5.1
  O/S: Linux
  Software that integrates emissions data processing with high-performance computing sparse-matrix algorithms to create gridded, speciated, hourly emissions for input to a variety of air quality models.
http://www.smoke-model.org
Technical Data Needed
E
M
I
S
S
I
O
N
M
O
D
E
L
I
N
G

## Slide 116: Air Quality Modeling
Reference(s):
  AirKnowledge:
    https://airknowledge.gov/MODL-SI.html
  Technical Work:
    https://www.epa.gov/scram
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 117: Air Quality Modeling and SIPs
CAA Section 172(c) requires States with an NAA to submit an attainment demonstration that uses:
  Emissions Inventory (base and future years)
  Adopted Control Measures
For PM2.5, all States (with NAAs) must submit an attainment demonstration which includes modeling (40 CFR §51.1007)
  Photochemical grid modeling and/or local dispersion modeling
  Precursor demonstrations to avoid precursor control measures
For ozone, moderate and above NAAs are required to submit an attainment demonstration with modeling (40 CFR §51.908)
  Photochemical grid modeling
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 118: Photochemical Grid Models (PGM)
Large-scale air quality models that account for chemical and physical atmospheric processes in predicting pollutant concentrations.
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 119: Photochemical Grid Modeling
Simulate the multiple and complex chemical and physical processes that produce air pollution
Platforms for integrating multiple emissions source categories and emissions control strategies in a single simulation
The ultimate goal of PGMs is to assist policy makers in determining the most efficient ways of reaching a future air-quality goal.
  Models are used to predict the effects of future control strategies
  Controls necessary for SIP attainment demonstrations (States)
  Air quality impacts of national rules (EPA)
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 120: Current Generation of PGMs
“One-Atmosphere” Modeling
  Multi-pollutant: Ozone, PM, visibility, acid and nutrients deposition, air toxics, etc.
  Multi-scale: International, National, Regional, Local
Advanced Computing Technologies
  Fast runtime (highly efficient for parallel & distributed computing) and cross-platform portability (supercomputers to PCs)
Examples include Comprehensive air Quality Model (CAMx) and Community Multi- scale Air Quality (CMAQ) model
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 121: Dispersion Models
Source-oriented models (ex: smelters) that characterize atmospheric processes by dispersing a directly emitted pollutant to predict concentrations at selected downwind receptor locations.
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 122: Dispersion Modeling
Guideline on Air Quality “Appendix W” addresses requirements for PSD permit modeling
2022 and 2024 Guidance for ozone and PM2.5 permit modeling
https://www.epa.gov/scram/guidance-ozone-and-fine-particulate-matter-permit-modeling
Additional Resources
https://www.epa.gov/scram/clean-air-act-permit-modeling-guidance
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 123: Overview: How models fit together
Pollen Example:
While the focus of this flow chart is modeling pollen, the concepts of how models fit together is the same as with AQ pollutant modeling

## Slide 124: Overview: How models fit together (cont.)
These flow charts depict how emissions and meteorological models are used as inputs to the photochemical grid model

## Slide 125: Model Inputs: Emissions
For Ozone
  Hourly gridded emissions of NOx, VOC, and CO
For PM2.5
  Hourly gridded emissions of NOx, VOC, SO2, ammonia, CO, and speciated primary PM
    Area and Nonroad: industrial equipment, aircraft, recreational marine, gasoline vapors from refilling, lawn mowers, etc.
    Mobile: cars, trucks, buses, etc.
    Point: utilities, refineries, etc.
    Biogenic: certain tree and plant species emit ozone and PM precursors
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 126: Model Inputs: Meteorology
Models need many meteorological variables (gridded, hourly) as input to simulate advection, diffusion, deposition, chemical transformation, etc.
  Wind fields
  Temperature
  Moisture
  Vertical diffusion or Planetary Boundary Layer (PBL) height
Use gridded data from a meteorological model such as the Weather Research & Forecasting (WRF) model
  More information available at:
  https://www.epa.gov/scram/air-modeling-meteorological-grid-models
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 127: Model Performance Evaluation
Operational Evaluation: compare predicted concentrations to observed concentrations
  Statistics (bias, error, etc.)
  Scatterplots
  Time series plots
If model performance is “acceptable” then the modeling system can be used to predict future air quality.
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 128: Future Year Predictions and Control Strategies
Emissions are projected to a future year and the model is run again (the meteorology is held constant)
  The difference between the base and future year is the predicted future air quality impacts
  The model can be run again with alternative future year emissions control strategies
  The base year is rooted in the modeling design value and the control scenarios use the model to predict future year expeditious attainment
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 129: Future Modeling Years
Future modeling years depend on attainment dates and details contained in the O3 and PM2.5 implementation rules
  PM2.5: 5-and 10-year deadlines under Subpart 1
  O3: 3, 6, 9, 15, 17, and 20-year deadlines under Subpart 2
  Generally model a future year which is one year prior to attainment deadline
    Emissions controls need to be in place in the year or season prior to the deadline
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 130: Source Apportionment
Regional air quality models include configuration options for tracking O3 and PM pollution precursor impacts on receptors
  Distinct from observation-based receptor modeling
CMAQ (Community Multiscale Air Quality)
  Integrated Source Apportionment Method (ISAM)
• CAMx (Comprehensive Air Quality Model with extensions)
  Ozone Source Apportionment Tool (OSAT)
  Particulate Matter Source Apportionment Tool (PSAT)
  Anthropogenic Precursor Culpability Assessment (APCA)
Transport SIP and PSD applications
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 131: Model Improvements
Advanced coupled version of WRF and CMAQ was developed and is used in the research community
  Allows for real-time feedback between met and air quality models
  https://www.epa.gov/cmaq/wrf-cmaq-model
  Where to find the latest on models?
  check out the Community Modeling and Analysis System (CMAS) at: https://www.cmascenter.org
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 132: Modeling Guidance for SIP Attainment Demonstrations
EPA’s recommendations for grid-based air quality modeling for 2015 Ozone, 2012 PM2.5 and Regional Haze reasonable progress analyses.
Does not cover dispersion modeling of PM2.5 for nonattainment area NSR and PSD
  Guideline on Air Quality Models “Appendix W” addresses requirements for permit modeling
https://www.epa.gov/scram/state-implementation-plan-sip-attainment-demonstration-guidance
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 133: Attainment Demonstration Software
A new software called SMAT-CE (Software for the Modeled Attainment Test - Community Edition) is being formally released as a replacement for Model Attainment Test Software (MATS).
SMAT-CE replicates the same tests that are performed by MATS, with identical (or nearly identical) results. SMAT performs the ozone and PM2.5 attainment tests and calculates changes in future year visibility at Class I areas.
https://www.epa.gov/scram/photochemical-modeling-tools
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 134: Unmonitored Area Analysis (UAA)
Calculate future year design values in unmonitored areas
  Uses interpolated ambient design values and model output (fused data)
  Supplemental analysis to the monitored based tests
  MATS can create spatial fields needed for the UAA
Similar tests for O3 and PM2.5
UAA not designed to look for unmonitored PM micro-scale hotspot issues
  12 km resolution sufficient for annual PM2.5
  Finer resolution for 24-hr PM2.5 may be appropriate
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 135: Local Area Analysis (LAA)
Focused on evaluating influence of primary PM2.5 at monitors
  LAA provides a method to examine local primary PM source contributions at FRM monitors
Can use either dispersion model or fine grid Eulerian model (~1km?)
EPA recommends methods for adding secondary PM components from grid-based models with primary components from dispersion model
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 136: Example Modeling Domains
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 137: What if your model has issues?
Weight of Evidence -Weight of evidence (WoE) is used for additional modeling runs not specifically stated in the guidance, other technical studies, straying from the default model configuration.
WOE approaches (i.e. processes used to assess the evidence in support of a hypothesis) can and should be used as needed on any issue needing additional discussion or assessment.
When used in modeling, one application is the justification from deviating from model defaults.
Technical weight of evidence is usually found in the appendix to the SIP and referenced in the SIP body.
Coordination with EPA on what is needed within a weight of evidence is very important.
Documentation is critical.
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 138: Precursor Demonstration
For PM2.5, rule allows a demonstration to avoid additional control measures on precursor specific pollutants
Two different type of precursor demonstrations
  Source/Sector specific – tied to information directly related to a specific sector, such as industrial sources
  Comprehensive – looks at all sectors combined
Developing demonstrations is complicated
  Takes a lot of time and coordination with EPA
  Needs a lot of data and modeling
  EPA must approve prior to avoiding any control measures, which complicates timing of submittal of plans, implementation of control measures and approvability of plans.
Technical Data Needed
AQ
M
O
D
E
L
I
N
G

## Slide 139: PM2.5 Precursor Demonstration
A precursor demonstration is a tiered analysis that can be broken down into five stages each with a decreasing level of confidence in the demonstration.
The various precursor demonstrations available are the following:
  Concentration Based Analysis
    Ambient Data
    Air Quality Modeling (zero-out) - point source set to zero for SO2/NOx, all sectors set to zero only for NOx/all sectors set to zero for VOCs
  Sensitivity Based Analysis (only if needed)
    70% reduction
    50% reduction
    30% reduction
PM2.5 Precursor Demonstration Guidance (epa.gov): https://www.epa.gov/pm-pollution/pm25-precursor-demonstration-guidance
AQ
M
O
D
E
L
I
N
G
Technical Data Needed

## Slide 140: Control Strategies & Permits
Reference(s):
  AirKnowledge:
    https://airknowledge.gov/PERM-SI.html
    https://airknowledge.gov/PLAN-SI.html
  Technical Work: https://www.epa.gov/ground-level-ozone-pollution
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 141: Control Strategies
S/L/Ts have main responsibility to develop
  There are several good sources to help
    https://www.epa.gov/catc/about-clean-air-technology-center
      Good starting point for RACT/BACT/LAER
  National and Regional organizations:
    −AAPCA https://cleanairact.org/
    −NACAA http://4cleanair.org/
    −CenSARA, LADCO, MARAMA, Metro 4/SESARM, NESCAUM, OTC, WESTAR/WRAP
      https://censara.org/
      https://metro4-sesarm.org/
      www.westar.org
      https://marama.org/
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 142: Control Strategy Development
Steps
  Determine priority pollutants
  Identify control measure options
  Work with potentially affected source groups and others to determine appropriate controls
  Incorporate final control measures into SIP
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 143: Control Technologies
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S
Engineering and efficiency solutions for reducing air pollution from sources
The EPA Control Techniques Guidelines (CTGs) provides control technology options
Alternative Control Techniques Documents (ACTs) describe other available control technologies and their respective cost effectiveness
The Control Strategy Tool (CoST) integrates inventories, control technologies, and costs to develop control strategies

## Slide 144: Reasonably Available Control Measures (RACM)
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S
Section 172(c)(1) of the CAA applies to all NAAs
  EPA guidance interprets RACM provision to require a demonstration that:
    State has adopted all reasonable measures to meet RFP requirements and to demonstrate attainment as expeditiously as practicable
    No additional measures that are reasonably available will advance the attainment date or contribute to RFP for the area.

## Slide 145: Reasonably Available Control Technology (RACT)
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S
Subset of RACM
Minimum requirement for existing sources
  Lowest Achievable Emissions Rate (LAER) is applied to new or modified sources
EPA RACT definition (not in the CAA):
  “the lowest emission limitation that a particular source is capable of meeting by the application of control technology that is reasonably available considering technological and economic feasibility” (44 FR 53762; September 17, 1979).
NAA SIPs must demonstrate the application of RACT in the attainment plan emissions control strategies

## Slide 146: BACM/BACT and MSM
BACM = Best Available Control Measure
BACT = Best Available Control Technology
MSM = Most Stringent Measures
Similar process to determining RACM/RACT, but for serious and severe NAA areas
Regulatory mechanism could be an air quality permit, consent order, source specific regulation or other mechanism
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 147: 5% Reduction
Continued failure to reach attainment by statutory deadline
Must show a 5% reduction in the emissions budget per year until reach attainment
Final requirement to try to ensure attainment in a timely manner
  Alaska: Fairbanks North Star Borough Serious PM2.5 Nonattainment Area latest area to reach this threshold.
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 148: Contingency Measures
SIPs must provide for the implementation of measures if an area fails to attain the NAAQS or make RFP
  Must be identified, but not necessarily in place at the time the SIP is submitted to EPA
  Estimated emission reductions must equal 3% of VOC or NOx emissions beyond the levels needed for attainment or RFP goal
https://www.epa.gov/air-quality-implementation-plans/final-contingency-measures-guidance
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 149: New Source Review (NSR)
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S
Training:
AirKnowledge: https://airknowledge.gov/PERM-SI.html
Technical Work:
https://www.epa.gov/nsr/learn-about-new-source-review
https://www.epa.gov/catc

## Slide 150: Three types of NSR permits
Nonattainment NSR permits are required for new major sources/major source modifications in nonattainment areas
Prevention of Significant Deterioration (PSD) permits are required for new major or major sources making modifications in attainment and maintenance areas
Minor source NSR permits applied in attainment or maintenance areas to help ensure there is no violation of a NAA’s attainment plan
A permit is generally required prior to construction of the source
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 151: NSR Goals
Economic growth can proceed without creating any new nonattainment problems
Public health and welfare are protected from any adverse effect which might occur even at air pollution levels better than the NAAQS
Preserve, protect, and enhance the air quality in areas of special natural recreational, scenic, or historic value, such as national parks and wilderness areas.
  EPA issues NSR permits on Federal Lands and where states don’t have approved programs
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 152: Which pollutants are regulated under NSR?
Criteria Air Pollutants:
  CO, SO2, VOC, NOx, NO2, Pb, PM2.5 and PM10
Some pollutants not covered by NAAQS are subject to PSD
  GHGs - https://www.epa.gov/nsr/clean-air-act-permitting-greenhouse-gases
  Total PM
  Fluorides, sulfuric acid mist, reduced sulfur compounds
  Metals
  HAPs are not covered
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 153: What Does NSR/PSD Determine?
Defines what measures will be used to control new air pollution emissions from a facility:
Lowest Achievable Emissions Rate (LAER)
  For nonattainment areas
  Does not consider cost, energy, or other environmental factors
Best Available Control Technology (BACT)
  For PSD areas, i.e. attainment areas
  Considers cost effectiveness of control options
  Not an annual limit; BACT is a short-term limit (lbs/hour)
Rate may be in a permit or regulation
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 154: Potential to Emit (PTE)
The maximum capacity of a source to emit a pollutant under its physical and operational design
  Based on operating 8760 hours/year, unless restricted by a permit condition or some other physical restriction
  Can include effects of emissions controls, if enforceable by permit or:
    State Implementation Plan (SIP),
    Tribal Implementation Plan (TIP) or
    Federal Implementation Plan (FIP) conditions
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 155: NSR nonattainment area permit requirements
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S
Emissions offsets reductions must be:
Quantifiable, enforceable, permanent and surplus (QEPS)
From actual emissions – real, no “paper” reductions
From authorized emissions sources
Federally enforceable at the time of permit issuance for new or modified source
In effect before the new source can commence operation
Emissions reductions from existing sources to balance emissions from proposed new or modified sources
Offset must be at least 1:1

## Slide 156: PSD Permit Requirements
Main requirements
  Install Best Available Control Technology (BACT)
  Perform air quality analysis to assess impacts on air quality; ensure air quality in clean areas does not degrade
  Perform additional impacts analysis
    Assess impacts on national parks & wilderness areas
    Assess impacts on soil & vegetation
    Assess other air quality-related values
  Allow for opportunities for public involvement
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 157: PSD Permit Requirements, cont.
In 2019, EPA introduced MERPs (Modeled Emission Rates for Precursors)
  Intended to help states with PSD permitting by creating MERP “bubbles”
  https://www.epa.gov/nsr/guidance-development-modeled-emission-rates-precursors-merps-tier-1-demonstration-tool-ozone
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 158: 28 Source Categories subject to the PSD 100 TPY Threshold
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S
Coal cleaning plants
Kraft pulp mills
Portland cement plants
Primary zinc smelters
Iron and steel mills
Primary aluminum ore reduction plants
Primary copper smelters
Municipal incinerators
Hydrofluoric acid plants
Sulfuric acid plants
Nitric acid plants
Petroleum refineries
Lime plants
Phosphate rock processing plants
Coke oven batteries
Sulfur recovery plants
Carbon black plants
Primary lead smelters
Fuel conversion plants
Sintering plants
Secondary metal production plants
Chemical process plants
Fossil-fuel or combination of boilers
Petroleum storage/transfer units
Taconite ore processing plants
Glass fiber processing plants
Charcoal production plants
Fossil fuel fired steam electric plants

## Slide 159: PSD SIP Requirements
All pollutant-emitting activities from major stationary sources:
  Same industrial group (same SIC code)
  Contiguous or adjacent properties
  Common ownership or control
Defining modification
  All units with physical or operational change
  Few exclusions
    Routine maintenance repair and replacement
    Increase in hours of operation*
  Artificial separation of a project is not allowed
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 160: PSD Additional Impact Assessment and Class 1 Areas
Analyze impacts on soils, vegetation, and visibility
PSD provides special treatment for Class 1 areas including certain national parks, and national wilderness areas
Federal Land Manager defines Air Quality Related Values (AQRVs)
  Establish criteria for adverse impacts
  Determine if a source will adversely impact AQRV’s
  Make recommendation to the permitting agency
Permitting authority makes the final decision
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 161: PSD Regulations and Guidance
Regulations:
  40 CFR 51.166: Specifies the minimum requirements that a PSD air quality permit program under Part C of the Act must contain in order to warrant approval by EPA as a revision to a State implementation plan (SIP).
  40 CFR 52.21: Delineates the federal PSD permit program, which currently applies as part of the SIP, in approximately one third of States that have not submitted a PSD program meeting the requirements of 40 CFR 51.166.
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 162: Plant-wide Applicability Limits (PALs)
Permit mechanism to avoid NA NSR/PSD in future for an existing source
Pollutant specific
If total emissions after a modification are below the PAL, PSD is not triggered
Effective for 10 years
  https://www.epa.gov/nsr/plantwide-applicability-limit-pal-emissions-level
Technical Data Needed
C
O
N
T
R
O
L
M
E
A
S
U
R
E
S

## Slide 163: Who can you go to in your organization for technical support?
Look at organization charts
Find those responsible for the monitors and submitting data to AQS
Find those responsible for issuing permits to the major sources that will be impacted
Find out if you have on-staff modelers, and what models they know.
No staff?
Find those who are responsible for contracting support!
COMMUNICATE TIMELINES EARLY
Technical Data Needed
H
O
M
E
W
O
R
K

## Slide 164: SIP Preparation
SIP Preparation

## Slide 165: Preparations for Starting a SIP
Do you have answers to the following questions?
  Can you define the problem, and know the source(s)?
  Do you have data readily available or do you need to gather data?
  What resources do you have to develop the SIP, in-house staff, funding?
  Do you currently have the authority to issues regulations to address the problem or must you get the regulatory authority?
  How well does your administration or the local administration understand the problem?
SIP Preparation

## Slide 166: Drafting and Finalizing a SIP Local/State Processes
SIP Preparation

## Slide 167: Communications with EPA
Working with Regional EPA Staff very important
Start discussions early
Get agreement on the following documents to avoid issues in the future
  SIP Development Plan
  TAP – Technical Analysis Protocol
  IPP - Inventory Preparedness Plan
  EPA Checklist
DOCUMENT, DOCUMENT, DOCUMENT
SIP Preparation

## Slide 168: Communications with EPA
SIP Development Plan
  Basic schedule overview for EPA to assist with their planning and help get everyone on the same page
  Identifies potential controversial issues
  Identifies responsible parties – state, local, contractor, EPA
SIP Preparation

## Slide 169: Communications with EPA, cont.
TAP – Technical Analysis Protocol
  Documents what models will be used (year and version)
  Documents and provides rationale for model choices and versions
  Documents any model adjustments made for unique issues or circumstances.
  Living document that grows and is modified over time
  Provides historical information in case of EPA staff turnover
  Can include agreements to minimize adverse pressure for changes
  Can be incorporated in the SIP appendix to give background information
SIP Preparation

## Slide 170: Communications with EPA, cont.
IPP - Inventory Preparedness Plan
  Document that lays out the plan for developing the inventories.
  Where data will come from – Source tests, surveys, NEI, etc.
  What years will be used
  How the data will be QA/QCd.
  Can assist in the development of ‘weight of evidence’ – identifying information or data that doesn’t ‘fit’ into specific requirements for emission inventories or modeling but is important to the area
SIP Preparation

## Slide 171: Communications with EPA, cont.
EPA Checklist
  Typically regional office develops checklists they will use to evaluate SIPs for the completeness check
  Ask if you can get a copy of the checklist to assist in ensuring that nothing is missed
SIP Preparation

## Slide 172: EPA’s SIP LEAN Process
SIP Preparation

## Slide 173: EPA LEAN Process – 2 Toolkits
https://www.epa.gov/sites/default/files/2013-10/documents/leanenvirotoolkit.pdf
  General Toolkit for efficiencies and reduction of environmental waste
State Implementation Plan (SIP) Lean Toolkit for Collaboration Between EPA and Air Agencies (copy will be emailed around)
  Focus on SIPS, lays out recommendations and process with example templates
  Two main goals – early engagement and ensuring EPA has opportunity to review full SIP/SIP amendment prior to official public comment period.
  In SIP 101 course, templates were built from the EPA SIP LEAN Toolkit
  https://www.epa.gov/air-quality-implementation-plans/state-implementation-plan-sip-lean-toolkit-collaboration-between
SIP Preparation

## Slide 174: SIP LEAN – Early engagement
Key to any SIP work is identifying schedule, roles and responsibilities, and issues and concerns.
Filling out a:
  SIP Development Plan (timeline, responsibilities, questions and issues document) – aligns with LEAN approach
  Technical Analysis Protocol – TAP - (how modelling will be conducted (if needed), what models will be used, etc) – not identified specially in LEAN, but will help with technical issues
  Inventory Preparedness Plan (IPP) – (what data will be used in the SIP and how it will be collected) – could be important to determining SIP development timelines as some data may take longer to collect – not identified specially in LEAN, but will help with technical issues
SIP Preparation

## Slide 175: SIP LEAN - communications/process
EPA wants a number of commitments for the Early Engagement Draft (ie. pre–Public Notice Draft of SIP/SIP Amendments):
  Notification of when an agency will have an early draft submission ready
  An agency will submit an early engagement draft of the full SIP/SIP amendment
  EPA wants time to review the full draft and provide comments – they will provide comments within an agreed-upon timeframe in a manner an agency prefers, but typically in writing.
  Agency addresses EPA’s comments through edits within the early engagement draft
Agency is ready to release for public comment (EPA will likely also comment formally during this period as well)
SIP Preparation

## Slide 176: Drafting and Finalizing a SIP State/Local Processes
Develop/Track/Fine Tune Timelines
  Expand initial timeline development (demonstration - example tool)
  Data requests and data gathering
  Prep development work (SIP Dev Plan, IPP, TAP)
Developing policy recommendations based on technical info and local situation
  To assist policy - knowing EPA’s stance is very helpful (see Preparations for Starting A SIP)
Engaging local jurisdictions, stakeholders, FLMs (if required/appropriate), public and incorporating feedback [don't wait until public comment period for feedback and input]
Local/State/Tribal processes for adopting rules, plans
SIP Preparation

## Slide 177: SIP Submittal
SIP Submittal

## Slide 178: What happens after you have the SIP complete at the state/local/Tribal level?
SIP Submittal

## Slide 179: EPA Electronic SIP Submission System (eSIP)/State Planning Electronic Collaboration System (SPeCS)
Allows State to upload draft and submissions, supplemental information and withdraw SIPs.
  State and EPA staff can track the SIP submittal process.
A state can alternatively submit paper version
  Must be accompanied by an electronic duplicate.
https://www.epa.gov/air-quality-implementation-plans/submit-sips-online
SIP Submittal

## Slide 180: 40 CFR 51 Appendix v
Criteria for Determining the Completeness of Plan Submission
  “The EPA shall return to the submitting official any plan or revision thereof which fails to meet the criteria set forth in Appendix v, and request corrective action, identifying the components absent or insufficient to perform a review of the submitted plan.”
SIP Submittal

## Slide 181: 40 CFR 51 Appendix v, cont.
Allows for parallel processing of a SIP
  SIP submission before a state officially adopts it.
  State must specifically request.
  State must include the related draft/proposed regulation.
Details submission requirements
  No confidential business information should be included, and identification of copyrighted materials is necessary.
SIP Submittal

## Slide 182: 40 CFR 51 Appendix v, cont.
SIP must include administrative materials:
  The State’s formal request for EPA to approve the SIP.
  Proof of adoption of the SIP and regulations or other form of control measures.
  Proof of public hearing(s) and response to comments.
SIP must include technical support documents:
  Modeling platform, including documentation of software and data used in modeling.
  Evidence that RACT/RACM are met.
  Evidence that emissions limits will be met.
SIP Submittal

## Slide 183: EPA staff involved in SIP reviews
EPA Regional Administrators (RA) are delegated the authority to receive, return, approve, or disapprove SIPs.
  Review, evaluation, rulemaking are done at the regional level.
  Caveats
    EPA Offices of General Counsel and Regional Council must review Federal Register Notice responses to comments received during NPR public comment period.
    SIP Consistency Process may be required if the action is breaking new ground or departs from previous EPA decisions; a pre-decisional, internal EPA deliberative process.
SIP Submittal

## Slide 184: Federal Register – the daily journal of the U.S. Government
https://www.federalregister.gov/
  No subscription fee – includes all federal agencies’ regulatory actions.
  Can search 1994 to present.
  Final rules are categorized in the Code of Federal Rules (CFR).
Most states have something similar for state regulatory actions.
SIP Submittal

## Slide 185: Federal Register
SIP Submittal

## Slide 186: Public Comments
All official correspondence received by EPA in accordance with a notice of proposed rulemaking (NPR) in the FR become part of the EPA rulemaking docket.
Comments received before the submissions of a SIP revision are not considered in the EPA rulemaking.
EPA rulemaking is only based on the formal SIP submission and comments received during the comment period.
Exceptions for late comments are at EPA’s discretion.
  The NPR can state that late comments will not be accepted.
SIP Submittal

## Slide 187: Final Rulemaking Notice
EPA Regional Office prepares the final rulemaking notice (FRN).
Considers all relevant comments received after the NPR.
  Preamble in the FRN includes a response-to-comment section.
The plan is promulgated 30-days after the FRN.
  Can be exceptions for good cause offering a shorter effective date.
SIP Submittal

## Slide 188: EPA Action Options
Disapproval
  Sanctions clock starts for the state to correct the deficient SIP.
Limited Approval
  SIP revision satisfies some requirements but is not fully approvable and may result in start of FIP and/or sanction clocks.
Conditional Approval
  SIP may be approved if the state commits to adopt control measures within 1 year. Avoids sanctions, but if state doesn’t follow through, disapproval is likely and sanctions clock starts.
Full Approval
  Submitted SIP meets all requirements and EPA approves with no clocks for future action.
Approved SIP contents become federal law and can only be changed through additional SIP revision(s).
SIP Submittal

## Slide 189: Code of Federal Regulations Title 40 (Part 52) Approval and Promulgation of SIPs
Record of the EPA Administrator’s approval, disapproval, and promulgation of State SIPs.
Every State/Tribe/Territory has its own subpart under Part 52.
Promulgation - the act of formally proclaiming or declaring a new law after its enactment.
For U.S. environmental regulations formal promulgation occurs after EPA considers all public comments received on the proposal and follows publication of the final rule in the Federal Register (Part 52).
SIP Submittal

## Slide 190: Federal Implementation Plan (FIP)
24 months after EPA disapproves or makes a finding of failure to submit a required plan, it has nondiscretionary duty to promulgate a FIP.
The FIP should correct the deficiency in the SIP; no more, no less.
  Partial FIP is a possibility.
Sanctions clock is turned off only after EPA approves a SIP revision that corrects the deficiency.
SIP Submittal

## Slide 191: What else can happen if a State misses a SIP deadline?
Sanctions kick in:
  EPA Administrator may apply discretionary sanctions (CAA 110(m)).
  Mandatory sanctions (CAA 179) may also apply -
    Increased emissions offsets for new or modified sources
    Transportation program restrictions
Sanctions triggered by:
  Finding of failure to submit a complete SIP
  Finding of failure to implement any element of an approved SIP
  Disapproval of a SIP
  Failure to submit a SIP revision for which EPA has issued a SIP call or disapproval notice
SIP Submittal

## Slide 192: What happens after the 20-year maintenance plan?
SIP Submittal

## Slide 193: Background – Redesignation To Attainment
Monitors Show Attainment
Agency Submits Redesignation Request and Maintenance Plan – First 10 years
Agency Submits SIP Update – Second 10 Years
Only after EPA fully approves Maintenance SIP does the first 10-year clock start
Only after the EPA fully approves the SIP Update does the second 10-year clock start
SIP Submittal

## Slide 194: Procedures for processing requests to Redesignate Areas to Attainment
September 8, 1992 Memorandum from John Calcagni, entitled Procedures for processing requests for Redesignate Areas to Attainment
Memo Lists 5 requirements:
  EPA has determined that the NAAQS standards have been attained
  The applicable implementation plan has been fully approved by EPA under section 110(k)
  EPA has determined that the improvement in air quality is due to permanent and enforceable reductions in emissions
  The state has met all applicable requirements for the area under section 110 and Part D
  EPA has fully approved a maintenance plan, including a contingency plan for the area under section 175A
SIP Submittal

## Slide 195: Successful conclusion of 20 years in maintenance
Acknowledgement of completion from EPA (confirm with local EPA on format this will take)
Acknowledgement that Conformity is no longer required (confirm with local EPA on format)
Area may or may not be eligible for Federal Highway Administration (FHWA) Congestion Mitigation and Air Quality (CMAQ) funding (confirm specific project(s) w FHWA)
Approved Contingency measure plan – still in effect, so all control measures that were converted to contingency measures must still be available to be ‘turned on’ if there are violations of the NAAQS
  Regulations and statutes must be maintained
SIP Submittal

## Slide 196: Compliance and Enforcement
Compliance & Enforcement

## Slide 197: Compliance and Enforcement of SIPs
Reference(s):
  Training:
    https://airknowledge.gov/index.html
  Technical Work:
    https://www.epa.gov/enforcement/air-enforcement
Compliance & Enforcement

## Slide 198: State’s Compliance Role After a SIP is Approved by EPA
Continuation of air quality monitoring
  There may be monitoring requirements for sources too – such as continuous emissions monitoring and stack testing.
Enforcement of state rules, permits, other control strategies
  May involve site visits and source submittal of periodic reports.
State submits its own periodic reports to EPA, as required
Compliance & Enforcement

## Slide 199: EPA’s Compliance Roles Compliance Monitoring Strategy (CMS)
https://www.epa.gov/compliance/clean-air-act-caa-compliance-monitoring
Provides a national strategy to supplement state enforcement activities for stationary sources.
Provides States with flexibility to address local air pollution and compliance concerns.
Provides a framework for developing compliance monitoring programs that focus on achieving results.
Compliance & Enforcement

## Slide 200: Enforcement Civil Actions
Civil liability arises simply through the existence of a violation; no requirement for prior knowledge or intent.
Civil Administrative Actions: notice of violation or an order (with or without penalties) directing an entity to take action to come into compliance.
Civil Judicial Actions: court filing against entities that have failed to comply with statutory/regulatory requirements or comply with an administrative order.
Compliance & Enforcement

## Slide 201: Enforcement Civil Actions, cont.
Possible Outcomes:
  Settlements may include consent agreements/final orders, administrative orders on consent, or consent decrees.
  Penalties are designed to recover the economic benefit of noncompliance and to compensate for the seriousness of the violation.
  Injunctive Relief forces a regulated entity to perform or refrain from performing some designated action.
  Supplemental Environmental Projects are environmental improvement projects that violators voluntarily agree to perform.
Compliance & Enforcement

## Slide 202: Enforcement Criminal Actions
Criminal liability is triggered through a demonstration of intent to violate NAAQS.
Reserved for the most egregious violations that are willful or knowingly committed.
Possible Outcomes:
  Criminal Penalties are fines imposed by a judge at sentencing; may include restitution to those affected by the violation
  Incarceration
Compliance & Enforcement

## Slide 203: SIP Challenges Citizen Suits
The Clean Air Act (CAA)includes provisions that allow citizens to sue EPA when EPA fails to perform an act or duty required by the statute.
  The CAA was the first environmental law in the U.S. to allow citizen suits.
Plaintiffs must provide the EPA with a Notice of Intent (NOI) to sue in advance of a lawsuit.
Compliance & Enforcement

## Slide 204: SIP Challenges Citizen Suits, cont.
Under U.S. Code Title 42 §7604, citizens may sue:
  Any person, including the U.S. government, or other governmental agency for violating emission standards.
  The EPA Administrator for failing to perform any nondiscretionary act or duty under the CAA.
  Entities proposing to construct new or modified facilities without the proper permits.
Compliance & Enforcement

## Slide 205: SIP Challenges Citizen Suits, cont.
Requirements
  Citizens must be adversely impacted by violation.
  Violators, State, and EPA must have a 60-day notice of the alleged violation.
Violators may use the 60-day period to correct and give EPA or State an opportunity to enforce compliance.
Compliance & Enforcement

## Slide 206: SIP Challenges Citizen Suits, cont.
CAA 304(a)(1) may be used to enforce standards and limits in the current SIP, even if there is a pending SIP revision submitted to EPA.
CAA 304(a)(2) confers citizen suit authority to compel EPA to make findings and promulgate a FIP for SIP revisions that have not been submitted.
Compliance & Enforcement

## Slide 207: SIP Challenges Lawsuits
If EPA acts on a SIP revision, the EPA rulemaking is subject to challenge under the Administrative Procedure Act (APA) as a final action.
  Venue is a Federal Court of Appeals.
If EPA fails to act on a SIP revision within 12 months of completeness determination or if a rule is challenged as unlawful then EPA is subject to lawsuit.
  Venue is a Federal District Court.
Compliance & Enforcement

## Slide 208: SIP Challenges Lawsuits, cont.
Court Options
  Vacate and Remand: Rule or plan is no longer in effect.
  Remand without Vacating: Rule or plan remains in effect, but EPA will need either to re-propose or recommence final action.
  Remand with Partial Vacate: If possible, remove the defective part of the rule or plan.
  Uphold: Permit the rule or plan to remain in effect as promulgated.
Compliance & Enforcement

## Slide 209: Final Review
Final Review

## Slide 210: Status of NAAQS Reviews (from EPA August 2024)
 | Lead | Ozone | PM1 | Secondary (Ecological) NO2, SO2, PM2 | Primary NO2 | Primary SO2 | CO
Last Review Completed (final rule signed) | Sep 2016 | Dec 2020 | Dec 2020/Feb 2024 | Mar 2012 | Apr 2018 | Feb 2019 | Aug 2011
Recent or Upcoming Major Milestone(s) | Feb 7, 2024 Final ISA3 released Early 2025 Draft PA3 | May 2024 Science Policy Workshop Fall 2024 IRP3 Volumes 1 and 2 | March 6, 2024 Final Rule, effective May 6, 2024 | April 3, 2024 Proposed Rulemaking Dec. 10, 2024 Final Rulemaking (consent decree) | Mar. 18, 2024 IRP3 Volumes 1 and 2 Fall 2025 Draft ISA3 and IRP3 Volume 3 | TBD4 | TBD4
1 Combined primary and secondary (non-ecological effects) review of PM
2 Combined secondary (ecological effects only) review of NO2, SO2, and PM
3 PA – Policy Assessment; REA – Risk and Exposure Assessment; IRP – Integrated Review Plan; ISA – Integrated Science Assessment
4 TBD = To be determined
Additional information regarding current and previous NAAQS reviews is available at: http://www.epa.gov/ttn/naaqs/

## Slide 211: State Planning Milestones (from EPA - August 2024)
Pollutant (Standard) | Final NAAQS/EG Signature | Nonattainment Designations Effective | Infrastructure SIP Due | Attainment/EG Plans Due | Attainment Date/EG Compliance Date
Ozone (2015) | Oct 2015 | Aug 3, 2018 * | Oct 2018 | Aug 2021-2022, Jan 2023, Jan 2026** | Aug 2021, 2024, 2027, 2033, 2038 *
Ozone (2008) | Mar 2008 | July 2012 | Mar 2011 | July 2015/2016 Jan 2017, Aug 2020, May 2024*** | July 2015, 2018, 2021, 2027, 2032
SO2 (proposed annual secondary) | December 2024 (CD deadline) | TBD | December 2027 if NAAQS is revised | TBD | TBD
SO2 (2010 1-hr primary) | June 2010 | 1Oct 2013, 2Sept 2016, 3Apr 2018, 4Apr 2021 | June 2013 | 1Apr 2015, 2Mar 2018, 3Oct 2019, 4Oct 2022 | 1Oct 2018, 2Sept 2021, 3Apr 2023, 4Apr 2026
PM2.5 (2024 annual) | February 2024 | Spring 2026 | February 2027 | Fall 2027 | Spring 2032 (Moderate)
PM2.5 (2012 annual) | Dec 2012 | Apr 2015 | Dec 2015 | Oct 2016 (Moderate) | Dec 2021 (Moderate) Dec 2025 (Serious)
PM2.5 (2006 24-hr) | Oct 2006 | Dec 2009 | Oct 2009 | July 2011 | Dec 2015 (Moderate) Dec 2019 (Serious)
OOOOc Oil & Gas Emiss. Guideline | March 2024 | n/a | n/a | March 2026 | March 2029
UUUUa EGU Emiss. Guideline | April 2024 | n/a | n/a | April 2026 | April 2029
* September 24, 2018 for San Antonio, TX. Attainment dates are also September 24 of listed years.
** January 2023 for areas reclassified from Marginal to Moderate. Tentatively January 2026 for areas reclassified from Moderate to Serious.
***January 2017 for areas reclassified from Marginal to Moderate. August 2020 for areas reclassified from Moderate to Serious. May 2024 for areas reclassified from Serious to Severe.

## Slide 214: Additional Resources
EPA Green Book (Nonattainment Area classifications and status)
  https://www.epa.gov/green-book
Air Topics
  https://www.epa.gov/environmental-topics/air-topics
SIP Lean Toolkit
  https://www.epa.gov/air-quality-implementation-plans/state-implementation-plan-sip-lean-toolkit-collaboration-between
EPA SIP Guidance (websites with links to guidance, policies, process, etc)
  https://www.epa.gov/air-quality-implementation-plans
  https://www.epa.gov/air-quality-implementation-plans/develop-air-quality-sip#guidance
  https://www.epa.gov/title-v-operating-permits/epa-process-manual-caa-requests-under-111b-111d-112-and-129
Final Review

## Slide 215: Additional Resources, cont.
Compliance and Enforcement
  https://www.epa.gov/enforcement/clean-air-act-caa-and-federal-facilities
  https://www.epa.gov/enforcement/enforcement-policy-guidance-publications
Permit Modeling Guidance
  https://www.epa.gov/scram/clean-air-act-permit-modeling-guidance
New Source Review
  https://www.epa.gov/nsr
Transportation Conformity
  https://www.epa.gov/state-and-local-transportation
Redesignation and Clean Data Policy
  https://www.epa.gov/ground-level-ozone-pollution/redesignation-and-clean-data-policy-cdp
Final Review

## Slide 216: Regional/National Organization Contacts
AAPCA - Morgan Dickie: mdickie@csg.org; website: https://cleanairact.org/
NACAA - Loralei HoJay: lhojay@4cleanair.org; website: https://www.4cleanair.org/
CENSARA - Michael Vince: mvince@censara.org (get on email lists for quarterly meetings for planning)

## Slide 217: Instructor Email Contacts
Cindy Heil: cindy.heil@outlook.com
Alice Edwards: ale2akclub@gmail.com